## Slide 1: Superconductivity Technology for Discovery Science Technology for a Better World
Luca.Bottura@cern.ch
CERN, 4 April 2025

## Slide 2: Outline
What is a superconductor ?
What can you do with it ?
  At CERN (High Energy Physics) …
  … and elsewhere
Final exam
Make you advocates of superconducting technology, for a future that is greener, healthier, more prosperous, and sustainable
Objective

## Slide 3: Outline
What is a superconductor ?
What can you do with it ?
  At CERN (High Energy Physics) …
  … and elsewhere
Final exam

## Slide 4: The discovery – 1911
… thus the mercury at 4.2 K has entered a new state, which, owing to its particular electrical properties, can be called the state of superconductivity…
H. Kamerlingh-Onnes (1911)

## Slide 5: Superconductors vs. copper
15x2 mm
10 kA cables
Nb-Ti
superconductor
100x100 mm
Copper
resistive
13,000 A
13,000 A

## Slide 6: The big surprise – 1986
One Thousand and One Superconductors
B. Matthias (1918-1980)
Bednorz and Mueller
IBM Zuerich, 1986
Theoretical limit around 30 K

## Slide 7: The prize ! 1987

## Slide 8
Nb, Nb-Ti
High Temperature Superconductors (LTS)
Low Temperature Superconductors (LTS)
Room Temperature Superconductors (RTS)
(on Jupiter)
15 C
269 GPa

## Slide 9: Basic takeaway #1
A superconductor is a material that has zero resistance and can carry large currents with no loss
A material becomes superconducting only if it is cooled down below a critical temperature, typically between liquid helium (-269 ºC) and liquid nitrogen (-196 ºC)
Bonus knowledge: superconductivity is a quantum macroscopic phenomenon

## Slide 10: Outline
What is a superconductor ?
What can you do with it ?
  At CERN (High Energy Physics) …
  … and elsewhere
Final exam

## Slide 11: Particle accelerator basic
Large magnetic field gives higher energy with a smaller (cheaper !) accelerator
Image courtesy of Alamy
Particle beam
Magnetic field
E
particles
RF
acceleration
Particle accelerator = Merry-go-round

## Slide 12: LHC – Superconducting magnets
LHC dipole cross section
B
B
Extreme magnetic fields
B = 8.3 T (200,000 times earth magnetic field)

## Slide 13: LHC – Superconducting RF
LHC RF cavity cross section
Extreme electric fields
V = 2 MV (10,000 times household appliance)

## Slide 14: Basic takeaway #2
Superconducting magnets, radio-frequency (and power transmission cables) made it possible to realize the largest instrument built by humankind
LHC would not exist without superconductors
The superconductors used in the LHC (and future accelerators) would not be at the same level of technology readiness without the stewardship of High Energy Physics

## Slide 15: Outline
What is a superconductor ?
What can you do with it ?
  At CERN (High Energy Physics) …
  … and elsewhere
Final exam

## Slide 16: Magnetic Resonance Imaging
Hi-Ho Nb-Ti
Tevatron
SSC R&D
LHC
Prime choice for non-invasive imaging

## Slide 17: Next step in MRI
Radboud University (responsible institution), Amsterdam Medical Centre (AMC), Leiden University Medical Centre (LUMC), Maastricht University, Radboud University Medical Centre, Spinoza Centre for Neuroimaging – KNAW and University Medical Centre Utrecht (UMCU)
Hippocampus taken at different MRI field
HTS tape (REBCO) used in R&D magnets at CERN and associated laboratories

## Slide 18: MRI market size and projection

## Slide 19: Nuclear Magnetic Resonance
Bruker ASCEND 1.2 GHz
28.2 T in 54 mm (LTS+HTS)
NMR structure model of the SARS-CoV-2 N-NTD:RNA complex
Nb3Sn wires used in HL-LHC magnets
Unique insight in materials and molecules

## Slide 20: NMR market size and projection
Source: Vantage Market Research

## Slide 21: Thermonuclear fusion
CFS SPARC reactor, Devens (MA, USA)
ITER reactor, Cadarache (F)
Promise of unlimited, clean energy

## Slide 22: Powerful magnets for fusion
MIT/CFS SPARC TF Coil prototype
20 T at 20 K (HTS)
MIT/CFS SPARC CS Coil prototype
5.7 T, 5 T/s at 20 K (HTS)
Fusion-like internally cooled HTS cable developed at CERN for the target and capture solenoid of the Muon Collider

## Slide 23: Fusion market size and projection

## Slide 24: Basic takeaway #3
Superconductivity is the enabling technology for applications that have revolutionized our life
  Healthcare (MRI)
  Biology and pharmaceutical research (NMR)
Superconductivity can lead to paradigm shift in
  Energy production (fusion reactors, generators)
  Electric power distribution (transmission cables)
  Transportation (propulsion and levitation)
  Electronics and quantum (QUBITs)

## Slide 25: Outline
What is a superconductor ?
What can you do with it ?
  At CERN (High Energy Physics) …
  … and elsewhere
Final exam

## Slide 26: Quiz – 1/3
What is a superconductor ?
  An orchestra or choir conductor with extraordinary abilities
  A material that, when cooled down to cryogenic temperatures, can carry very large currents with no resistance
  A material that keeps the Pandora mountains afloat

## Slide 27: Quiz – 2/3
Why are superconductors important to discovery science ?
  Because physicists tend to get passionate about strange and useless materials
  Because they are cheap
  Because superconductivity is the enabling technology for instruments that have led to many of the fundamental discoveries of the last century

## Slide 28: Quiz – 3/3
Why is discovery science important to society ?
  Among the many reasons (science, collaboration, education), because the superconducting technology needed for discovery science is conducive to revolutionary changes in the way we live

## Slide 29: Cognizable in superconductors
Thank you for taking part to this class !
Now make good use of what you have learned…
… and we will be very happy to help you !