Transverse stability simulations with cavity HOMs in RCS
D. Amorim, E. Métral
Thanks to F. Batsch, J. S. Berg, F. Boattini, L. Bottura, X. Buffat, C. Carli,
A. Chancé, H. Damerau, M. Gast, A. Grudiev, I. Karpov, E. Lamb, E. Kvikne,
T. Pieloni, D. Schulte, L. Soubirou, K. Skoufaris, L. Thiele
This work was performed under the auspices and with support from the Swiss Accelerator Research and Technology (CHART) program (www.chart.ch).
Funded by the European Union (EU). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

---
TESLA cavities wakefield model
Single cavity wakefield shown here. We will use a single turn wake.
Compare three cavities:
Low Loss TESLA type cavity
Classic TESLA cavity
L. Thiele 2025 TESLA cavity
HOM list from the following references:
J. Sekutowicz et al. paper
S.-A. Udongwo presentation
L. Thiele cavity HOMs parameter file
List of HOMs available here: https://gitlab.cern.ch/muon-collider-bd/muc-impedance/-/tree/master/rcs1/rcs_tesla_cavity_hom_list

---
Beam and machine parameters for the RCS
Machine parameters	Unit	RCS 1	RCS 2	RCS 3	RCS 4
Circumference	m	5990	5990	10700	35000
NC magnet length	m	3655	2539	4366	20376
Bunch intensity	1012	2.7	2.7	2.7	2.7
Beam momentum	GeV/c	63	313.8	750	1500
Energy increase per turn	GeV	14.7	7.9	11.3	63.6
Rev. frequency	kHz	50	50	28	8.6
RF frequency	MHz	1300	1300	1300	1300
Harmonic number		25957	25957	46295	151433
RF voltage	GV	20.9	11.22	16.1	90.0
Number of RF stations		32	26	26	26
αp	10-4	6.0	11.0	7.0	2.0
Qx / Qy		44.36/ 31.56	33.29/ 23.07	41.78/ 35.69	65.62/ 58.60
Chromaticity Q’x/Q’y		scan	scan	scan	scan
Detuning from octupoles x/y	m-1	0 / 0	0 / 0	0 / 0	0 / 0
Beam parameters	Unit	Value
Bunch length 1σ	mm	5.7
Bunch intensity	Particles per bunch	2.7e12
εx / εy	μm rad	25
# of macropaticles		500k
# of turns wakefield		1
# of slices wakefield		2000
Was 24/24/10/10 10-4 previously
Was around 19/19/31/110 for both planes previously
Parameters from F. Batsch RCS tables

---
Example of start-to-end simulation, longitudinal properties
Chromaticity Q’ = 20, no initial transverse offset (jitter), 50-turn damper
The single cavity wakefield is multiplied by 700, 380, 540 and 3000 the number of cavities per RCS
Longitudinal emittance blow-up might affect the transverse beam dynamic

---
Example of start-to-end simulation,
transverse properties
Chromaticity Q’ = 20, no initial transverse offset (jitter), 50-turn damper
The single cavity wakefield is multiplied by 700, 380, 540 and 3000 the number of cavities per RCS
Longitudinal emittance blow-up might affect the transverse beam dynamic

---
Q’=0, scaling factor=1
Low Loss type cavity
Classic TESLA cavity
2025 TESLA cavity
Simulations with nominal number of cavities and the HOMs from each cavity design report
All cavity models preserve the transverse emittance up to RCS 4 extraction, for any damper and jitter parameter

---
Q’ = +20, scaling factor = 1
Low Loss type cavity
Classic TESLA cavity
2025 TESLA cavity
Some small emittance blow-up appear

---
Q’ = 0, scaling factor = 2
Low Loss type cavity
Classic TESLA cavity
2025 TESLA cavity
Double the number of RF cavities, doubling the wakefield strength
We seem to reach the threshold of stability
Blowup appears for all simulations with the classic TESLA cavity
Simulations with the 2025 TESLA cavity and with larger jitter become unstable

---
Q’ = +20, scaling factor = 2
Low Loss type cavity
Classic TESLA cavity
2025 TESLA cavity
Putting positive chromaticity helps to gain back some stability margin for the classic TESLA cavity

---
Q’ = 0, scaling factor = 5
Low Loss type cavity
Classic TESLA cavity
2025 TESLA cavity
We 5 times the wakefield strength, all cases are unstable at Q’=0

---
Q’ = +20, scaling factor = 5
Low Loss type cavity
Classic TESLA cavity
2025 TESLA cavity
Adding chromaticity doesn’t change the picture

---
Conclusion
Start-to-end simulation from RCS 1 to RCS 4 with the HOM for tables Low Loss, classic TESLA and L. Thiele 2025 TESLA cavity
	Nominal model	Factor 2 on the wakefield strength
Low Loss	Stable, with Q’=0 or Q’=20	Stable with small jitter / Probably close to instability threshold
Classic TESLA	Stable, with Q’=0 or Q’=20	Unstable with Q’=0 / Stable with Q’=+20
2025 TESLA by L. Thiele	Stable, with Q’=0 or Q’=20	Stable with small jitter / Probably close to instability threshold
Large longitudinal blow-up is present, affecting the bunch length. The effect on transverse stability needs to checked.

---
Thank you !
Funded by the European Union (EU).Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

---
Cavity HOM tables
L. Thiele TESLA (first 20 modes)
Low Loss
Classic TESLA

---
Large offset/jitter and chromaticity