## Slide 1: HQ and TQ magnets Quench Protection Study HFM Protection Studies WP4.5-T5-D1
24.04.2025
M. Wozniak & E. Ravaioli

## Slide 2: Outline
Scope
Magnets & Conductors
Circuit & Quench Detection
Details for protection with:
  QH and/or CLIQ
  E-CLIQ
  ESC
Summary of cases studied
Results

## Slide 3: Scope
Study HQ (High gradient, high field Quad) and TQ (Technology Quad) magnets (both develop within the framework of the US LARP)
Consider individually powered, long (7.15 m), single-aperture magnet
In terms of quench protection study:
    Outer layer QH (quench heaters) and CLIQ quench protection
    QH only or CLIQ only or both together
    Include three ways (glued, miniswap, impregnated) of placing QH
    Novel E-CLIQ quench protection (at conceptual level)
    Novel ESC quench protection with 4 capacitive units
    Study Time to Quench by quenching all turns at specific time
Quantify regarding quench protection:
    maximum adiabatic hot spot temperature
Keep is simple, do not consider failure cases, low current quenches etc.

## Slide 4: HQ magnet
Acknowledgement of design: GianLuca Sabbi
Current: 15366 A*
Gradient: 175 T/m**
Copper current density: 1621 A/mm²
Overall current density: 612 A/mm²
* Current adjusted to obtain the gradient
** Gradient assumed for this study, not clear what the original nominal value was

## Slide 5: TQ magnet
Acknowledgement of design: GianLuca Sabbi
Current: 11019 A*
Gradient: 200 T/m
Copper current density: 1738 A/mm²
Overall current density: 708 A/mm²
* Current adjusted to obtain the gradient

## Slide 6: Conductors
Cable
Number of strands: 35
Bare:
  width: 15.15 mm
  height low: 1.338 mm
  height high: 1.538 mm
Insulation thickness : 100 μm
Strand
Diameter: 0.8 mm
Cu/non-Cu ratio: 1.17
Jc(B, T) following Summer’s fit: Tc0: 16.33 K, Bc20: 26.45 T, Jc0: 4.663 1010 A/m²
Using the MQXF cable average measured Jc of 937 A/mm² @ 4.2 K, 16 T
Common
RRP Nb3Sn
RRR: 150
Filaments twist pitch: 18.5 mm
Cable transposition length: 109 mm
Glass fibre insulation
HQ (IR2TQ_V1)
Ic (1.9 K, 12.16 T) = 28991 A for Iop = 15366 A
Ic (1.9 K, 10.26 T) = 36166 A for Iop = 11019 A
Cable
Number of strands: 27
Bare:
  width: 10.05 mm
  height low: 1.172 mm
  height high: 1.348 mm
Insulation thickness : 125 μm
Strand
Diameter: 0.7 mm
Cu/non-Cu ratio: 0.89
TQ (IR2TQ_V1)

## Slide 7: Circuit and quench detection
This is the most pessimistic case with crowbar and diode parameters.
Time when quench protection is activated called trigger time (and power supply toff)
This is a parameter that is changed in the simulations from 10 ms to 40 ms
0V
0.0 Ω
PC
toff

## Slide 8: Quench heaters and insulation design
Polyimide film: 50 μm *
SS (304L) foil: 25 μm
Cu layer: 10 μm
Length of SS patch: 50 mm
Ground insulation: 0.5 mm Polyimide
Heater current peak: 150 A
Heater power supply: ±450 V, 7 mF
Additional insulation – variable
Epoxy adhesive: 15 μm
Identical to MBH QH
Details on the next slide
Identical to MBH QH powering
GND insulation
Cu layer
SS layer
Adhesive
Kapton
Additional insul.
Cable insulation
Cable bare
Cross-section:
(not to scale)
Not included, as in all the models I know of
* Some of the original TQ and HQ magnets used 25 μm Kapton insulation QH. Here, a more common today 50 μm is used instead.

## Slide 9: Additional insulation – QH application method
Approach name | Additional insulation |  | Description
 | Thickness (μm) | Material | 
Impregnated | 0 | N/A | QH placed directly on the coil was impregnated with the coil
Miniswap | 50 | G10 | 50 μm E-Glass cloth layer placed between QH and the coil QH impregnated with the coil []
Glued | 100 | G10 | QH glued to the coil after it had been impregnated. The thickness corresponds to additional coil insulation and glue layer (G10 used for both).
GND insulation
Cu layer
SS layer
Adhesive
Kapton
Additional insulation
Cable insulation
Cable bare
Cross-section:
(not to scale)

## Slide 10: Quench heaters placement - HQ
Two traces form a U-shaped heater pad. 8 pads per aperture.
OH (outer high field trace – 13 turns covered)
Not covering this turn with the heating element
Not covering this turn with the heating element
OL (outer low field trace – 11 turns covered)
OH
OL

## Slide 11: Quench heaters placement - TQ
Two traces connected at non-powered end. 8 traces per aperture.
Not covering this turn with the heating element
Not covering this turn with the heating element
OL (outer low field trace – 14 turns covered)
OL

## Slide 12: Quench heaters adjustment (not optimization)
The quench heater design differs from the 11 T (MBH) (LF and HF) heaters in the details described below.
The width of the quench heater has been adjusted to match the arch length of the coil blocks.
The length of the Cu patch (see picture) has been adjusted to result in a total heater trace resistance of 3 Ohm per trace. The two traces are in series, giving 6 Ohm, and this is powered with 900 V ( ±450 V to the ground) with a peak current of 150 A.
Room temperature resistance (heater power supply and connection to heaters) is 9 mOhm.
Longitudinal view:
(not to scale)
Length Cu
Width
Magnet name | Trace name | Length (mm) |  | # turns covered | Width (mm) | Wedge width covered (mm)
 |  | Copper | Stainless steel |  |  | 
HQ | OL | 86.3 | 50 | 11 | 19.1 | 0
 | OH | 65.3 |  | 13 | 22.6 | 0
TQ | OL | 66.4 | 50 | 14 | 22.4 | 0
Length SS

## Slide 13: E-CLIQ – very preliminary estimate – QH like
Longitudinal view:
(not to scale)
Magnet name | E-CLIQ name | Length (mm) |  | # turns covered | Width (mm) | Wedge width covered (mm)
 |  | Gap | Coil |  |  | 
HQ | OL | 86.3 | 50 | 11 | 19.1 | 0
 | OH | 65.3 |  | 13 | 22.6 | 0
TQ | OL | 66.4 | 50 | 14 | 22.4 | 0
Length Gap
Width
Length Coil
E-CLIQ pictures and results courtesy of Tim Mulder et al.
More details: https://indico.cern.ch/event/1517509/
Today E-CLIQ is at about TRL3, so predicting quench performance of a full-size magnet has large uncertainty
Without going into details, two quench delay times are studied for E-CLIQ: 2 ms and 10 ms
This time is not dependent on a local magnetic field (enthalpy to quench), so it is wrong, but nonetheless useful as a very preliminary estimate
Normal zone initiated with a ms!
Measured E-CLIQ
Results on SMC
“The same” numbers as for QH

## Slide 14: CLIQ unit and connections
Parameter | Value | Unit
Capacitance | 40 | mF
Initial voltage | 1000 | V
Internal resistance | 50 | mΩ
VF
0V
Rcrowbar
0 Ω
PC
CLIQ
Unit
+
E.O.#1
P2
P4
P1
P3
P1
P2
P3
P4
HQ magnet
P1
P2
P3
P4
TQ magnet
1 CLIQ unit connected in pole configuration

## Slide 15: ESC coils design
HQ magnet
TQ magnet
40 x 1 mm²
1 kV -> 2 kA
21 x 4 mm²
1 kV -> 6 kA
23 x 1 mm²
1 kV -> 3 kA
12 x 4 mm²
0.6 kV -> 6 kA
These are the only configuration tired.
No optimization whatsoever.
Sime interesting features can be already discussed.
Conductor:
Two sizes of bare copper square :
  1 mm² = 1 mm x 1 mm
  4 mm² = 2 mm x 2 mm
For HQ:
Not full arc is filled as high resistance for 1mm² wire for 40 turns resulting in relatively low ESC current
For TQ*:
For 4mm² wire, 12 turns the ESC unit initial voltage is lowered to 0.6 kV to stay below 6 kA (limit of CLIQ unit switch)
1 mm thick insulation
More details on ESC: https://indico.cern.ch/event/1517509/
*Iron yoke slightly adjusted for TQ magnet to make space for ESC coils

## Slide 16: ESC units and connections
Parameter | Value | Unit
Capacitance | 50 | mF
Initial voltage | 1000 (600) | V
Internal resistance | 50 | mΩ
VF
0V
Rcrowbar
0 Ω
PC
E.O.#1
P2
P4
P1
P3
+
ESC Unit
+
ESC Unit
+
ESC Unit
+
ESC Unit
P1
P2
P3
P4
P1
P2
P3
P4
P1
P2
P3
P4
P1
P2
P3
P4

## Slide 17: Protection cases studied
Magnet length: 7.15 m
12 protection cases studied, with :
STEAM tools have been used for simulations:
STEAM: https://cern.ch/steam
STEAM SDK: https://gitlab.cern.ch/steam/steam_sdk
LEDET: http://cern.ch/ledet
LEDET
Repeatability information:
https://gitlab.cern.ch/steam/analyses/tq-hq-quench-protection Tag: 2025.03.0
Initial temperature: 1.9 K
Protection case
Outer QH only (3 appl. met.)
CLIQ only
Outer QH (3 appl. met.) & CLIQ
E-CLIQ (2 delay times)
ESC (2 coil designs)
Time to Quench
  2 magnet design
  1 electrical order
  1 magnet length
  16 trigger times (10, 12, … , 40 ms)
Total: 384 simulations

## Slide 18: HQ –current vs time for trigger time of 2 ms
QH - glued
CLIQ
CLIQ + QH - glued
100 % quenched
E-CLIQ (2ms)
ESC (21x4mm² 1kV)

## Slide 19: TQ –current vs time for trigger time of 2 ms
QH - glued
CLIQ
CLIQ + QH - glued
100 % quenched
E-CLIQ (2ms)
ESC (12x4mm² 0.6kV)

## Slide 20: Results – top level summary as a conclusion
Magnet name | HQ | TQ
Time margin to 300 K (ms) | 28.5 | 20.8