## Slide 1: Status of MP checks for the LHC collimation system + TWOCRYST + BSRTMB
D. Mirarchi on behalf of the LHC Collimation Team, BE-OP-LHC, BE-CEM-MRO, BE-CEM-MTA, SY-BI-PM
259th Machine Protection Panel Meeting

## Slide 2: Overview - Collimation
Position, energy, b* limits of all ring collimators tested and validated
Local mode interlock carried out for one ring collimator per BIC
No devices in the inconsistency list found with Parameter Configuration Application
Both interlock on replacement pipe and on limits tested
Both SIS and BIS testes
PRS reboot carried out for one ring collimator per BIC plus each PXIs replaced during YETS
Links to the elog and collimation web page with detailed information in the checklist
Temperature completed for all ring collimators Both probes not working on TCSG.A6L7.B1 – left and TCLIA.4L8 – right (redundancy from other jaw)

## Slide 3: Overview - TWOCRYST
Links to the elog and collimation web page with detailed information in the checklist
All MP validation tests successfully completed for both SIS and BIS
Position interlock SIS
Position interlock BIS
PRS reboot
Access map and RBAC
High level architecture (LSA, sequencer, controls) and middle layer controls (FESA) for all devices were prepared, tested and deployed.

## Slide 4: Overview - BSRTMB
Links to the elog and collimation web page with detailed information in the checklist
Position interlocks as a function of energy successfully tested and validated
Sequences updated and settings generated, accordingly to 2022 run

## Slide 5: Status waiting for first beams – Threading
Beam left “circulating” step-by-step: collimators used to stop the beam in each IR (except IR4…)
Beam 1
Beam 2
a.k.a. Threading
Beam 1 | Beam 2
TDIS[A¦B].A4L2.B1 | TDIS[A¦B].A4R8.B2
TCP.6L3.B1 | TCP.B6R7.B2
TCTPV.4L5.B1 | TCSP.A4L6.B2
TCSP.A4R6.B1 | TCTPV.4R5.B2
TCP.B6L7.B1 | TCP.6R3.B2
TCTPH.4L8.B1 | TCTPH.4R2.B2
TCTPH.4L1.B1 | TCTPH.4R1.B2
Ring coll. at: LD = 0.5mm, LU = -1mm, RD = -1mm, RU = -2.5mm
TDIS[A|B] at: L = [4.0|-2.5], D = [2.5|-4.0]
BP and sequences tested and ready for first beam

## Slide 6: Commissioning/setup – settings
Collimator | IR | Setting |  | 
 |  | Inj. | FT (first ramp) | FT (if squeezing OR with INDIVs)
TCP (H&V) | 7 | 8 s | 20 s | 8 s
TCSP | 6 | 9 s | 25 s | 9 s
TCP | 3 | 12 s | 30 s | 30 s
TCTP | 1/2/5/8 | ±15 mm | ±15 mm | 10 s/±15 mm/10 s/15 s (@30cm)
TCDQ | 6 | 20 mm | 20 mm | 20 mm
Reduced set of collimators at COARSE settings
Two set of FT settings defined whether or not beams get squeezed: collimators kept fixed after reaching FT

## Slide 7: Conclusions
Ring collimators + new TWOCRYST devices + BSRTMB fully commissioned and validated:
ready for first beam in 2025!