HCAL TPG Status
November 9, 2011
Jeremiah Mans

---
HCAL TPG Goals (2012)
- Overall goal is to demonstrate uTCA electronics capable of running HCAL at either 1.6 Gbps or 4.8 Gbps by the end of 2012
  - Immediate focus on HF, as this is the region where front-end replacement would likely come first
- Use optical splitting on optical signal from the front-end to provide parallel current and upgrade branches
  - Cross-compare for validation
- Bunch-synchronization and link validation for the trigger are crucial components here
Optical
Splitter
HCAL
Upgrade
Crate
HCAL
Crate
Trigger
Upgrade
Crate(s)
Trigger
Crates
Lumi
CDAQ
FRL Crate
for Upgrades
Global DAQ

---
Splitter Progress
- Splitter performance: 5 +/- 1 dB loss
- Check of > 192 fibers at P5 indicates sufficient power budget with only minor adjustments to bias current, etc
- 2012 Splitter Installation
  - 2 HF HTRs (32 fibers/96 channels/8 trigger towers)
  - 40° one end of HB/HE (96 fibers/288 channels/224 trigger towers)
- LS1 Splitter Installation
  - Full HB/HE
Splitter tray under construction in Bat 904

---
miniCTR2 Recent Progress
- Received MMC mezzanine firmware from Wisconsin (T. Gorski) – working very well for the miniCTR2c cards. Currently manufacturing more daughtercards to populate full run of miniCTR2c cards at Minnesota and Kolkata
- Good progress on firmware to support 1.6 Gbps input link (current HCAL FE link)
- Software developing well: IPbus + XDAQ system in place for configuration, XMAS monitoring to be available soon (~3 weeks)

---
miniCTR2 Recent Progress
miniCTR2c running with HCAL FE module at Minnesota, properly aligning data with the orbit signal

---
2012 Plans
- HCAL will have a parasitic test stand at Pt 5 where we are validating the “parallel operation” mode
  - It would be ideal to have in-situ validation of the sychronization concepts for the optical-link-based trigger link
- HCAL will also have equipment at Bat 904 which can be integrated with trigger upgrade work

---
Full-scale uHTR Design
12 Fibers
From Detector
General Use
SFP+
PPOD RX
PPOD RX
LEDs
LEDs
XC6VLX240T
FF1759
(24 GTX PORTS)
XC6VLX130T
FF1156
(20 GTX PORTS)
12
12
12
4
PORT0
PORT1
PORT4
SFP+
LEDs
JTAG/GPIO
PPOD TX
PORT8
DRAM
12 Fibers
From Detector
Up to
12 Fibers
To Trigger

---
Focus on Trigger-Relevant Portion
XC6VLX240T
FF1759
(24 GTX PORTS)
XC6VLX240T
FF1759
(24 GTX PORTS)
PPOD RX
PPOD RX
12
12 Fibers
From Detector
4
PPOD RX
PPOD RX
12
12 Fibers
From Detector
LEDs
PPOD TX
PPOD TX
Up to
12 Fibers
To Trigger
12
- All channels enter a single FPGA – maximal flexibility in channel organization and summing (compared with existing HTR)
- All fibers live :	24 fibers = 72 channels @ 1.6 Gbps, 96-144 channels @ 4.8 Gbps

---
uHTR Production Prototype
Expect hardware
beginning of
August 2012

---
Overall schedule
- uHTRs, DTC/AMC13 will be produced for HF by the end of 2013
  - Pending funding, CMS approval
- Production can be continued for the full set of cards for HB/HE, depending on funding
- All uTCA crates should be installed during LS1 regardless