## Slide 1: RF MD: Long bunches
J.F. Esteban Müller, C. Bhat, P. Baudrenghien, T. Bohl, T. Mastoridis,
G. Papotti, E. Shaposhnikova, H. Timko, U. Wehrle

## Slide 2: Motivation
Longer bunches:
  Help to reduce heating in MKI, beam screens and collimators
  Less e-cloud effect
  For the same voltage  Larger emittance:
    Better stability
    Lower IBS growth rate
    But potentially more particle losses (degraded beam lifetime)
Goal of the MD: measure lifetime vs. bunch length

## Slide 3: Conditions
8 bunches/ring in buckets spaced by 1/9th turn
Nominal beam and machine conditions:
  Longitudinal emittances at injection (~0.5eVs)
  Nominal intensity per bunch with large spread (1.15 ± 0.15x1011p)
  Nominal voltage program
At 3.5 TeV, blow-up modulated along the
ring to achieve spread in bunch length
Voltage reduced at the end of the study
to further increase bunch length

## Slide 4: Modulated longitudinal blow-up
Ramp: blow-up target to 1ns (1.25ns operation)
Flat top: phase noise with amplitude modulated at frev
  Lengths between 1.15-1.50ns B1 and 1.25-1.65ns B2
Firmware designed by J. Molendijk

## Slide 5: Losses after blow-up
For each voltage settings we observe a statistical increase of losses with bunch length

## Slide 6: Conclusions
Longer bunches lose more particles, as expected.
Degradation of lifetime during one hour observation: from ~0.5%/h @ 1.2 ns to ~1.0 %/h @ 1.4 ns
Beam-beam effects could increase loss rate
Next step could be a physics fill with 1.3 ns at end ramp (instead of present 1.2 ns)