## Slide 1: KEK Site Report
Go Iwai, T. Kishimoto, K. Murakami, T. Nakamura, and S. Suzuki
High Energy Accelerator Research Organization (KEK)
Computing Research Center (CRC)

## Slide 2: KEKCC: A Largest Computer System
Linux Cluster + Storage System (GPFS/HSM)
  Accommodate multiple experiments in a single system
In production since September 2024
CPU: 12,096 cores
  AMD EPYC 9654, 2.4 GHz (Base clock, up to 3.7 GHz)
  192 cores/node (2 CPU/node, 96 cores/node)
  63 calculation nodes
  382K HS23 (6K HS23/node @3.5 GHz Measured w/o SMT)
    LINPACK: Rmax: 0.52 / Rpeak: 0.45 (PFlop/s)
Memory: 56 TB
  4 GB/job
Disk: 30 PB
  20 PB: GPFS for experimental groups
  10 PB: GPFS-HPSS-Interface (GHI) as an HSM cache
Tape: 120 PB as maximum capacity
Grid instances are running in KEKCC
2024

## Slide 3: Site Scale Evolution Resource History (Last 4-Gen)
Chart: Storage (PB)
| KEKCC-12 | KEKCC-16 | KEKCC-20 | KEKCC-24
Disk (PB) | 7 | 13 | 25.5 | 30
Tape (PB) | 8 | 26 | 41.5 | 48.1
HEPScore23 | 58880 | 235700 | 273350 | 381786
~382K HEPScore / 12K cores
273K HEPscore / 15K cores
+40% HEPScore
-20% cores
+20%
48 PB in use as of Sep 2025
Disk: 30 PB
x1.2
x1.4
x4.0

## Slide 4: More power with less energy
KEKCC-2024 | Upgrade Factor
Lenovo SR645v3 | 
AMD EPYC 9654 (96cx2/node) | 
192 cores/server x 63 servers | 
RedHat EL9 | 
Mellanox HDR100 | 
IBM Elastic Storage System | 
30 PB (10 PB for HSM) | +20%
IBM TS1160 x70 | 
20TB/vol, 400 MB/s | 
120 PB | +20%
Chart: Power Consumption (x103 kWh)
| Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Fall | Winter | Spring | Summer
KEKCC-2020 | 165661 | 168519 | 153845 | 157437 | 151655 | 147954 | 148266 | 152330 | 155794 | 148670 | 158938 | 142683
KEKCC-2024 | 114142 | 126199 | 127227.921 | 144329.249 | 134064 | 122245 | 139754.881 | 136959.536 | 136241.742 | 127507.616 | 137782 | 125690.332
KEKCC-2020 | 165661 | 334180 | 488025 | 645462 | 797117 | 945071 | 1093337 | 1245667 | 1401461 | 1550131 | 1709069 | 1851752
KEKCC-2024 | 114142 | 240341 | 367568.921 | 511898.17 | 645962.17 | 768207.17 | 907962.051 | 1044921.587 | 1181163.329 | 1308670.945 | 1446452.945 | 1572143.277
KEKCC-2024: 40% more HS23 with 15% less power consumption than KEKCC-2020
KEKCC-2020
KEKCC-2024
-15%

## Slide 5: Runtime in the Entire System
Chart: Runtime (%)
| 45536 | 45566 | 45597 | 45627 | 45658 | 45689 | 45717 | 45748 | 45778 | 45809 | 45839 | 45870
Others | 2.4272 | 3.9377 | 7.8762 | 3.7223 | 1.8846 | 5.1609 | 4.7558 | 6.7555 | 5.2031 | 5.5985 | 5.9062 | 4.3519
J-PARC | 42.5286 | 48.5849 | 44.0488 | 30.7004 | 35.6487 | 22.8952 | 26.9834 | 29.3743 | 41.4845 | 31.1338 | 30.5793 | 22.6303
Belle+Belle2 | 55.0441 | 39.675 | 43.1702 | 52.9277 | 53.488 | 50.4043 | 52.9734 | 51.3857 | 38.9785 | 53.9377 | 54.7987 | 65.2545
Grid | 0 | 7.8023 | 4.9048 | 12.6496 | 8.9787 | 21.5395 | 15.2873 | 12.4845 | 14.3339 | 9.3301 | 8.7158 | 7.7632
Runtime (%) | 77.5914 | 86.6752 | 90.957 | 80.7913 | 71.3862 | 69.3911 | 95.0679 | 92.2101 | 81.6379 | 77.175 | 92.0333 | 80.224
Local batch jobs
Nearly 100% of jobs for Belle2
CPU time version is in backup slides
Low utilisation 6 months after system replacement
Almost fully utilised since March

## Slide 6: CPU efficiency (Only for Grid Jobs)
Runtime
CPU time
Chart: 
| 45536 | 45566 | 45597 | 45627 | 45658 | 45689 | 45717 | 45748 | 45778 | 45809 | 45839 | 45870
Belle VO | 0 | 1287542.0209 | 1555980.2481 | 4470001.1751 | 5337408.1315 | 8530447.6573 | 12925036.6324 | 10358521.8068 | 14954862.3502 | 7232286.9549 | 5219047.336 | 4518479.038
ILC VO | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.4177 | 99.7792 | 32.3505 | 5854.0401
Other VOs | 0 | 0.00042408 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Total | 0 | 1287542.0213 | 2843522.2694 | 7313523.4446 | 12650931.5761 | 21181379.2334 | 34106415.8658 | 44464937.6726 | 59419802.4406 | 66652189.1747 | 71871268.8612 | 76395601.9392
Chart: 
| 45536 | 45566 | 45597 | 45627 | 45658 | 45689 | 45717 | 45748 | 45778 | 45809 | 45839 | 45870
Belle VO | 0 | 11267621.6964 | 7579724.0546 | 19534650.936 | 11755019.3045 | 22560640.1322 | 21936984.6229 | 17376373.3606 | 17662634.6717 | 10863199.1554 | 12105477.2501 | 9266746.928
ILC VO | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 573.9729 | 5362.0978 | 2353.8352 | 133668.5777
Other VOs | 0.8666 | 582.3346 | 1031.7595 | 489.7889 | 699.4133 | 592.0271 | 586.5334 | 551.658 | 401.8548 | 342.8641 | 267.9238 | 511.619
Total | 0.8666 | 11268204.8975 | 18848960.7117 | 38384101.4366 | 50139820.1544 | 72701052.3137 | 94638623.4701 | 112015548.4886 | 129679158.9881 | 140548063.1054 | 152656162.1145 | 162057089.2392
10% of KEKCC for 100% availability
50% efficiency

## Slide 7: 5 PB of Belle2 RAW data for 0.5 ab-1 of total int. luminosity
2019a-b
0.5 PB
6 fb-1
2019c
0.1 PB
4 fb-1
2020a-b
1.5 PB
64 fb-1
2020c
0.8 PB
16 fb-1
2021a-b
1.4 PB
122 fb-1
2021c
0.3 PB
54 fb-1
* Belle2 RAW data centres: BNL, UVic, CNAF, DESY, KIT, and CCIN2P3
LS1
1.5 Years
2024a-b
0.8 PB
106 fb-1
2022a-b
0.8 PB
160 fb-1
w/ HLT
Contributes 50%+ spatial reduction
Int. L: 0.5 ab-1
w/o SROOT-ROOT conversion
Replaced rsync with xrootd
Garbage Collection
at the sharp drop-off
2024c
1.2 PB
45 fb-1
415
5.3

## Slide 8: Networking
Network hardware replacement in summer 2025
International network backbone

## Slide 9
10G-LR
10G-LR
XPDR
Ciena 6500
SINET
Grid System
KEKCC
FW SRX4100
J-PARC SW
J-PARC Router
J-PARC Campus Network
Outer SW 1
ARISTA 7280
KEK FW 1
PA
KEK FW 2
PA
Core SW 2
N9K
KEK Campus Network
Core SW 1
N9K
100G-SR4
100G-SR4
10G-SR
10G-SR
vPC
10G-SR
10G-SR
Ethernet6/47
Ethernet7/47
Ethernet12/22
Ethernet2/51
Ethernet1/22
Ethernet2/48
Ethernet3/48
Ethernet6/45
Ethernet7/45
Ethernet12/23
KEKCC SW
Nexus 9516
Outer SW 2
ARISTA 7280
MLAG
J-PARC
LHCONE
KEK
SINET
Sep 2024
Replaced in summer 2025!

## Slide 10
No change in total bandwidth before and after update (100G for LHCONE, 10G for Non-LHCONE traffic).
10G-SR
10G-LR
10G-LR
XPDR
Ciena 6500
SINET
Grid System
KEKCC
FW SRX4100
J-PARC SW
J-PARC Router
J-PARC Campus Network
Outer SW 2
Catalyst 9500
KEK FW 2
PA5410
KEK FW 1
PA5410
Core SW 1
C9K
KEK Campus Network
Core SW 2
C9K
vPC
10G-SR
10G-SR
Ethernet6/47
Ethernet7/47
Ethernet12/22
Ethernet2/51
Ethernet1/22
Ethernet2/48
Ethernet3/48
Ethernet6/45
Ethernet7/45
Ethernet12/23
J-PARC
LHCONE
KEK
SINET
Aug 2025
LHCONE
ARISTA 7280
100G-SR4
100G-SR4
KEKCC SW
Nexus 9516
Outer SW 1
Catalyst 9500
Bandwidth Bottleneck
10G-SR
Stack

## Slide 11: Recap: International Network Route Transatlantic Back Again
March 2024
Upgraded Feb 2019
Planned 100G x2+
84 ms to 120 ms for CC-IN2P3, Lyon, Fr
+50% longer
Siberian 100G route for Euro has been upgraded to the transatlantic route with 100G x4 lines
Dedicated line for the traffic between Japan and Euro, not shared with traffic for the US
To minimise the latency:
  traffic passes through fewer routers on the shortest route close to the Arctic
Changed on 26th March, 2024
Topic Today!

## Slide 12: JGN: Tokyo Hong Kong Line
Japan Gigabit Network (JGN) has been another LHCONE traffic backbone between Tokyo and Hong Kong for specific Asian sites, e.g., KISTI, ASGC, and IHEP, for a decade
  JGN is operated by NICT (MIC) but not NII (MEXT), our primary NREN provider
Decommissioned in December 2025
  Thank JGN for long-standing stable operation!

## Slide 13
S. Suzuki @ATCF9

## Slide 14: Grid Service Deployment Status
OS migration RHEL7 to RHEL9
Data transfer test in summer 2025

## Slide 15: Service Deployment as of Sep 2024 RHEL7 with ELS running a lot
Service | Service | OS | VM/Bare metal | Ethernet | IPv6 | HA | UPS
 | StoRM | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | 
 | VOMS | RHEL7 + ELS | VM | 10GE | ✅ | ✅ | ✅
 | IAM | RHEL9 | Bare metal | 10GE | ✅ | ✅ | ✅
 | AMGA | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | ✅
 | Top BDII | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | Site BDII | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | FTS3 | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | ARC-CE | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS Stratum Zero | RHEL9 | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS Stratum One | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS publisher | RHEL9 | VM | 10GE | ✅ |  | 
 | Frontier Squid HTTP Proxy | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
as Belle2 dedicated

## Slide 16: Decommissioning GridFTP, then SRM As of March 2025
Service | Service | OS | VM/Bare metal | Ethernet | IPv6 | HA | UPS
 | StoRM | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | 
 | VOMS | RHEL7 + ELS | VM | 10GE | ✅ | ✅ | ✅
 | IAM | RHEL9 | Bare metal | 10GE | ✅ | ✅ | ✅
 | AMGA | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | ✅
 | Top BDII | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | Site BDII | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | FTS3 | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | ARC-CE | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS Stratum Zero | RHEL9 | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS Stratum One | RHEL9 (Mar ‘25) | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS publisher | RHEL9 | VM | 10GE | ✅ |  | 
 | Frontier Squid HTTP Proxy | RHEL9 (Minor fix) | VM | 10GE | ✅ | ✅ | ✅
as Belle2 dedicated
Turned off GridFTP in January, SRM in March

## Slide 17: Ongoing migration campaign to RHEL9 As of September 2025
Service | Service | OS | VM/Bare metal | Ethernet | IPv6 | HA | UPS
 | StoRM | RHEL9 (Sep ‘25) | Bare metal | 10GE | ✅ | ✅ | 
 | VOMS | RHEL7 + ELS | VM | 10GE | ✅ | ✅ | ✅
 | IAM | RHEL9 | Bare metal | 10GE | ✅ | ✅ | ✅
 | AMGA | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | ✅
 | Top BDII | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | Site BDII | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | FTS3 | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
 | ARC-CE | RHEL7 + ELS | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS Stratum Zero | RHEL9 | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS Stratum One | RHEL9 | Bare metal | 10GE | ✅ | ✅ | 
 | CVMFS publisher | RHEL9 | VM | 10GE | ✅ |  | 
 | Frontier Squid HTTP Proxy | RHEL9 | VM | 10GE | ✅ | ✅ | ✅
as Belle2 dedicated
Migrated to SciTags-enabled DTNs on RHEL9

## Slide 18: Transfer Volume from/to StoRM (Not Including Internal Data Transfer)
Chart: Throughput (PB/Month)
| KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | KEK→ | →KEK | Sep-24 | Oct-24 | Nov-24 | Dec-24 | Jan-25 | Feb-25 | Mar-25 | Apr-25 | May-25 | Jun-25 | Jul-25 | Aug-25
Belle II RAW | 0.038359 | 0.037502 | 35.2917 | 48.7051 | 46.7948 | 10.0269 | 7.26 | 15.2394 | 63.9134 | 753.1679 | 0.47757 | 0.20462
Belle II RAW | 0.077269 | 0.074536 | 68.0399 | 88.7208 | 37.1005 | 2.5584 | 2.5998 | 0.047544 | 0.50025 | 488.22 | 74.7242 | 45.7335
Belle II Not RAW | 0.35513 | 0.44416 | 30.0929 | 50.1301 | 435.6849 | 104.0535 | 165.0321 | 196.9779 | 222.9954 | 277.9134 | 803.1047 | 640.2456
Belle II Not RAW | 5.4828 | 5.1999 | 423.6351 | 285.0211 | 966.5165 | 566.1158 | 528.4304 | 436.3141 | 289.8883 | 434.3286 | 222.8516 | 192.5238
Others | 0.00014608 | 6.6985e-05 | 0.0080625 | 0.90639 | 1.4041 | 2.9725 | 1.9618 | 0.016215 | 0.1045 | 2.6812 | 0.28082 | 3.1806
Others | 0.00053276 | 6.879e-05 | 0.13721 | 0.01314 | 1.5892 | 12.478 | 5.8824 | 0.36792 | 3.4156 | 0.14112 | 0.24456 | 0.36147
Total (KEK→) | 0.39364 | 0.87537 | 66.268 | 166.0095 | 649.8932 | 766.9461 | 941.2001 | 1153.4337 | 1440.4469 | 2474.2094 | 3278.0725 | 3921.7033
Total (→KEK) | 5.5606 | 10.8351 | 502.6473 | 876.4023 | 1881.6085 | 2462.7607 | 2999.6732 | 3436.4028 | 3730.207 | 4652.8967 | 4950.717 | 5189.3358
Data transfer test several times before OS migration
4 PB
5 PB
Regularly a few 100 TB in a month

## Slide 19: Half a day data transfer test between KEK and Belle2 RDCs (BNL, UVic, CNAF, DESY, KIT, and CCIN2P3)
Average throughput: 80 Gbps in both directions
The bottleneck at 100G
Most likely saturated at FTS optimisation limit (could be improved)
80 Gbps
80 Gbps
KEK→RDCs: 77.8 Gb/s Max: 88.0 Gb/s
RDCs→KEK: Mean: 64.0 Gb/s Max: 74.0 Gb/s

## Slide 20: Authentication and Authorisation
New CA is in production
Migrating X.509/VOMS to JWT/IAM

## Slide 21: KEK Grid CA and beyond
Initially only for domestic users, then extend the service for specific experiment members outside Japan, e.g.: Belle2
CA’s root certificate will expire soon (in this month)
Expected to migrate from X.509 to JWT authentication by the date – Unfortunately not!
Launched a new CA (KEK Grid CA 2024) in September 2025 to continue X.509-based auth. for the next few years
  Accredited and included in the latest EGI Trust Anchor v1.137 (Sep 15, 2025)
  New root certificate has longer validity and a signature signed by a more secure algorithm, i.e.: SHA-2
  The current root certificate is signed by SHA-1, which NIST has disallowed 10+ years ago
3.8K user certs
4.5K host certs
20 years operation
Chart: Issued Certificates (x1,000)

## Slide 22: Migrating X.509/VOMS to JWT/IAM
IAM instances have been deployed for Belle2
  Verified some basic use cases (TPC with FTS) using token-based authentication
  Will have mini-DC using JWT to be ready for co-operated Data Challenge between Belle2 and Hyper-K in 2027
In transition phase toward Token-only AuthNZ:
  Currently, VOMS registration service for personal identification with X.509, then synchronise to IAM
  Started IAM as VOMS (with VOMS AA) authentication in September 2025
  Still highly rely on X.509 (CA)
Need to replace CA’s functions such as: in-person personal identifiy verification
  Developing KEK’s institutional IdP to federate with GakuNin – the academic ID federation, lead by NII, (and eduGain)
  Plan to upgrade IAL2 (Identity Assurance Level 2)
  Then, move forward decommissioning VOMS and CA
Periodic sync.
VOMS
X.509 proxy cert issuer
IAM
Token provider
Request tokens, or VOMS cert
User registration process, co-working with IAM
Personal identification with X.509
Registration Service

## Slide 23: Summary
KEKCC has been in production in September 2024
  Just completed the first year of four-year contract
   Well utilised (~90%)
OS migration campaign to RHEL9 is ongoing
  Completed: CVMFS and StoRM DTNs
  Achieved 80+ Gbps throughput between KEK and B2RDCs
    Belle II HL scenario: 40 TB/day (3.7 Gbps)
APAN-JP (AS7660) will take over operating the Tokyo-HKIX link from JGN in 2026
A new CA (KEK Grid CA 2024) has been successfully launched in September 2025!
  Ongoing to deploy IdP for migrating to JWT/IAM

## Slide 24: Thank you for your attention!