## Slide 1: BLM for the Injectors project LINAC4 & PSB - additions
Beam Instrumentation Review – 19/10/2011

## Slide 2: ACFC principle
A status signal selects in which branch of a fully deferential stage the input current is integrated.
Two comparators check the deferential output voltage against a threshold, whenever is exceeded, the status signal changes to the complementary value (0 ! 1 or 1 ! 0) and the input current is integrated in the other branch.

## Slide 3: ACFC data processing
0
Time
counts
2 μs
2 μs
2 μs
ADC values
thhigh
thLow
The number of counts accumulated are combined with the ΔADC values to provide the integrated loss over 2 μs.
Most of the operation is handled by the FPGA . That is, counting of pulses , clock the ADC and make difference of the ADC values.