## Slide 1: MS-5024: Supply of Transmitters for the HL-LHC High Power RF System

## Slide 2: RF system
FPC
HPRF High Power RF station (including power transmission lines)
FPC Fundamental Power Coupler
HOMC High Order Mode Coupler
LLRF Low Level RF
HPRF
Cryomodule
LLRF
Controls
HOMC

## Slide 3
P5 - CMS
P1 - ATLAS
Surface
Underground
100m
LHC undergroud
Integration HPRF
8 Crab Cavities
8 Power Amplifiers IOT
8 Circulators
8 Loads
2 Faraday Cage
8 Crab Cavities
8 Power Amplifiers IOT
8 Circulators
8 Loads
2 Faraday Cage
Four different places with four HPRF stations each
Total 16 HPRF stations

## Slide 4
Point 1
Point 5
Left side
Right side
The cavities are powered by 4 amplifiers IOT 400MHz.
One for each cavity.
The 4 circulators and 4 loads are placed close the access holes, to be connected with the WR2300 adapter.
Integration of the HPRF in the galleries

## Slide 5
Integration of the HPRF in the galleries
1
2
3
4
The cavities are powered by 4 amplifiers IOT 400MHz. One for each cavity.

## Slide 6: Power requirements from HPRF system
10 seconds
10 ms
RF output power [kW]
40 kW → 50 kW
Time
80 kW → 100 kW
Average output power is ~ 50 [kW]
0 kW

## Slide 7: HPRF stations Technical Specification
High Voltage Power Supply;
Satellite auxiliary power supplies (heater, coil, grid, ionic pump, controls, etc…);
Tube protective system (crowbar);
Cooling subsystems;
PLC control system (monitoring, interlocks, sensors, interfaces, etc…).
PARAMETERS AND CONDITIONS | VALUES
Maximum dimensions (L x l x h) | 2.0 × 2.0 × 2.5 meters
Input power | 480 VAC / 250 A – 50 Hz
Collector voltage | 35 to 40 KV, by steps of 0.5 kV
Focus power supply | 0 to 30 V / 0 to 30 A, floating at minus collector voltage from ground
Ionic pump power supply | 5 kV / 5 mA, floating at minus collector voltage from ground
IOT Grid power supply | 0 to minus 200 V / 0 to 1 A, floating at minus collector voltage from ground
Continuous operation | 24/24 hours, 7/7 days, 11/12 months per year

## Slide 8: Integration of the HPRF in the galleries
Volume L x l x h each HPRF station must be
maximum 2 x 2 x 2,5 meters all inclusive
Inside a gallery  NO possibility to increase the size !

## Slide 9: Detailed Schedule – MS-5024: Supply of Transmitters for the HL-LHC High Power RF System
Tender Process Milestones | Provisional Schedule
MS-5024 documents dispatched to firms | 18 November 2024
MS Industry Webinar | 12 May 2025
MS answers submission | Link still open on CERN’s forthcoming page: https://forthcoming-ms.app.cern.ch/#!/
Dispatch of IT documents to firms | Mid-May 2025
Submission deadline for bidders | Mid-June 2025
Finance Committee and contract award | September 2025
Contract start-up | September 2025

## Slide 10: MS-5024 – Key Qualification requirements
Distribution of the Contract performance
  The Lead Firm shall provide the design.
Minimal annual turnover of 6m CHF per annum and appropriate levels of staff resources
Proven competence and experience in design and manufacturing in the field of High-Power RF Systems.
  Design, Assembly and Testing of high-power electrical equipment for RF applications.
  Provide relevant references that are similar in scope, complexity and volume.

## Slide 11: MS-5024: Distribution of Contract Performance
Technical deliverables and activities | Shall be performed by the Firm or the Lead Firm only | May be performed by any member of the Group of Firms | May be subcontracted
Contract management | x |  | 
Procurement of raw materials and components |  | x | x
Detailed Design File | x |  | 
Manufacturing of the Supply |  | x | x
Assembly of Supply |  | x | x
Factory Acceptance Tests |  | x | x
Technical documentation |  | x | x
Packing of the Supply |  | x | x
Commissioning |  | x | x
Additional deliverables and / or activities |  | x | x