## Slide 1: Electron gun & collector for the new AD e-cooler Numerical assessment
Teresa Guillen Hernandez
10/04/2025

## Slide 2: Geometry and materials
Material | Elastic modulus [MPa] | Yield stress [MPa] | Ultimate stress [MPa]
Alumina | 390 | 300 | 400
SS 304L | 200 | 175 | 450
Tungsten | 405 | 750 | 980
Symmetry
Coef. of thermal expansion
Thermal conductivity
Plasticity 304L
Plasticity Tungsten
Notes: 58% elongation at break inox

## Slide 3: Mechanical analysis - gravity
Operation support
Very low stresses
Rankine criteria |  | 
= 0.55 MPa | ⩽ | = 259 MPa
= 0.55 MPa | ⩽ | = 2900 MPa
Rankine criteria |  | 
 | ⩽ | 
 | ⩽ | 
Notes: OPERATION SUPPPORT - Fixed support at 205mm from the flange.

## Slide 4: Cooling ?
Cooling needed

## Slide 5: Thermo-mechanical analysis – No tantalum
St steel
Tungsten
Higher temperatures
(T max ceramic 147 °C)
smaller area
(T max ceramic 115 °C)
Stresses ceramics
= 80 MPa
= 117 MPa
Stresses ceramics
= 93 MPa
= 135 MPa
Titanium kind of between in terms of temperatures
(T max ceramic 138 °C).
Similar to St steel in terms of plasticity.
Ceramics = 15 MPa and = 18 MPa
Notes: Which is the limit of plasticity we can afford?? To be checked how much is this plasticity in terms of deformation
Ratcheting – 20% in 15 cycles (from 2.4% to 2.9%)
Tungsten higher thermal conductivity, so we are hotter (conduction), and we have more radiation.
Thermal expansion of Titanium smaller, less stresses on the ceramic

## Slide 6: Thermo-mechanical analysis – new conf to reduce plasticity
Thicker and bigger contact
Thinner and smaller contact
Lower temperatures
Lower stresses
= 80 MPa – 66 MPa
= 117 MPa – 97 MPa
Plasticity??
Notes: LOWER TEMP. Less conduction, so colder and therefore, less radiation
Lower stresses everywhere
Plasticity???? Not much difference

## Slide 7: Conclusions
Cooling needed
Titanium flanges reduce the stresses on the ceramics
We will have plasticity. How much we can afford?
Ratcheting is a problem
Reduce the thermal contact and made it more flexible