## Slide 1: Status of the CRIS experiment
Kieran Flanagan
University of Manchester

## Slide 2: Outline of talk
Introduction to collinear resonant ionization spectroscopy (CRIS)
Progress since 2008
Recent Results: laser spectroscopy of Fr
Outlook

## Slide 3: Nuclear moment and radii from laser spectroscopy
3s
3p
2P3/2
2P1/2
2S1/2
Fj
Fi
Spin, magnetic and electric
moments , all nuclear
observables are extracted
without model dependence.
DnIS = DnMS + DnFS
Isotope Shift
ppm shift
Changes in nuclear charge
radii and sensitive to changes in the dynamic nature and deformation as well as volume.

## Slide 4: Sensitivity or resolution?
Relative Frequency (GHz)
68Cu
ΔE=const=δ(1/2mv2)≈mvδv
10
0
10
20
Collinear Concept
Applied Doppler
tuning voltage
For ionic spectroscopy
Doppler tuning voltage
applied to light collection
region
PMT
Charge
exchange
Ion
Source
Separator
electrostatic
acceleration
In-source
laser spectroscopy
Sensitive to sub 1 atom/s but limited by Doppler broadening to cases with large hfs
High resolution (sub 10MHz) but low sensitivity (>106 /s)

## Slide 5
Status of laser spectroscopy
Since 1995
Before 1995
Z
N
J. Phys. G 21 707 (1995)
Gaps in chart
Production difficulties
Half life
Chemistry
Atomic physics
J. Phys. G 37 113101(2010)

## Slide 6
Collinear Resonant Ionization Spectroscopy (CRIS)
Combining high resolution
nature of collinear beams
method with high sensitivity
of in-source spectroscopy.
Allowing extraction of
B factors and quadrupole
moments.
Relative Frequency
(GHz)
68Cu
10
10
0
10
20
4GHz
30MHz
Yu. A. Kudriavtsev and V. S. Letokhov,
Appl. Phys. B29 219 (1982)

## Slide 7: Previous CRIS at JYFL
Relative frequency (MHz)
2000
4000
Ion Counts
50
30
1:30 From Jyvaskyla off-line tests
Factor of 1000 improvement on photon detection
High background rate 5cts/bunch
150MHz linewidth

## Slide 8: Status in 2008
Proposal to the INTC accepted
New beam line to be
located in the old
COMPLIS area.
COMPLIS decommissioning
scheduled for the summer
of 2008.
Design work for new beam line started in spring of 2008.

## Slide 9: Technical Design
Basic scheme went through several iterations before converging on the final design in 2008.
UHV requirements constrained the design and forced the beam line to be ~3m in length

## Slide 10: November 2008
Initial Installation of railway track for the beam line. The concept allows an individual to remove vacuum sections.

## Slide 11: April 2009
Beam line installation

## Slide 12: 2009: Vacuum testing
Initial bake out of the UHV section and differential pumping tests.
Charge exchange cell and hot oil circulator was tested (with mixed results)

## Slide 13: 2010: Ion optics installation

## Slide 14: Ion optic tuning
National Instruments PXI based system
Can control up to 36 high voltage supplies (currently 20 supplies are used)
System uses 5kV and 10kV Spellman supplies (MPS series)
Signal from a Keithley picoammeter is transferred to the PC for tuning.

## Slide 15: 2010: Installation of lasers

## Slide 16: October 2010

## Slide 17: 2011:Off-line ion source
Diagnostics on the ion source were carried out with a wire scanner and a Faraday cup.
A LabView programme was created to apply volts to the steering and focusing optics in the chamber, and to read the current on the Faraday cup.

## Slide 18: Ion source tests
Optimizing the ion beam profile using the optics of the Einzel lense.
The current on the ion source was set at 40 A and the bias voltage was 2 kV.
Stable operation of 100-300pA over many days of use.
Currently tested with Rb, Cs and In.

## Slide 19: MCP detector installed and tested
MCP arranged to look at secondary electrons from a biased copper dynode.
For beam tuning the dynode acts as a Faraday cup.
TOF spectra of a bunched Rb beam from ISCOOL measured.
~103 ions/bunch
FWHM~1μs

## Slide 20: Re-ordering of quantum states in Francium
π(1/2+) proton intruder state becomes the ground state in 195At and 185Bi
Systematic reduction in energy of the
deformed π(1/2+) in isotopes in this
region of the chart
Suggestion that 199Fr has
I=1/2+ ground state spin
with an associated large
oblate deformation.
1/2+
7/2-
9/2-
1/2+
7/2-
9/2-
201Fr
203Fr
The isomer shifts of 201,203Fr
and their magnetic moments
will provide important
information to better
understand the evolution of
nuclear structure in this region.

## Slide 21: On-line run 2011
Commissioning run of the CRIS experiment
Goals of the experiment
  Demonstrate CRIS at ISOLDE
  Demonstrate laser assisted decay spectroscopy with CRIS (Kara Lynch)
  Fully commission the beam line (charge exchange cell, high voltage tuning, ion detection setup and digital data acquisition.
  Test new laser system for CRIS.

## Slide 22: Data Acquisition
MCP/PMT
Laser system
Trigger generator
Lecroy digital scope
NI PXI chassis
Voltage scanning (PC)
Data Acquisition PC
ISCOOL

## Slide 23: Digital Data Aquisition
Example of an ion bunch recorded by the digital data acquisition.
Full time stamping of every event for off-line analysis.

## Slide 24: Beam tuning effect
Associated with a misalignment of the beam through the charge exchange cell. As a high voltage is applied to the cell the beam is further deflected.
Negative voltage
Positive voltage

## Slide 25: Results
Resonant ionization of Fr
Two step scheme.
1064nm laser off
Laser on
Laser off

## Slide 26: Results
Further optimization of the 422nm (scans carried out over a range 20-200μJ/pulse.
Majority of the background is due to 422+422 non-resonant ionization.
With both lasers blocked the observed background is associated with collisional ionization.
Pressure ~1-2x10-8mbar
Laser on
Laser off

## Slide 27: Results: HFS of 207Fr
Literature: A(S1/2)=8484(1)MHz I=9/2
Preliminary result from this work: A(S1/2)=8390(100)[200]MHz
Low background
rate~0.05/s
Efficiency~1:106
Low power 1064
Noise in the mcp
Transmission (10%)

## Slide 28: Results: resolution
Multiplet of three transitions within the peak.
Linewidth ~1GHz.
Preliminary results.
Analysis is on-going.
New laser system was used in this experiment. Characteristics of this device are under study.

## Slide 29: Summary
Beam line fully commissioned
~50% neutralization efficiency of Fr demonstrated. Beam mistuning minimized.
First hyperfine spectra of Fr measured.
Digital data acquisition demonstrated
Decay spectroscopy station demonstrated (Kara Lynch, the next talk)
Suppression of Fr (with lasers off) is ~ factor of 10000
Currently low experimental efficiency, can account for some this effect.

## Slide 30: Outlook for 2012
On-going off-line tests using the CRIS beam line and ion source.
New atomic beam unit has been constructed to study future RIS schemes and better test the laser system.
Further on-line experiments planned for Fr and now also neutron rich Cu.

## Slide 31: Many thanks to the ISOLDE team and all of the people involved in the CRIS project.

## Slide 32: Thank you for your attention
J. Billowes, M.L Bissell, B. Cheal, T.E. Cocolios, A. Dax, K.T. Flanagan, M. Hori, H. A. Khozani‎, T. Kobayashi, F. Le Blanc, O. Levinkron, D. Lunney, K.M. Lynch, G. Neyens, T.J. Procter, M.M. Rajabali, S. Rothe, A.J. Smith, A. Soter, H.H Stroke, W. Vanderheijden, K. Wendt.
Collaboration