## Slide 1
All texts, comments, illustrations and images contained in the documentation of any kind provided by SuReal are the exclusive property of SuReal and are protected worldwide by copyright and intellectual property laws. Any reproduction in whole or in part without the prior consent of SuReal is strictly prohibited.
26/05/2025
Certifications in Sustainable Real Estate

## Slide 2
Together, we go towards
a zero carbon society.
Who is SuReal?
SuReal is a “boutique” consultancy firm offering strategic ESG advice to very in-depth expertise in all domains of sustainability. We guide investors, developers, architects, governement agencies, contractors, manufacturers and general companies in making their projects, standing assets and companies more sustainable.
Our approach is not based on gimmicks or greenwashing but on truly realistic and future-proof actions with one sole aim: having an impact on society.
> 6.000.000
> 6.000.000
> 1.200.000
14
30
m2 of ESG Guidance
m2 Real Estate projects
CO2eq.ton/year saved
countries operative
sustainability experts

## Slide 4: Context
INTRODUCTION
BREEAM
WELL
MINERGIE
EXAMPLES
Q&A

## Slide 5
From greenwashing
to green
Understanding the why

## Slide 6
MINERGIE

## Slide 7
Source: Sphera

## Slide 8
3 pillars

## Slide 9: Benefits – Why?
Internationally recognised
Third-party assurance
Asset, portfolio and market level benchmarking
Enhancing economic and social value
Build trust
Better performing assets
Increased asset value
Mitigated asset and reputation risk
Easy to assess costs
Reduce operational costs
Contribute to ESG goals
Risk Management and Asset value
Deliver positive impact
Assessment & solutions for various sustainability goals
A credible scientific framework to inform decisions
Disclosures and reporting on international commitments and regulations
Mitigating environmental impact
Notes: Commercieel succes
Vertrouwen opbouwen
Possitieve impact

## Slide 10
BREEAM

## Slide 11
Object | Integrated sustainability
Origin | UK
Historic | 1990
Independant certification organisation | Yes, independant third party verification
Recognition | International recognition
Cotation system | Themes (10), points (prerequisite and optional)
Additional construction cost | +- 0,5% - 4% of construction cost
Certificate validity | Depending on type of certificate
ESG importance | Clear link with SDG’s, ESRS & EU Taxonomy – focus buildings
BRE : Building Research Establishment
- EAM : Environmental Assessment Method

## Slide 12: Scopes

## Slide 13: New Construction scheme
The New Construction standards can be used to assess the design, construction, intended use and future-proofing of new building developments, including the local, natural or manmade environment surrounding the building.
The standards can be used to assess most types of new buildings, including new homes and new-build extensions to existing buildings. Each uses a common framework that is adaptable, depending upon the building’s type and location.
The manual will be updated during 2025 and will be stricter than the V6 version.

## Slide 14: Refurbishment & Fit-doo Scheme
Mainly applied to renovation. Different parts to be chosen from:
  Part 1 : Fabric and Structure
  Part 2 : Core Services
  Part 3 : Local Services
  Part 4 : Interior Design
Same themes but adapted credits available
Example : ENE 01 is an audit of the building and not a PEB file
Is particularly adapted for Heritage building (adapted credits, stricter or softer)
-> A renovation project can also be considered for the New Construction scheme but tougher credits

## Slide 15
BREEAM In-Use is an environmental assessment method that enables property investors, owners, managers and occupiers to determine and drive sustainable improvements in the operational performance of their buildings. It provides sustainability benchmarking and assurance for all building types.
Certification is valid for 3 years
In-Use scheme

## Slide 16: Environmental Categories (New Construction and RFO)
Energy
Health & Wellbeing
Innovation
Land use
Materials
Management
Pollution
Transport
Waste
Water

## Slide 17: Ratings

## Slide 18: Assessment Stages
Concept design
Detailed design
Design Stage Certificate
Post Construction Stage Certificate

## Slide 19: Assessment Stages BREEAM
Design and brief
Detailed Design
Construction
Post construction
Concept Design
Concept
Design development
Technical design
Production information + Building specifications
Tenderinjg documentation
Modificating and evidence gathering
Construction to practical completion
Post construction
Initial occupation
Evaluating
Starting to design
Pre assessment
Design stage assessment
Construction stage assessment
Final PCS BREEAM CERTIFICATE
BREEAM
PERMIT
RECEIVED
CHOOSE DESIGN TEAM
REGISTER PROJECT
BUILDING COMPLETION
PERMIT
SUREAL
WELL
Interim design stage CERTIFICATE
Registration + pre assessment
Pre certification
Final PCS WELL CERTIFICATE
Registration + pre assessment
Hand-in + correct remarks
Hand-in + correct remarks

## Slide 20
WELL
Healthier companies outperform their peers

## Slide 21: WELL
Object | Wellbeing of users
Historic | 2015
Independant certification organisation | Yes
Recognition | International recognition
Origin | USA
Cotation system | Themes (10), points (prerequisite and optional)
Cost | +- 0,6% - 5%
Certificat validity | 3 years, then recertification
CSR importance | Beyond buildings – best integration
from IWBI : International Well Building Institute

## Slide 23
WELL Certification

## Slide 24
Education
Restorative
Promote
Controllability
Prevention
Communication
Accessibility
Adaptability
On site performance test
Management
Certification validity
WELL Certification

## Slide 25
WELL Core
WELL Community
WELL Portfolio
WELL Certification
WELL Scopes

## Slide 26
Types of evidences :
On site performance testing and photographic evidence
Policies and operational schedule
Professional narratives
Technical drawings and documents
Ongoing reporting
WELL Evidences
Notes: There is a testing after in contrary with BREEAM

## Slide 27: WELL Features
Air
Water
Nourishment
Light
Movement
Thermal Comfort
Sound
Materials
Mind
Community

## Slide 28: WELL Timeline Recertification

## Slide 29: Ratings
Notes: Platinium: only if cooperation with tenant
Gold: only promoter

## Slide 30
MINERGIE

## Slide 31
MINERGIE
Minergie promotes sustainable and high-quality buildings by focussing on reducing energy consumption while still enhancing comfort within buildings. It introduces stringent requirements for insulation, air tightness and the use of renewable energy sources.
Minergie is recognised as the most important sustainability standard for buildings in Switzerland. It is furthermore aligned to legislation and can be used in the Canton Geneve to comply to standards in terms of energy.
The Minergie label defines clear elements that all have to be implemented in the building to obtain the label, and is thus not a label like BREEAM where multiple options are necessary to come to the required result.
Notes: The benefit of Minergie, compared to BREEAM, is that it’s simpler to implement as there is a clear list of requirements, if you reach all of them, you have the label. In that sense it is thus closer to the EU Taxonomy. There is thus no system of different levels of label.
It can be used to comply to the requirements of the Canton Geneva in terms of energy: a building that is Minergie certified is HPE (Haute Performance Energetique) and a building that is Minergie-P-Eco or Minergie A is THPE (Tres Haute Performance Energetique). HPE is required as a minimum, THPE can be used to get extra subsidies from the Canton.
It is significantly stricter than BREEAM in terms of energy, which is the main focus. The comfort is more in line with BREEAM, but a bit more difficult to obtain in terms of thermal comfort.

## Slide 32
Basis version of Minergie
Focus on energy efficiency and thermal comfort
Minimisation of energy consumption
On top of Minergie Base
Aims for ultra-low energy consumption
Envelope of the highest quality
On top of Minergie Base
Net-zero energy balance
Produce as much energy as it consumes
Supplement to be added to any other version of Minergie
Introduction of extra aspects of ecological construction and health
MINERGIE Versions
Notes: Minergie is the basic version, requirements on thermal comfort, consumption, thermal comfort and (very light) LCA requirements
Minergie-P contains all requirements of the Minergie Base but is close to the passive house standard. There is very high standards on the envelope (such as results of blower door test).
Minergie-A contains all requirements of the Minergie Base but focusses on net-zero energy. A Minergie A building has to produce as much energy as it consumes.
Minergie Eco can be added on top of all other Minergies, and contains extra requirements on health of the occupants (like WELL) and ecological construction. It functions as BREEAM or WELL: it is a list of credits where at least 50% of these credits has to be implemented.

## Slide 33
MINERGIE Requirements
Source: Minergie.ch
Notes: To be seen if interesting: This slide contains all the requirements of Minergie Base, P & A.

## Slide 34
EXAMPLES OF SUCCES

## Slide 35: Well being
© Amazon Office
BREEAM + WELL communities Accessibility

## Slide 36: Well being
© Amazon Office
BREEAM + WELL communities green and social cohesion

## Slide 37: Windows: Daylight and view out
>30% is within 6 m of windows
80% of occupied spaces have an average daylight factor (2%) and minimum daylight point of min 0.6%.
Window-to-wall ratio >20%
View out of min. 10 m
Façade Belliard
Notes: L01.1: Provide Indoor Light
At least 30% is within 6 m of windows Hea 01: Daylight
80% of occupied spaces have an average daylight factor (2%) and minimum daylight point of min 0.6%.
Hea 01: View out
Window-to-wall ratio of at least 20%+ view out of min. 10 m 15% of occupants can sit in common space

## Slide 38
70 m
<0,6
Glazing properties:
Ug: 0,54
g-value: 0,3
LT: 60%

## Slide 39
Daylight
Thermal comfort
Daylight
Energy
Optimal Solution
$
CO2
Low energy
consumption
Thermal comfort
Hea04
T01
Hea01
L01
L06
Ene01
Ene04

## Slide 40: Comfort and Energy
©SuReal

## Slide 41: Embodied carbon

## Slide 42: Energy

## Slide 43
Climate Change Adaptation

## Slide 44
Q&A

## Slide 45
All texts, comments, illustrations and images contained in the documentation of any kind provided by SuReal are the exclusive property of SuReal and are protected worldwide by copyright and intellectual property laws. Any reproduction in whole or in part without the prior consent of SuReal is strictly prohibited.
Sunita.vanheers@sureal.be
Thank you