## Slide 1: Progress Update #4 Payton Harvill
29.04.2025

## Slide 2: Reminder From Last Time:
Coding Improvements:
  New frequency indexing method: multiplies detected peaks by estimated period and rounds to nearest index.
  Improved consistency in period calculations but still large uncertainty (30ns–100ns).
  Considering alternative analysis methods due to issues in low SNR cases.
Magnesium Systematics:
  30 MHz discrepancy observed; Zeeman splitting ruled out.
  New theory: Photon recoil and laser power dependence cause resonance shifts.
  Plan: Measure Mg resonance at different laser powers to quantify shift.

## Slide 3: Improving the Uncertainty Calculation:
The Scipy method I use for fft production and peak detection uses a covariance matrix for error propagation but based on the covariances between the fitted parameters from the linear fit.
Now, I want to try to use a monte carlo method for error calculation to see if that will better represent the uncertainty within my dataset– we’ll see how that goes.
Additionally, we use an AOM (Acousto-optic modulator) in the experimental setup. I realized that whenever it switches, there is a signal that the PMTs can detect. This is prevalent in sweeps when there are no ion bunches being detected, so I will remove the indices where this occurs in PMTs as sort of a “background subtraction” with the sweeps where there are ions being detected.

## Slide 4: Magnesium Systematics

## Slide 5: Testing Photon Recoil
In order to confirm this phenomenon we performed three main runs changing specific variables:
Changing the amount of helium buffer gas in the paul trap to change the amount that we cool the ions in our bunches
Change the number of ions in each bunch by changing the loading time of ions to the trap
Doing this with both the anticollinear and collinear lasers and changing the laser power for multiple runs because the direction of propagation of the laser (theoretically) has a different effect on the photon recoil effect
From last time: Photon Recoil
Results from ions absorbing or emitting photons, which transfers momentum and alters their velocity. In MR-TOF devices, this leads to a shift in resonance frequency.
There is also a laser power dependency: the higher the laser power, the larger the centroid (of resonance frequency) shift

## Slide 6: The end.