## Slide 1: CERN’s Accelerator Complex Connecting the dots…
Alex Huschauer BE/OP

## Slide 2: Topics
The CERN Accelerator Complex
Satisfying the Experiments
The Next Step

## Slide 3: Topics
The CERN Accelerator Complex
Satisfying the Experiments
The Next Step

## Slide 4: Our Accelerator Complex

## Slide 5: Linear Accelerator 4 (LINAC4)
The source is extracting H- ions at an energy of 45 keV
Accelerates beam up to 160 MeV
Can provide a pulse of H- ions every 1.2 s
P+
e-
e-

## Slide 6: Our Accelerator Complex

## Slide 7: Proton Synchrotron Booster (PSB)
1st circular accelerator with 4 superposed rings
Circumference of 157 m
Accelerates protons from 160 MeV to 2 GeV
Each ring will inject over multiple turns, using charge exchange injection
  Converting H- into protons
Can cycle every 1.2 s
x’
x
+
-
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Before stripping foil
x’
x
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Behind stripping foil
The (PSB) cycle
1.2 seconds

## Slide 8: Our Accelerator Complex

## Slide 9: Proton Synchrotron (PS)
The oldest operating accelerator at CERN
Circumference of 628m
Increases energy from 2 GeV to max. 26 GeV
Cycle length ranges from 1.2s to 3.6s
Many RF systems allow for complex beam manipulations
  Among others, the 25 ns bunch spacing for LHC
Various types of extractions:
  Fast extraction
  Multi-turn extraction (MTE)
  Slow extraction

## Slide 10: Our Accelerator Complex

## Slide 11: Super Proton Synchrotron (SPS)
The first accelerator in the chain at ~30m under ground
Circumference of 6.9 km
Increases proton beam energy up to 450 GeV
Provides:
  Slow extracted beam to the North Area
  Fast extracted beam to LHC, AWAKE and HiRadMat

## Slide 12: Our Accelerator Complex
Clock-wise
Counter
Clock-wise

## Slide 13: Large Hadron Collider (LHC)
1232 main dipole magnets that deviate the beams around the 27 km circumference
392 main quadrupole magnets that keep the beams focused
~6000 corrector magnets to preserve the beam quality
Main magnets use superconducting cables (Cu-clad Nb-Ti)
12’000 A provides a magnetic field of 8.33 Tesla
Operating in 150 tons of superfluid helium at 1.9K

## Slide 14: Large Hadron Collider (LHC)

## Slide 15: Topics
The CERN Accelerator Complex
Satisfying the Experiments
The Next Step

## Slide 16: The Injectors Preparing LHC Beams
To LHC clock-wise or counter clock-wise
East Area
nTOF
nTOF
East Area
ISOLDE
nTOF
nTOF
ISOLDE
ISOLDE
ISOLDE
ISOLDE
PSB
PS
SPS
Time

## Slide 17: The LHC Cycle
Injection
Ramp
Stable Beams
Squeeze
&
Adjust
Ramp down
450 GeV
6.8 TeV

## Slide 18: Integrated Luminosity

## Slide 19: Topics
The CERN Accelerator Complex
Satisfying the Experiments
The Next Step

## Slide 20: The High-Luminosity LHC upgrade is under way
The HL-LHC will use new technologies to provide 10 times more collisions than the LHC
The stored beam energy will increase from ~300 MJ to ~600 MJ
It will give access to rare phenomena, greater precision and larger discovery potential
It will start operating in 2030 and run until 2041

## Slide 21: New Facilities and Equipment Being Added

## Slide 22: The CERN Long-Term Schedule
Run 3
Long shut-down 3
Run 4
Long shut-down 4

## Slide 23
The future lies ahead, waiting to be shaped
Success with your career at CERN!