## Slide 1: Some examples of scientific impact
M. Campbell1, J. Alozy, R. Bolzonella, R. Ballabriga, E.H.M. Heijne2, X. Llopart, M. Saphorster3 and L. Tlustos2
CERN, PH Department
1211 Geneva 23
Switzerland
1 Honorary Professor at Glasgow University
2 also with IEAP, Prague
3 also with DFKZ, Heidelberg
Notes: I am going to talk about the hybrid pixel detector readout chips that have been designed at CERN in the framework of the Medipix2 and 3 collaborations.

## Slide 2: Disclaimer
I can never do justice to the huge amount of high-quality work and publications from our Collaboration members with ~25 min
I have tried to select topics which are complementary to those covered in the other presentations
These are just a few examples from those who provided recent input to me
There is a bibliography in the backup slides
Apologies if your favourite detector or application is missing

## Slide 3: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 4: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 5: Scopus search “medipix” OR “timepix”
Extracted from Scopus: 19th Sept 2025

## Slide 6: Scopus search “medipix” OR “timepix”
Extracted from Scopus: 19th Sept 2025

## Slide 7
Citations | Authors | Title | Year | Source title | Volume | Issue | Page | EID
912 | Llopart X.; Ballabriga R.; Campbell M.; Tlustos L.; Wong W. | Timepix, a 65k programmable pixel readout chip for arrival time, energy and/or photon counting measurements | 2007 | Nucl. Inst. and Meth. A | 581 | 1-2 SPEC. ISS. | 485 | 2-s2.0-35348817342
674 | Llopart X.; Campbell M.; Dinapoli R.; San Segundo D.; Pernigotti E. | Medipix2: A 64-k pixel readout chip with 55-μm square elements working in single photon counting mode | 2002 | IEEE Transactions on Nuclear Science | 49 I | 5 | 2279 | 2-s2.0-0036815755
463 | Poikela T.; Plosila J.; Westerlund T.; Campbell M.; Gaspari M.D.; Llopart X.; Gromov V.; Kluit R.; Beuzekom M.V.; Zappon F.; Zivkovic V.; Brezina C.; Desch K.; Fu Y.; Kruth A. | Timepix3: A 65K channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout | 2014 | Journal of Instrumentation | 9 | 5 | C05013 | 2-s2.0-84903648134
254 | Ballabriga R.; Campbell M.; Heijne E.H.M.; Llopart X.; Tlustos L. | The Medipix3 prototype, a pixel readout chip working in single photon counting mode with improved spectrometric performance | 2007 | IEEE Transactions on Nuclear Science | 54 | 5 | 1824 | 2-s2.0-35348948593
248 | Jakubek J. | Precise energy calibration of pixel detector working in time-over-threshold mode | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S262 | 2-s2.0-79959818317
215 | McMullan G.; Chen S.; Henderson R.; Faruqi A.R. | Detective quantum efficiency of electron area detectors in electron microscopy | 2009 | Ultramicroscopy | 109 | 9 | 1126 | 2-s2.0-67650544797
200 | Ponchut C.; Rigal J.M.; Clément J.; Papillon E.; Homs A.; Petitdemange S. | MAXIPIX, a fast readout photon-counting X-ray area detector for synchrotron applications | 2011 | Journal of Instrumentation | 6 | 1 | C01069 | 2-s2.0-79952662448
199 | Ballabriga R.; Campbell M.; Heijne E.; Llopart X.; Tlustos L.; Wong W. | Medipix3: A 64 k pixel detector readout chip working in single photon counting mode with improved spectrometric performance | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S15 | 2-s2.0-79959823582
182 | Turecek D.; Holy T.; Jakubek J.; Pospisil S.; Vykydal Z. | Pixelman: A multi-platform data acquisition and processing software package for Medipix2, Timepix and Medipix3 detectors | 2011 | Journal of Instrumentation | 6 | 1 | C01046 | 2-s2.0-79952653981
169 | Holy T.; Jakubek J.; Pospisil S.; Uher J.; Vavrik D.; Vykydal Z. | Data acquisition and processing software package for Medipix2 | 2006 | Nucl. Inst. and Meth. A | 563 | 1 | 254 | 2-s2.0-33745003477
Extracted from Scopus: 12th Aug 2025
Top 10 publications mentioning ‘Medipix’ OR ‘Timepix’ in Abstract, Title, Keywords by number of citations

## Slide 8
Citations | Authors | Title | Year | Source title | Volume | Issue | Page | EID
912 | Llopart X.; Ballabriga R.; Campbell M.; Tlustos L.; Wong W. | Timepix, a 65k programmable pixel readout chip for arrival time, energy and/or photon counting measurements | 2007 | Nucl. Inst. and Meth. A | 581 | 1-2 SPEC. ISS. | 485 | 2-s2.0-35348817342
674 | Llopart X.; Campbell M.; Dinapoli R.; San Segundo D.; Pernigotti E. | Medipix2: A 64-k pixel readout chip with 55-μm square elements working in single photon counting mode | 2002 | IEEE Transactions on Nuclear Science | 49 I | 5 | 2279 | 2-s2.0-0036815755
463 | Poikela T.; Plosila J.; Westerlund T.; Campbell M.; Gaspari M.D.; Llopart X.; Gromov V.; Kluit R.; Beuzekom M.V.; Zappon F.; Zivkovic V.; Brezina C.; Desch K.; Fu Y.; Kruth A. | Timepix3: A 65K channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout | 2014 | Journal of Instrumentation | 9 | 5 | C05013 | 2-s2.0-84903648134
254 | Ballabriga R.; Campbell M.; Heijne E.H.M.; Llopart X.; Tlustos L. | The Medipix3 prototype, a pixel readout chip working in single photon counting mode with improved spectrometric performance | 2007 | IEEE Transactions on Nuclear Science | 54 | 5 | 1824 | 2-s2.0-35348948593
248 | Jakubek J. | Precise energy calibration of pixel detector working in time-over-threshold mode | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S262 | 2-s2.0-79959818317
215 | McMullan G.; Chen S.; Henderson R.; Faruqi A.R. | Detective quantum efficiency of electron area detectors in electron microscopy | 2009 | Ultramicroscopy | 109 | 9 | 1126 | 2-s2.0-67650544797
200 | Ponchut C.; Rigal J.M.; Clément J.; Papillon E.; Homs A.; Petitdemange S. | MAXIPIX, a fast readout photon-counting X-ray area detector for synchrotron applications | 2011 | Journal of Instrumentation | 6 | 1 | C01069 | 2-s2.0-79952662448
199 | Ballabriga R.; Campbell M.; Heijne E.; Llopart X.; Tlustos L.; Wong W. | Medipix3: A 64 k pixel detector readout chip working in single photon counting mode with improved spectrometric performance | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S15 | 2-s2.0-79959823582
182 | Turecek D.; Holy T.; Jakubek J.; Pospisil S.; Vykydal Z. | Pixelman: A multi-platform data acquisition and processing software package for Medipix2, Timepix and Medipix3 detectors | 2011 | Journal of Instrumentation | 6 | 1 | C01046 | 2-s2.0-79952653981
169 | Holy T.; Jakubek J.; Pospisil S.; Uher J.; Vavrik D.; Vykydal Z. | Data acquisition and processing software package for Medipix2 | 2006 | Nucl. Inst. and Meth. A | 563 | 1 | 254 | 2-s2.0-33745003477
Extracted from Scopus: 12th Aug 2025
Top 10 publications mentioning ‘Medipix’ OR ‘Timepix’ in Abstract, Title, Keywords by number of citations

## Slide 9: Top 10 publications mentioning ‘Medipix’ OR ‘Timepix’ in Abstract, Title, Keywords by number of citations
Citations | Authors | Title | Year | Source title | Volume | Issue | Page | EID
912 | Llopart X.; Ballabriga R.; Campbell M.; Tlustos L.; Wong W. | Timepix, a 65k programmable pixel readout chip for arrival time, energy and/or photon counting measurements | 2007 | Nucl. Inst. and Meth. A | 581 | 1-2 SPEC. ISS. | 485 | 2-s2.0-35348817342
674 | Llopart X.; Campbell M.; Dinapoli R.; San Segundo D.; Pernigotti E. | Medipix2: A 64-k pixel readout chip with 55-μm square elements working in single photon counting mode | 2002 | IEEE Transactions on Nuclear Science | 49 I | 5 | 2279 | 2-s2.0-0036815755
463 | Poikela T.; Plosila J.; Westerlund T.; Campbell M.; Gaspari M.D.; Llopart X.; Gromov V.; Kluit R.; Beuzekom M.V.; Zappon F.; Zivkovic V.; Brezina C.; Desch K.; Fu Y.; Kruth A. | Timepix3: A 65K channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout | 2014 | Journal of Instrumentation | 9 | 5 | C05013 | 2-s2.0-84903648134
254 | Ballabriga R.; Campbell M.; Heijne E.H.M.; Llopart X.; Tlustos L. | The Medipix3 prototype, a pixel readout chip working in single photon counting mode with improved spectrometric performance | 2007 | IEEE Transactions on Nuclear Science | 54 | 5 | 1824 | 2-s2.0-35348948593
248 | Jakubek J. | Precise energy calibration of pixel detector working in time-over-threshold mode | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S262 | 2-s2.0-79959818317
215 | McMullan G.; Chen S.; Henderson R.; Faruqi A.R. | Detective quantum efficiency of electron area detectors in electron microscopy | 2009 | Ultramicroscopy | 109 | 9 | 1126 | 2-s2.0-67650544797
200 | Ponchut C.; Rigal J.M.; Clément J.; Papillon E.; Homs A.; Petitdemange S. | MAXIPIX, a fast readout photon-counting X-ray area detector for synchrotron applications | 2011 | Journal of Instrumentation | 6 | 1 | C01069 | 2-s2.0-79952662448
199 | Ballabriga R.; Campbell M.; Heijne E.; Llopart X.; Tlustos L.; Wong W. | Medipix3: A 64 k pixel detector readout chip working in single photon counting mode with improved spectrometric performance | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S15 | 2-s2.0-79959823582
182 | Turecek D.; Holy T.; Jakubek J.; Pospisil S.; Vykydal Z. | Pixelman: A multi-platform data acquisition and processing software package for Medipix2, Timepix and Medipix3 detectors | 2011 | Journal of Instrumentation | 6 | 1 | C01046 | 2-s2.0-79952653981
169 | Holy T.; Jakubek J.; Pospisil S.; Uher J.; Vavrik D.; Vykydal Z. | Data acquisition and processing software package for Medipix2 | 2006 | Nucl. Inst. and Meth. A | 563 | 1 | 254 | 2-s2.0-33745003477
Extracted from Scopus: 12th Aug 2025

## Slide 10
Citations | Authors | Title | Year | Source title | Volume | Issue | Page | EID
912 | Llopart X.; Ballabriga R.; Campbell M.; Tlustos L.; Wong W. | Timepix, a 65k programmable pixel readout chip for arrival time, energy and/or photon counting measurements | 2007 | Nucl. Inst. and Meth. A | 581 | 1-2 SPEC. ISS. | 485 | 2-s2.0-35348817342
674 | Llopart X.; Campbell M.; Dinapoli R.; San Segundo D.; Pernigotti E. | Medipix2: A 64-k pixel readout chip with 55-μm square elements working in single photon counting mode | 2002 | IEEE Transactions on Nuclear Science | 49 I | 5 | 2279 | 2-s2.0-0036815755
463 | Poikela T.; Plosila J.; Westerlund T.; Campbell M.; Gaspari M.D.; Llopart X.; Gromov V.; Kluit R.; Beuzekom M.V.; Zappon F.; Zivkovic V.; Brezina C.; Desch K.; Fu Y.; Kruth A. | Timepix3: A 65K channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout | 2014 | Journal of Instrumentation | 9 | 5 | C05013 | 2-s2.0-84903648134
254 | Ballabriga R.; Campbell M.; Heijne E.H.M.; Llopart X.; Tlustos L. | The Medipix3 prototype, a pixel readout chip working in single photon counting mode with improved spectrometric performance | 2007 | IEEE Transactions on Nuclear Science | 54 | 5 | 1824 | 2-s2.0-35348948593
248 | Jakubek J. | Precise energy calibration of pixel detector working in time-over-threshold mode | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S262 | 2-s2.0-79959818317
215 | McMullan G.; Chen S.; Henderson R.; Faruqi A.R. | Detective quantum efficiency of electron area detectors in electron microscopy | 2009 | Ultramicroscopy | 109 | 9 | 1126 | 2-s2.0-67650544797
200 | Ponchut C.; Rigal J.M.; Clément J.; Papillon E.; Homs A.; Petitdemange S. | MAXIPIX, a fast readout photon-counting X-ray area detector for synchrotron applications | 2011 | Journal of Instrumentation | 6 | 1 | C01069 | 2-s2.0-79952662448
199 | Ballabriga R.; Campbell M.; Heijne E.; Llopart X.; Tlustos L.; Wong W. | Medipix3: A 64 k pixel detector readout chip working in single photon counting mode with improved spectrometric performance | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S15 | 2-s2.0-79959823582
182 | Turecek D.; Holy T.; Jakubek J.; Pospisil S.; Vykydal Z. | Pixelman: A multi-platform data acquisition and processing software package for Medipix2, Timepix and Medipix3 detectors | 2011 | Journal of Instrumentation | 6 | 1 | C01046 | 2-s2.0-79952653981
169 | Holy T.; Jakubek J.; Pospisil S.; Uher J.; Vavrik D.; Vykydal Z. | Data acquisition and processing software package for Medipix2 | 2006 | Nucl. Inst. and Meth. A | 563 | 1 | 254 | 2-s2.0-33745003477
Extracted from Scopus: 12th Aug 2025
Top 10 publications mentioning ‘Medipix’ OR ‘Timepix’ in Abstract, Title, Keywords by number of citations

## Slide 11
Citations | Authors | Title | Year | Source title | Volume | Issue | Page | EID
912 | Llopart X.; Ballabriga R.; Campbell M.; Tlustos L.; Wong W. | Timepix, a 65k programmable pixel readout chip for arrival time, energy and/or photon counting measurements | 2007 | Nucl. Inst. and Meth. A | 581 | 1-2 SPEC. ISS. | 485 | 2-s2.0-35348817342
674 | Llopart X.; Campbell M.; Dinapoli R.; San Segundo D.; Pernigotti E. | Medipix2: A 64-k pixel readout chip with 55-μm square elements working in single photon counting mode | 2002 | IEEE Transactions on Nuclear Science | 49 I | 5 | 2279 | 2-s2.0-0036815755
463 | Poikela T.; Plosila J.; Westerlund T.; Campbell M.; Gaspari M.D.; Llopart X.; Gromov V.; Kluit R.; Beuzekom M.V.; Zappon F.; Zivkovic V.; Brezina C.; Desch K.; Fu Y.; Kruth A. | Timepix3: A 65K channel hybrid pixel readout chip with simultaneous ToA/ToT and sparse readout | 2014 | Journal of Instrumentation | 9 | 5 | C05013 | 2-s2.0-84903648134
254 | Ballabriga R.; Campbell M.; Heijne E.H.M.; Llopart X.; Tlustos L. | The Medipix3 prototype, a pixel readout chip working in single photon counting mode with improved spectrometric performance | 2007 | IEEE Transactions on Nuclear Science | 54 | 5 | 1824 | 2-s2.0-35348948593
248 | Jakubek J. | Precise energy calibration of pixel detector working in time-over-threshold mode | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S262 | 2-s2.0-79959818317
215 | McMullan G.; Chen S.; Henderson R.; Faruqi A.R. | Detective quantum efficiency of electron area detectors in electron microscopy | 2009 | Ultramicroscopy | 109 | 9 | 1126 | 2-s2.0-67650544797
200 | Ponchut C.; Rigal J.M.; Clément J.; Papillon E.; Homs A.; Petitdemange S. | MAXIPIX, a fast readout photon-counting X-ray area detector for synchrotron applications | 2011 | Journal of Instrumentation | 6 | 1 | C01069 | 2-s2.0-79952662448
199 | Ballabriga R.; Campbell M.; Heijne E.; Llopart X.; Tlustos L.; Wong W. | Medipix3: A 64 k pixel detector readout chip working in single photon counting mode with improved spectrometric performance | 2011 | Nucl. Inst. and Meth. A | 633 | SUPPL. 1 | S15 | 2-s2.0-79959823582
182 | Turecek D.; Holy T.; Jakubek J.; Pospisil S.; Vykydal Z. | Pixelman: A multi-platform data acquisition and processing software package for Medipix2, Timepix and Medipix3 detectors | 2011 | Journal of Instrumentation | 6 | 1 | C01046 | 2-s2.0-79952653981
169 | Holy T.; Jakubek J.; Pospisil S.; Uher J.; Vavrik D.; Vykydal Z. | Data acquisition and processing software package for Medipix2 | 2006 | Nucl. Inst. and Meth. A | 563 | 1 | 254 | 2-s2.0-33745003477
Extracted from Scopus: 12th Aug 2025
Top 10 publications mentioning ‘Medipix’ OR ‘Timepix’ in Abstract, Title, Keywords by number of citations

## Slide 12: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 13: Medipix3 at LNLS Brazil
PIMEGA 540D
Medipix3-based
144 ASICs
300µm Silicon Sensors,
9.4 megapixels (3072 × 3072 pixels)
vacuum compatible
2000 frames per second.
Slide courtesy of J-M Polli

## Slide 14: Medipix3 at LNLS Brazil
PIMEGA 450D
Medipix3-based
120 ASICs
675µm Silicon Sensors
7.9 megapixels (256 x 30720 pixels)
A 1.7 m long arc
1000 Frames Per Second.
Slide courtesy of J-M Polli

## Slide 15: Timepix3 at Diamond Light Source
Tristan
Timepix3-based
160 ASICs
300µm Silicon Sensors
10 megapixels (4096 x 4096 pixels)
Streamed data
25ns timestamp per hit
Slide courtesy of D. Omar

## Slide 16: Timepix3 at Diamond Light Source
time
Laser shot
(time zero)
Formation of crystals
Tristan image of diffraction from laser induced nucleation.
Histogram of events after single laser shot (red line) with 100 ms binning.
Diffraction peaks present within first time-bin after single laser exposure
Slide courtesy of D. Omar

## Slide 17: Timepix4 at DESY
TEMPUS single-chip prototype developed by DESY
  Main detector in various user experiments
  Check the usability of the high-speed serialisers
  Explore the event-driven mode
Scientific experiments made so far:
  Nuclear Resonance Scattering (NRS)
  Parametric Down Conversion for Ghost Imaging
  X-ray Photo Correlation Spectroscopy (XPCS)
Slide courtesy of J Correa

## Slide 18
X-ray Photo Correlation Spectroscopy and X-ray Cross-Correlation Analysis – sub μs correlation functions
Campaigns at ESRF – ID10, APS - 8ID and Eu.XFEL - MID
In a recent experiment we demonstrated that using
TEMPUS we could reach correlations:
    Down to 250 ns for the speckles smaller than a pixel
    Down to 20 ns for speckles larger than a single pixel
Timepix4 at DESY
Slide courtesy of J Correa

## Slide 19: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 20
Gamma ray detection at CEA-LIST
More than 30 years of expertise at in the field of ionizing radiation imaging, leading to Nanopix Family, the most compact coded aperture gamma cameras in the world!
A combination of
Medipix collaboration ASICs,
miniaturised electronics,
specific spatially-coded aperture collimators
and embedded algorithms
allowing to remotely visualize radioactivity
Developments in close collaboration with :
Nanopix2 (2019)
Timepix inside
Nanopix (2015)
Timepix inside
Nanopix3 (2025)
Timepix3 inside
Slide courtesy of V. Schoepff

## Slide 21
Operational radiation protection
Dismantling & decommissioning
Nuclear Waste Management
Post-accidental situations
Homeland Security
Marie Curie’s lab, France
Gamma ray detection at CEA-LIST
Slide courtesy of V. Schoepff

## Slide 22: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 23
What if incoming particles deposit charge which is too low to be detected in a pixel?
Advantage of direct pixel ASIC readout – MCP gain can be substantially reduced and therefore its lifetime is in significantly increased
Slide courtesy of A. Tremsin

## Slide 24: 4Dphoton: Integrate Timepix4 in a photo tube
Concept already proven with 4 Timepix chips
See: J Vallerga et al. https://iopscience.iop.org/article/10.1088/1748-0221/9/05/C05055
Ongoing effort with Timepix4 started
See: M. Fiorini et al. https://iopscience.iop.org/article/10.1088/1748-0221/13/12/C12005/pdf
Slide courtesy of M. Fiorini

## Slide 25: 4Dphoton: Integrate Timepix4 in a photo tube
Custom design and Pin Grid Array (PGA) by INFN, and produced by Kyocera
CERAMIC CARRIERS
MCP-PMT prototypes
Prototype vacuum tube produced by Hamamatsu Photonics Japan (HPK)
  First prototypes received in 2024
Main characteristics:
  Multi-alkali S20 photocathode
    peak QE > 30% at 380 nm
  6 μm MCP channel diameter (7.5 μm pitch)
Several variants for complete characterization
  2-MCP stack and 3-MCP stack
  1d - 2d - 3d end-spoiling
Dry air
Laser 405 nm
HV

## Slide 26: 4Dphoton: Integrate Timepix4 in a photo tube
Characterization Measurements
Dark Count Rate (DCR) and gain measurements performed on dark noise acquisitions
Timing resolution measurements:
  single pixel resolution reaching a plateau at 95 ps
  cluster resolution improving up to 65 ps
MCP_in-MCP_out = 2400 V
1 minute shutter
E[Q] = 236.0 ke-
Test beam campaign
Tracking system: 2 Timepix4 assemblies bonded to 300 μm thick p-on-n planar Si sensors
RICH setup: Cherenkov radiator and optics setup
Timing system: 2 Cherenkov detectors
PicoTDC to precisely measure the timing of the detectors
Slide courtesy of M. Fiorini

## Slide 27: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 28
How about neutrons?
No need for photo-cathode
Dope MCP with a neutron absorbed (10B or natGd)
Integrate MCP and ASIC in beam vacuum

## Slide 29
Neutron detector development at UC Berkeley
Early versions were Timepix-based
Timepix3-based systems now deployed
Timepix4-based systems in preparation
This example shows how a neutron beam can be used to help optimise crystal growth: (b) Eu concentration (c) and (d) Li concentration
Neutron energies used: 1meV to 10keV in one experiment
Slide courtesy of A. Tremsin

## Slide 30
Scintillator Neutron Detector + Event Driven Timepix Camera:
6LiF/ZnS and (Gd2O2S (Tb/6LiF)) for thermal neutron detection
Scintillation light coupled to a image intensifier for amplifiying
Timepix Camera for TOA registering of photon events
Advantages: Adjustable FOV (with different spatial resolution), no vaccum operation
CSNS BL13
ERNI Neutron Detector
ASI TPX3Cam
CSNS Timepix4 Camera
Neutron detector development at CSNS (China)
Slide courtesy of H. Lui

## Slide 31
~ 28um spatial resolution (GOS)
Metal shell lighter
(ZnS)
Metal Watch
(ZnS)
Neutron transmission imaging with Timepix4 Camera
Neutron detector development at CSNS (China)

## Slide 32: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 33
Time of Flight Mass Spectrometry at Maastricht
Slide courtesy of R. Heeren

## Slide 34
Time of Flight Mass Spectrometry at Maastricht
Imaging time 33.3 mins compared with 2 months…
Slide courtesy of R. Heeren

## Slide 35
Mass images of rat brain using Timepix3cam
Each area (a) to ( e) highlights different (m/z) regions and therefore different molecules
(f) and (g) indicate zooms with pixel sizes of 2mm and 0.5 mm respectively
Full image size 1.3 Gpixels
18 mm
16.5 mm
Time of Flight Mass Spectrometry at Maastricht
Slide courtesy of R. Heeren

## Slide 36: Outline
Collaboration publications
Other synchrotron science applications
  Medipix3 at the Brazilian light source
  Timepix3 at Diamond
  Timepix4 at DESY
Detection of gamma rays at CEA Saclay
Visible light imaging
  4Dphoton (INFN Ferrara)
Neutron detection and imaging
  Timepix devices developed by UC Berkeley
  On-going developments at the China Spallation Neutron Source
Time of Flight Mass Spectrometry (Maastricht/Nikhef)
Future High Energy Physics experiments
  Gridpix for large area TPC readout (Bonn/Nikhef)
  Possible applications in IEC (Glasgow)
Some personal observations

## Slide 37
50 µm
Micromegas on a pixelated readout ASIC
Gas amplification increases signal of single electron to detection level
=> high efficiency to see all primary electron
→ improve spatial and energy resolution.
55Fe decay: 5.9 keV photon
→ ~225 electrons
  Gridpix for large area TPC readout (Bonn/Nikhef)
Slide courtesy of J Kaminski

## Slide 38
Development with Timepix
TPC with 160 GridPixes
Development with Timepix3
TPC with 32 GridPixes
high precision measurements
Demonstrated
- feasibility of large
number of GridPixes
- excellent spatial
resolution (systematics
below 10 µm)
- excellent energy
resolution for 1 m long
tracks; dE/dx ~ 3%
  Gridpix for large area TPC readout (Bonn/Nikhef)
Slide courtesy of J Kaminski

## Slide 39
Timepix4 Tracker for the ePIC detector at the EIC
Timepix4
Front End Board
2xStations to measure scattered electrons of different momenta, each with 4 layers of Timepix4
EIC at BNL, USA
“A machine that will unlock the
secrets of the strongest force in
Nature”.
Construction: 2026
Data taking early 2030’s
UoG building Low-Q2 Taggers.
Only Timepix4 can operate at the required data density rates
Slide courtesy of D. Manueski

## Slide 40
The Low-Q2 Tagger will detect scattered electrons from collisions at the ePIC detector interaction point, tagging the virtual photon momentum.
Challenging high energy physics detector. (Design still being finalized)
Large area detector (For Timepix)
  Total 144 Timepix4 chips (Dependent on beampipe design)
  2 Stations, each 4 Layers of 3x6 Timepix4
  About 1000cm2 of Timepix4.
  TSV technology required
High, nonuniform data rates
  10+ tracks every 10 ns bunch crossing
  Up to maximum 20kHz per pixel
  Synchrotron and other beam backgrounds
  Total estimation 600 Gb/s
  Require front end data filtering by FPGA
Close to electron beam
  As close as possible to beam to maximize acceptance
  Not too close to introduce beam impedance
Reconstruction through magnets
  Dipole and quadrupoles before detectors.
  Machine learning to reconstruct initial momentum from track.
Extends physics range of central detector
Rate Distribution of Bremsstrahlung and DIS scattered electrons
Timepix4 Tracker for the ePIC detector at the EIC
Slide courtesy of D. Manueski

## Slide 41
Some personal observations
Philippe Starck
Juicy Salif citrus squeezer
Finnish Design Shop
Some compare High Energy Physics with a famous Italian design:
Beautiful
Expensive
But almost completely useless
With the Medipix Collaborations we have demonstrated that the pursuit of advanced detector readout concepts can impact many other areas of science
But some elements are required:
Individual and collective imagination/vision
A willingness to pool ideas and resources
Openness to the requirements of others
Highly skilled engineers
Access to leading edge processes
Organisation, tenacity, patience
Fair and workable licensing

## Slide 42: And, finally..
Thanks to all of you (and also those not present) for the continuing, friendly and enthusiastic collaboration over the last years. Our team was boosted morally by each collaboration meeting
Thanks to all those at CERN (esp. in EP and KT) who supported our team and kept us going in spite of sometimes challenging circumstances
Thanks also to our industrial partners who took a leap of faith to make our developments available to a wider community. You have been responsible for bringing our developments to the wider world

## Slide 43: Mouse skull
Medipix3RX images: S. Procz et al.
Medipix3
X-ray tube 25kVp
8 x 6 tiles
500mm GaAs
Bias: -200 V
SPM 24-Bit
TH0 6 keV

## Slide 44: SD Card
Medipix3RX images: S. Procz et al.
CF card
Medipix3
Width: 42.8 mm
Mag. 1.74x
CdTe 1mm
Bias: -290 V
SPM 24-Bit
8x7 tiles

## Slide 45
Thank you for your attention!
Medipix3RX images: S. Procz et al.

## Slide 46
Bibliography
https://www.nature.com/commsmat
Ptychographic X-ray computed tomography of porous membranes with nanoscale resolution
Górecki, R., Polo, C.C., Kalile, T.A. et al. Ptychographic X-ray computed tomography of porous membranes with nanoscale resolution. Commun Mater 4, 68 (2023).
https://doi.org/10.1038/s43246-023-00396-x
https://doi.org/10.1021/acs.nanolett.4c03662
DOI: 10.1103/PhysRevB.111.144103

## Slide 47
[1] A. G. Jarvis, H. A. Sparkes, S. E. Tallentire, L. E. Hatcher, M. R. Warren, P. R. Raithby, D. R. Allan, A. C. Whitwood, M. C. R. Cockett, S. B. Duckett, J. L. Clark, I. J. S. Fairlamb, CrystEngComm 2012, 14, 5564-5571.
[2] Coppens et al., Chem Commun., 2004, 2144.
[3] M. R..Warren et al., Angew. Chem., 2009, 121, 5821-5824
[1] Cormary et al., Inorg. Chem., 2012, 51, 7492-7501.
[2] Schaniel et al., Adv. Mat., 2007, 19, 723-726.
Tristan –a 10 Million Pixel Large Area Time Resolved Detector for Synchrotron use.
David Omar, Giulio Crevatin, Alan Greer, Ian Horswell, Jonathan Spiers, Richard Placket, Paul Booker, Gale Lockwood, Dan Beckett, Emily Galvin, John Lipp, Michelangelo Di Palo, Mark Warren, Scott Williams, and Nicola Tartoni1 DOI 10.1109/TNS.2022.3204064
J. Correa et al. (2024). J. Synchrotron Rad. 31. https://doi.org/10.1107/S1600577524005319
Y. Chushkin et al. (2025). J. Synchrotron Rad. 32 https://doi.org/10.1107/S1600577525006599
A.S. Tremsin, J.V. Vallerga, "Unique capabilities and applications of Microchannel Plates detectors with Medipix/Timepix readout", Radiation Measurements 130 (2020) 106228.
https://doi.org/10.1016/j.radmeas.2019.106228
A.S. Tremsin, Y. Gao, A. Makinde, H.Z. Bilheux, J.C. Bilheux, K. An, T. Shinohara, K. Oikawa, "Monitoring residual strain relaxation and preferred grain orientation of additively manufactured Inconel 625 by in-situ neutron imaging", Additive Manufacturing 46(2021) 102130.
https://doi.org/10.1016/j.addma.2021.102130
Bibliography

## Slide 48
https://doi.org/10.1021/acs.analchem.2c02870
Anal. Chem. 2022, 94, 14652−14658
NÌM A535 (2004) 506-510
NIM A845 (2017) 233-235
TNS, 64, 5, 2017, pp 1159
NIM A 1075 (2025) 170397
NIM A 1081 (2026) 170840
Bibliography

## Slide 49
Backup

## Slide 50: All publications - Author names

## Slide 51: All publications - Affiliations

## Slide 52: All publications - Subject areas