## Slide 1: Mini Lecture Course: Accelerator Design for a Multi-TeV Muon Collider Lecture 3: Characterize Solenoid-based cooling channels
Katsuya Yonehara
Senior Scientist
June 9, 2025

## Slide 2: Scope of today’s lecture
Review previous lectures
Explore solenoid-based cooling channel using simplified toy models
  Single Solenoid Coil
  Multiple Solenoid Coils
  Multiple Solenoid Coils and alternating polarity configuration
Review key theoretical analysis of FOFO channels
  K.J. Kim and C.Wang, PRL85, 760 (2000)
  G. Penn and J. Wurtele, PRL85, 764 (2000)
  G. Dugan, PRAB4, 104001 (2001)
Introduction to specific solenoid-based cooling channel designs
  Rectilinear channel (Stratakis et al.)
  Helical channel using (Derbenev et al.)
  HFOFO channel (no formal theoretical paper published)

## Slide 3: Quick Review of Previous Lecture (I)
Beam dynamics is analogous to the dynamics of a simple harmonic motion
  Solving harmonic oscillator via canonical transformation
Harmonic motion  Hill’s equation (translate the differentiation from to )
Or
Comparing
Translation from harmonic oscillation to beam dynamics
Mechanical harmonic oscillation framework

## Slide 4: Quick Review of Previous Lecture (II)
Introduce new canonical momentum
The beam (gaussian) distribution function is a function of the Courant-Snyder invariant; The -matrix is given
is called the Courant-Snyder invariant, or emittance
=
=
=
Twiss parameters from phase space

## Slide 5: Quick Review of Previous Lecture (III)
Solution of Hill’s equation
is a periodic solution  Beam motion is stable
Thin lens and paraxial approximation
Or , where
Parallel beam
focused beam
Definition of focusing length

## Slide 6: Quick Review of Previous Lecture (IV)
Thin lens and paraxial approximation
Stability condition,
Demonstrate FODO cell in G4Beamline
Example:
Phase advance per cell degrees
Focusing length m
m

## Slide 7: Demo: FODO cell (70 deg)
x (mm)
z (mm)
x’ (rad)
x (mm)
Solid black points in x-x’ plot is taken with one FOCO-cell period
Five black points are visible per full revolution, corresponding to ~70 degrees phase advance  360/70 ~ 5.14 cells/rev
Observed x ~ 61.6 mm at x’~ 0.0338 rad
~ 0.00156 m rad
fodocell_phase60_05160030.nb
1
2
3
4
5
6

## Slide 8: Demo: FODO cell (Unstable condition)
If the FODO lattice set with the beam optics must be unstable
With the drift gap increased to 5710 mm, the FODO cell exceeds the stability condition
Since has no real solution, the optics become unstable
fodocell_unstable_05160040.nb

## Slide 9: Demo: Single Solenoid Coil
Coil length L
Coil inner radius a
Coil thickness t
Fernow coil (referred from PRSTAB 10, 064001 (2007)
Coil length = 400 mm
Coil inner radius = 400 mm
Coil thickness = 100 mm
Current = 100 Amp/mm2
fofocell_fernow_focus_05220060.nb

## Slide 10: Demo: Single Solenoid Coil
Conventional Solenoid Focusing Model
As the formula shows, the focusing length is independent from the coil geometry
 Thin lens approximation
The estimated focusing length
Solenoid center (z = 500 mm)
profile on coil axis z
(Tesla)
m
Coil length = 400 mm
Coil inner radius = 400 mm
Coil thickness = 100 mm
Current = 100 Amp/mm2
Observed peak magnetic field = 5.1 Tesla
300 mm@ 200 MeV/c
NB:
fofocell_fernow_focus_05220060.nb
NB: Solenoid field calculation may depend on the simulator; We use G4Beamline which may differ from ICOOL

## Slide 11: Demo: Single Solenoid Coil
Solenoid center (z = 500 mm)
Solenoid center (z = 500 mm)
NB:
Beam is rotated in the coil (Larmor motion)
Focusing strength seems too strong to focus particle
Focusing length should be longer than coil length ()
fofocell_fernow_focus_05220060.nb

## Slide 12: Demo: Single Solenoid Coil
Coil length = 200 mm
Coil inner radius = 400 mm
Coil thickness = 100 mm
Current = 100 Amp/mm2
Observed peak magnetic field = 2.7 Tesla
550 mm
Solenoid center (z = 500 mm)
Observed focusing length is ~500 mm
Coil length = 100 mm
Coil inner radius = 400 mm
Coil thickness = 100 mm
Current = 100 Amp/mm2
Observed peak magnetic field = 1.4 Tesla
1076 mm
Solenoid center (z = 500 mm)
Observed focusing length is ~1800 mm
Focusing length agrees well with prediction
Prediction is underestimated
fofocell_fernow_focus_05220070.nb

## Slide 13: Induced Angular Momentum
Set the Larmor rotation frame
The linearized equations of motion is given
Twiss parameters
Introduce the normalized canonical angular momentum
is a Larmor angular velocity

## Slide 14: Induced Angular Momentum
The transverse covariance matrix includes angular momentum
Or, taking 4x4 matrix to estimate emittance

## Slide 15: FOFO Channel
Fernow’s coil (referred from PRSTAB 10, 064001 (2007))
and (b)
Non-flipping solenoid coil
Difference between (a) and (b) is an initial beam condition whether beam starts from coil center or in the coil gap
Coil
RF
Absorber
(c) and (d)
Flipping solenoid coil

## Slide 16: Demo: FOFO Channel
Fernow’s coil (referred from PRSTAB 10, 064001 (2007)
Coil length = 400 mm
Coil inner radius = 400 mm
Coil thickness = 100 mm
Current = 100 Amp/mm2
Period = 1000 mm
and (b)
Non-flipping solenoid coil
fofostudy_fernow_fig1a_05280140.nb

## Slide 17: Demo: FOFO Channel
fofostudy_fernow_fig1a_05280140.nb
x’ (rad)
x (mm)
x’ (rad)
x (mm)
Filamentation due to mismatching
Red: Initial phase space
Red: Initial phase space

## Slide 18: Demo: FOFO Channel
fofostudy_fernow_fig1b_05280150.nb
x’ (rad)
x (mm)
x’ (rad)
x (mm)
Red: Initial phase space
Red: Initial phase space

## Slide 19: Beta function and passband (stability condition)
Stability condition for solenoid-based channel is quite different from FODO channel because the FOFO solenoid magnet does not follow the thin lens approximation
Instead, the stability condition can be predicted from Mathieu equation
Thin solenoid coil
Thick solenoid coil
Matheu equation can be solved numerically
0.73 m
0.13 m
Our simulation
(agreed very well)
NB: Table shows passband in different coil configurations from us (e.g.

## Slide 20: Demo: FOFO Channel
Fernow’s coil (referred from PRSTAB 10, 064001 (2007)
Coil length = 400 mm
Coil inner radius = 400 mm
Coil thickness = 100 mm
Current = 100 Amp/mm2
Period = 1000 mm
(c) and (d)
Flipping solenoid coil
fofostudy_fernow_fig1a_05280140.nb

## Slide 21: Demo: FOFO Channel
fofostudy_fernow_fig1c_05290160.nb
x’ (rad)
x (mm)
x’ (rad)
x (mm)
Red: Initial phase space
Red: Initial phase space

## Slide 22: Demo: FOFO Channel
fofostudy_fernow_fig1d_05280170.nb
x’ (rad)
x (mm)
x’ (rad)
x (mm)
Red: Initial phase space
Red: Initial phase space

## Slide 23: FOFO Bandpass
Stop band
Transmission efficiency
It seems that the stop band momentum range is different from Fernow’s paper; This may be because g4beamline uses different field calculation formula from ICOOL (?)
(GeV/c)

## Slide 24: Rectilinear Channel
Stratakis demonstrated the advanced FOFO channel
So called Rectilinear channel
Solenoid coil is tilted in vertical direction to induce dispersion
Solenoid coil
(coil is slightly tilted in vertical direction)
RF cavities
Absorber
Top view
Side view

## Slide 25: Rectilinear Channel
Initial cooling channel use region
 Benefit a large momentum acceptance

## Slide 26: Rectilinear Channel
Later cooling channel use region
 is flat in  Good for advanced cooling

## Slide 27: Helical Cooling Channel
Use continuous combined magnet (straight solenoid + helical dipole & quadrupole magnets)
 No stop band due to a periodic focusing channel
Equations of motion on the reference frame
Rotation of reference particle (red line), which is based on cyclotron motion

## Slide 28: Helical Cooling Channel
Challenge of designing helical cooling channel is following
Helical magnet is complicated
RF cavities must be inserted into a helical magnet
If helical channel is used, the matching has to flip sign of the momentum compaction factor from positive to negative

## Slide 29: Helical FOFO
His concept starts from a periodic orbit with near pi resonance
where is a periodic orbit, is a tune, then
Yuri claims that FOFO has an issue to produce low and high (which is ideal for ionization cooling) because
: circumference of RFOFO, or the length of one cell period of rectilinear channel

## Slide 30: HFOFO
This is good since can be extremely large when is integer
( is called a chromaticity)
Making integer channel means making phase advanced FOFO channel  Helical FOFO channel
Helical FOFO channel could have a large momentum acceptance by tuning higher order chromaticity
Helical orbit permits a large acceptance
Alternative solenoid eliminates angular momentum
Forming one period with multiple solenoid cells induces a weak focusing (6 solenoid coils induce one period)

## Slide 31: HFOFO
Initial HFOFO channel has 6 solenoid coils to induce one beta oscillation
Reference particle has a position offset from solenoid coil center
Absorber is located low and high region while RF cavities are located other regions
Tilted solenoid induces dispersion

## Slide 32: Feasibility of Cooling Channel
Channel requires strong magnetic fields
Channel requires high gradient RF fields
Channel should be compact, so that integration is challenging
Channel should be accessible and replaceable
Channel should have a large tolerance
Channel should be radiation hard
Channel requires high resolution beam instrumentation

## Slide 33: Summary
VCC Rectilinear Cooling Channel
HCC Helical Cooling Channel
HFOFO is not shown this plot but it has similar as Initial (x)
Final Cooling Channel expected to be High Field Solenoid Channel
Bunch merge transforms multi-bunched beam into single bunched beam
Y
Longitudinal Emittance (mm)
Bunch
Merge
For acceleration
to Higgs Factory
For acceleration to multi-TeV collider
Final
Cooling
post-merge 6D Cooling
For acceleration to NuMAX (325MHz injector acceptance 3mm,24mm)
Initial Cooling
Target
Phase
Rotator
Front End



pre-merge 6D Cooling (original design)
Exit Front End
(15mm,45mm)
Initial
(X)
Initial
(Y)
VCC &
Hybrid
HCC
Final
Specification Achieved (simulations)
M. Palmer, Muon Collider Workshop 2019 in CERN