## Slide 1: Availability, Efficiency and Integrated Luminosity: Rising to the challenge in the FCC-ee
Jack Heron, Hannah Dostmann, Lukas Felsberger, Daniel Wollmann, Jan Uythoven
5th May 2025

## Slide 2: Future Circular Collider (FCC) 91km
Large Hadron Collider (LHC)
27km

## Slide 3
2030
2044
2060
2070
2095+
Now
FCC-ee
91-365 GeV
FCC-hh
100 TeV
FCC Timeline
…………………….

## Slide 4: FCC-ee (electron-positrons)
45.6 GeV
150 ab-1
Energy
Integrated Luminosity
80 GeV
10 ab-1
120 GeV
5 ab-1
182.5 GeV
1.7 ab-1
Operation Years
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
W
Z

## Slide 5: Availability and Luminosity
Stable Beams
Operation
Down Time
FCC-ee:
365 days
−120 (extended shutdowns)
− 30 (annual commissioning)
− 20 (machine development)
− 10 (technical stops)
185 days for physics

## Slide 6: Breakdown into Systems and Subsystems
FCC-ee
Failure Rate
Repair Duration
Availability
Integrated Luminosity
1) Systems

## Slide 7: RF System
Acknowledgement: Olivier Brunner, Andy Butterworth, Franck Peauger, Ivan Karpov
Using AFT fault data 2015-2024
LHC:
  16 SRF cavities
FCCee:
aft.cern.ch
aft-stats.web.cern.ch

## Slide 8: AFT data for all systems across CERN complex

## Slide 9: For each System
Failure data of a similar representative system:
  Fault rate (MTBF)
  Repair time (MTTR)
Scaling factor
  Elaborated w/ equipment experts based on number of critical units, complexity, etc.
Redundancy:
  “Can continue without 1 in 10 of these components”
Location:
  Drive time from CERN to relevant AP
  Cool down time at the relevant AP
Mean time between failures (MTBF)
Mean time to repair (MTTR)
https://reliabilityanalyticstoolkit.appspot.com/active_redundancy_with_repair

## Slide 10: Two fault types:
Remote Repair Faults
  Repair achieved from the control room
  E.g. by resetting components
Human Repair Faults
  Requires human intervention
  Approach time 0.3-1.5 h
  Cool down time 0.7-24 h
https://www.istockphoto.com/vector/isometric-control-center-gm164401684-15526568
https://www.flaticon.com/free-icon/technician_6342684
Using (for example) AFT fault data 2015-2024

## Slide 11: Breakdown into Systems and Subsystems
FCC-ee
Failure Rate
Repair Duration
Availability
Integrated Luminosity
2) Accelerator Performance

## Slide 12: “Realistic” Repair Timeline:
Diagnosis + attempts to reset from control room
Approach time
Remote repairs
Human repairs
Humans in tunnel
We can’t fix it from here. Get someone out there!
Once human repairs start, they will finish.
1 h
Operation resumes if possible before humans are in the tunnel
20 min – 1.5 h
Repair
Operation
resumes here
Fault
Cool-Down time
45 min - 24 h

## Slide 13: FCC-ee Operation Cycle
Adjust
Set Up
10 min
10 min
Pilot bunch injection
10 min
Polarisation
1.5 h
Fill
Physics
20 h
Burn Off
Down for Repair
Dump
Default
Repair completed
Collider failure
Injector Complex failure
Stable Beams
Operation
Down
Time
  Z,WW
 | Z | WW | ZH | tt
Fill time (min) | 7.7 | 2.5 | 1.52 | 1.45
Lifetime (min) | 15 | 12 | 12 | 11
 | Z | WW | ZH | tt
 | 7.7 | 2.5 | 1.52 | 1.45
 | 15 | 12 | 12 | 11
  ,
Resonant depolarization is impossible

## Slide 14
Overall Performance
 | Z | WW | ZH | tt
Integrated luminosity target [ab-1] | 150 | 10 | 5 | 1.5
Delivered integrated luminosity is low in all energy modes
Due to low availability and low efficiency
Particularly bad in Z and W modes due to long turnaround

## Slide 15
Unavailability & Lost Luminosity
Injector Complex
Technical Infrastructure

## Slide 16
RF System
Failed RF cavities each week
Repairs needing human tunnel access
Operational Cost Factors:
High failure rate of cavities, esp. in tt (1352 cavities)
Requires a hard-working maintenance service
Redundancy eliminates down time completely
Collider
Booster
Z
W
H
tt
Z
W
H
tt
Redundancy

## Slide 17: Power Converters
Z
W
H
tt
Z
W
H
tt
Collider
Booster
Current optics configuration:
  Sextupoles powered in groups of four
  Correctors powered individually
How many power converters can we lose without dumping the beam?
  Needs a detailed study from optics and machine protection
Assumes the same degree of redundancy as exists currently in LHC

## Slide 18: Solution: Injection of Polarised Bunches
  Z,W
More than doubles delivered integrated luminosity
 | Z | W | H | tt
Integrated luminosity target [ab-1] | 205 | 19.2 | 10.8 | 3.12

## Slide 19
Reliability Targets

## Slide 20: Conclusions
R&D Opportunity:
  Injection of polarised bunches
Forecasted integrated luminosity is low in all energy modes
  Low availability and low efficiency
Systems of highest concern:
  RF
  Power Converters
  Injector Complex
  Technical Infrastructure
  Beam Losses

## Slide 21: Systematic Reliability/Availability Support
Success in FCCee requires machine-wide improvement in reliability
Pre-TDR phase:
  Coherent approach for all system designs:
    Requirements and milestones, performance benchmarking
    More nuanced reliability models in parallel with design process
    “Low-hanging fruit” – R&D opportunities evaluation
    Performance/Cost optimisation over the whole machine
TDR & Beyond:
    Tools, training, expertise
    Support for modular / hot-swappable design paradigm
    Diagnostics & Health Monitoring
    Fault prediction
    Fault tracking & Analytics
    Lifecycle Reliability

## Slide 22: Acknowledgements
Jacqueline Keintzel
Franck Peauger
Olivier Brunner
Andy Butterworth
Ivan Karpov
Serge Pittet
David Nisbet
Davide Aguglia
Ben Todd
Byamba Wicki
Jean-Paul Burnet
Klaus Hanke
Chris Roderick
Ioan Kozsar
Alessandro Masi
Damien Lafarge
Tomasz Ladzinski
Verena Kain
Frank Zimmerman
Markus Zerlauth
Jesper Nielsen
Mario Parodi
Charline Marcel
Manfred Wendt
Roderik Bruce
Anton Lechner
Marco Calviani
Antonio Perillo Marcone
Guillermo Peon
Inigo Martin Melero
Laurent Delpraz
Yann Dutheil
Christoph Wiesner
Jan Uythoven
Jeremie Bauche
Wolfgang Hofle
Roberto Kersevan
Gregory Pigny
Rudiger Schmidt
Arjan Verweij
Benoit Salvant
Bernhard Holzer
Bettina Mikulec
Cedric Hernalsteens
Rama Calaga
Roberto Losito
Katsunobu Oide
Hannes Bartosik
Paolo Craievich (PSI)
Masanori Sato (KEK)
William Corocho (SLAC)
Ralph Boespflug (DESY)
Rainer Wanzenberg (DESY)
Michaela Schaumann (DESY)
Cristian Maccarrone (ESRF)
Laurent Hardy (ESRF)
Antoine Chance (CEA)
Jorg Wenninger
Gijs de Rijk
Daniel Valuch
Belen Maria Salvachua Ferrando
Matteo Solfaroli Camillocci
Alice Vanel
Luke Von Freeden
Robert Kieffer
Igor Syratchev
Helga Timko
Rafaele Tegas
Giacomo Lavezzari
Manuel Colmenero Moratalla
Milosz Blaszkiewicz