## Slide 1: Anomaly Detection and Signal Denoising of TbT BPM data
Q. Bruant, Y. Nasr, L. Vitileia, J. Piscart, H. Le Corre,
A. Gomez, C. Ndungu-Ndegwa,
F. Bugiotti, B. Dalena
Thanks to: J. Keintzel, M. Gael, Y. Ohnishi

## Slide 2: Motivation and Context
1

## Slide 3: FCC and SuperKEKB
http://fcc-cdr.web.cern.ch/
CDRs publié dans European Physical Journal C (Vol 1) and ST (Vol 2-4)
International FCC project (CERN as host lab)
Continue to study experimental high energy particle physics
Accelerator options: FCC-hh, FCC-ee, FCC-he
Existing e+e- collider:
small size FCC-ee
proofs of principle of several design choices
https://doi.org/10.1093/ptep/pts083

## Slide 4: TbT BPMs data pipeline
Automatically detect faulty BPMs
Reduce noise on good BPMs
Features extraction
Features selection
Detection via DBSCAN

## Slide 5: Detecting faulty BPMs
2

## Slide 6: DBSCAN
Clustering algorithm
  hyperspace of features extracted from Multivariate Time Series (MTS)
One vs all approach
Distance-based approach
Feature 1
Feature 2
: first considered point in cluster
: point in cluster
: point in cluster with no new neighbour within ε
ε
: outlier out of ε range from other points
Main approach:
One given measurement, all BPM tracks, features selected for the measurement by library
  Outlier detection in given measurement

## Slide 7: Features and datasets
Features are extracted automatically via the Time2Feat library.
The unsupervised mode select the features based on a PCA decomposition with and without a given feature to tell if this feature is relevant.
For HER:
Dataset: HER_2024_02_06_IK_H_Vinjkick/ HER_2024_02_06_16_22_57.data
Features: standard deviation, median, autocorrelation, FFT components, location of max, …
Total number of features kept: 37/201
For LER:
Dataset: LER_2024_02_06_IK_H_Vinjkick/ LER_2024_02_06_17_02_14.data
Features: percentage of recurring values, FFT components, variance, etc…
Total number of features kept: 31/207

## Slide 8: Main Results
HER_2024_02_06_16_22_57.data
LER_2024_02_06_17_02_14.data
HER :
4/6 of expected faulty BPM are detected.
LER :
3/6 of expected faulty BPM are detected.
Faulty BPM HER (DBSCAN) | Expected faulty BPM HER | Faulty BPM LER (DBSCAN) | Expected faulty BPM LER
MQEAE35 | MQEAE35 |  | MQD3P23
MQD3E18 | MQD3E18 | MQEAP29 | MQEAP29
MQR2ORE | MQR2ORE |  | MQD3P8
 | MQEAE37 |  | MQEAP10
MQEAE33 |  | MQEAP35 | MQEAP35
MQD3E29 |  | MQW2ORP | MQW2ORP
 | MQD3E23 | MQEAP32 | 
MQEAE25 |  | MQEAP33 | 
MQEAE20 | MQEAE20 | MQEAP44 | 
 |  | MQD3P29 | 
 |  | MQI6P | 
 |  | MQEAP38 | 

## Slide 9: Faulty BPM plots

## Slide 10: Isolation Forest + SVD
1
2
3
4
5

## Slide 11: Signal Denoising & Feature Extraction

## Slide 12: Anomaly Detection with Isolation Forest

## Slide 13: Results
Ring | Expected Faulty BPMs | Correctly Detected
High Energy Ring (HER) | 6 | 5
Low Energy Ring (LER) | 6 | 4
  Detected 83% of expected faulty BPMs in HER and 67% in LER.
  Found additional BPMs showing strong anomalies, suggesting hidden faults.
  Next steps: investigate new candidates and refine detection thresholds.

## Slide 14: Denoising
3

## Slide 15: Evaluation Metrics
Peak Retention Ratio
Noise Reduction Ratio
SNR Improvement
Frequency Shift
How well the main peak is preserved
How much noise is removed
How much signal quality is improved
How much the main frequency changed

## Slide 16: Algorithms
Separates signal from noise by decomposing data into orthogonal components, and keeping the largest ones
SVD
Reduces dimensionality by identifying patterns of highest variance in the data
PCA
Uses a neural network to predict the true positions, without the random noise
LSTM

## Slide 17: What is an LSTM
  LSTMs work in the same way as RNNs, but each cell is more complex
    The key difference is that LSTMs maintain a “cell state” in addition to the hidden state, which allows it to keep longer-term information
    This allows it to avoid the vanishing gradient problem

## Slide 18: How denoising work
  Having a relatively deep model allows it to learn complex relationships in the data
  We add BatchNorm and Dropout for normalization
We combine these cells into 3 layers of 50 LSTM cells
  The model will learn the underlying patterns in the data
  We then use the model’s predictions as our estimate of the denoised signal
We train the model on a series of noisy positions

## Slide 19: Example BPM positions
File used: HER_2024_06_25_23_52_21.data

## Slide 20: Examples Frequences
File used: HER_2024_06_25_23_52_21.data

## Slide 21: Models Comparison
Metrics | SVD | PCA | LSTM
Peak Retention Ratio | 0.99 | 0.99 | 0,95
Noise Reduction Ratio | 0.45 | 0.4 | 0.57
SNR | 2.99 | 2.58 | 8,4
Frequency Shift | 0.0035 | 0.0035 | 0
Time to denoise | < 1 min | 1 min | ~ 1h

## Slide 22: Perspectives
Further understanding and improvements of the algorithms
Comparison with OMC FFT spectrum
Reconstruct the Optics functions with SOMA on denoised data
Characterize the algorithms on simulated BPMs signals
Look at other AI techniques

## Slide 23: TbT BPM data
BPM data (gen. sdds format)
Synchronization
SVD cleaning
BPM cuts
If high singular
intrinsic errors
Else
Harmonic analysis
Optics parameters reconstruction
ACCELERATOR
Position [mm]
Turn number
BPM data

## Slide 24: Examples
Normal BPM
Faulty BPM