## Slide 1: BDF Vacuum Vessel Feedthrough Connection
Gemma Humphreys, Jean-Louis Grenard, Christophe Mucher
23.05.2025

## Slide 2: Objectives of the brainstorming
Discuss requirements for feedthroughs and if they are enough defined
Discuss different possible solutions and assess if PRO/CONS are well identified
Discuss if other solutions can be envisaged

## Slide 3: BDF Vessel Baseline
Baseline Design
Helium vessel
Initial design had a small opening in the roof for all feedthroughs
Concept made use of the overhead crane for removal
All connections wanted outside of vessel
  Reduce leakage
  Any failure risks are in same location
But having feedthrough on top is not an option for TCC8 configuration (limited by available lifting height)
Crane ++ concept
~11m
~8m
~8.5m
→ How we came to the next proposal
Baseline Document: View of Vol. 2 (2020): SPS Beam Dump Facility: Comprehensive Design Study

## Slide 4: BDF Vacuum Vessel – Current Concept
Primary Functions:
Minimise activation of the surrounding air
Maintain vacuum level of 10-3 mbars
House the target, related proximity shielding and relevant cooling components
Maintain target alignment with the beamline
Keep beam line vacuum continuity
Auxiliary Functions:
Contain a system to ease the removal of the target and shielding
Provide structural integrity
Integrate with the safety systems
Allow for integration of coolant pipes into the vessel
Guide Rails
Vacuum vessel door
Vacuum vessel flanges connections
External Dimensions (without guide rails):
  6410 x 2050 x 2965mm
Internal Dimensions:
  6210 x 1750 x 2665mm
Volumes:
  Internal = 28.96m3
  External = 38.96m3
Empty Weight:
  ~25000kg
Foreseen Internal Load:
  ~142000kg

## Slide 5: Vacuum Vessel Feedthroughs
2 x DN25 Water Cooling Pipes
(Proximity Shielding)
2 x DN50 Helium Cooling Pipes
(Target)
Thermocouples
Feedthrough Requirements:
Frequency of opening vessel and exchanging the target
  Once per year vessel opening
  Once per 5 years target exchange
Must have a method to correct for misalignment (e.g. bellows)
  Manufacturing tolerances
  Thermal expansion
  Misalignment from pipe weight
Prevent leaks when in operation or when disconnecting the pipes for vessel opening
Maintain vacuum
Allow for simple and fast connection/disconnection
Ideally remotely compatible
Spare
Beam pipe
Pumping ports

## Slide 6: Feedthrough Parameters
Focusing only on the cooling feedthrough connections:
Target
  2 x DN50 Pipes
  Helium
  Temperature: ~200°c
  Pressure: ~16 bar
  Leak rate: 10-6mbar.l/s
Proximity Shielding
  2 x DN25 Pipes
  Water
  Temperature: ~30°c
  Pressure: Up to 16 bar
Note: Target and Proximity shielding feedthroughs must be integrated separately

## Slide 7: Human vs Robotic Intervention
Dose rate in this area:
  Integrated: 1 – 5 kGy/year
  Residual: 500-800 µSv/h
Human intervention – relatively quick and simple process for connection and disconnection
  Vacuum vessel length optimised for radiation levels to be low enough for human intervention at the door
Robotic Intervention – takes more time and requires area to be easily accessible by robots

## Slide 8: Target Removal Tentative Sequence

## Slide 9: Beam Line Removal

## Slide 10: Beam Instrumentation Package Removal

## Slide 11: Collimator Shielding Removal

## Slide 12: Collimator Removal

## Slide 13: Beam Pipe Removal

## Slide 14: Installation of Lifting and Shielding Tool for Vessel Door

## Slide 15: Disconnection of Utilities and Vacuum Vessel Door Unbolting

## Slide 16: Vacuum Vessel Door Removal 1/2

## Slide 17: Vacuum Vessel Door Removal 2/2

## Slide 18: Vacuum Vessel Open

## Slide 19: Transfer Rail Installation

## Slide 20: Push/pull Chain Mechanism Connection 1/2

## Slide 21: Push/pull Chain Mechanism Connection 2/2

## Slide 22: Trolley Extraction 1/2

## Slide 23: Trolley Extraction 2/2

## Slide 24: Upstream Shielding Partial Removal

## Slide 25: Proximity Shielding Upper Copper Removal

## Slide 26: Proximity Shielding Upper Copper Removed

## Slide 27: Target Removal

## Slide 28: Space Requirement for Target Exchange

## Slide 29: Current Configuration
DN200 Bellows
Remotely Operated Flange Connections
Weight of the connector is around 10kg and currently unsupported, weight of pipes would also rest on connector
Rigid pipes from within vacuum vessel, likely connected to flexible ones onwards from vessel

## Slide 30: Alternative Options – Support Module
Support frame attached to floor which connectors are held in.
Assembly still uses connector, bellows and rigid pipes which change to flexible ones.
Advantages | Disadvantages
Freedom to customise a support completely optimised to the application | Collimator position may need to change Hard to access remotely Need all connectors to align with the designated slots

## Slide 31: Support Module Removal

## Slide 32: Support Module Removal – Collimator Moved

## Slide 33: Support Module Removal – Connectors Disconnected

## Slide 34: Support Module Removal – Connector Module Moved

## Slide 35: Alternative Options – Collimator Support
Attach connectors to collimator for support. Assembly still uses bellows and rigid pipes
Advantages | Disadvantages
Don’t need an additional unit to support connector | Difficult to access the connectors further away to loosen them Collimator would need to have dedicated pipe holes running through it Collimator heat could dissipate into pipes

## Slide 36: Alternative Options – Flexible Pipes
Flexible hoses with a twist-lock/push-lock mechanism into either side of the vacuum vessel door
Advantages | Disadvantages
Removes need for bellows and flange connector Flexible pipes naturally correct for misalignment Uses less space on the door | Door structure would need to be changed Pipes could be more prone to wear and tear More potential for spills during connection and disconnection
Note:
Pipes within vessel would need to be long enough to partially open the door before disconnecting the pipe
Would likely need a pipe support within the vessel to prevent strain on connection
Possible for DN25 and DN50
Possible for DN25
Walther-prazision

## Slide 37: Alternative Options – Bellows Connected Internally
Bellows attached to the door internally, connectors bolted to the door externally, rigid pipes
Advantages | Disadvantages
Connector fully supported by door Connector could remain attached to the door | Introduces complications for removal Bellow size would increase to give access to screws Connector is constrained and reduces misalignment correction

## Slide 38: Alternative Options – Large Bellow
One connection set for the target, one for the proximity shielding
Advantages | Disadvantages
Would only require 2 bellows and 2 connectors | The connector would be very heavy and complicated Reduces ease to redesign later in the design process Larger connector would require more torque for tightening Could reduce misalignment capabilities as each pipe is constrained to their designated slot

## Slide 39: Questions
Are there alternative solutions?
Is a solution which is remotely compatible that doesn’t involve using bellows a viable option?
What are the main restrictions for remote handling of connections?
Are there any issues that would arise from any of these options that haven’t been covered?
Under what conditions would human intervention not be possible for connection and disconnection?
What other questions should we be asking?