## Slide 1: What is matRad?
Nermine Muradi, University of Tetova & Medical High school Nikola Stein
Particle therapy Masterclass
Slides by:
Nermine Muradi Aris Mamaras
Viridiana Badillo
Enrique Sánchez
Yiota Foka

## Slide 2
“Simulations of treatment planning of breast cancer and comparison with real cases”
Particle Therapy Masterclass 2021

## Slide 3: Erasmus+
Learning never exhaust the mind.
PTMC
HITRIplus project

## Slide 4: Radiotherapy
Patient fixation
Imaging (esp. CT, but also MRT or PET)
Identification & delineation of tumor volume and organs on 3D image
Treatment Planning
Verification & quality assurance
Patient positioning
Irradiation (several “fractions“)
Adapted from W. Schlegel & A. Mahr: 3D Conformal Radiation Therapy Springer Multimedia DVD & from the presentation of Joao Seco and Niklas Wahl

## Slide 5: What is MatRad?
matRad is an open source software tool for designing radiation therapy plans with a modulated beam of photons, protons and carbon ions.
Its name derives from the combination of two words:
MatLab + Radiation = MatRad
Developed by scientists at the German Cancer Research Center, DKFZ in Darmstadt.
Implemented for educational and research purposes
Source: http://bit.ly/3sX756v
Source: http://bit.ly/3uXfNDt

## Slide 6: Images

## Slide 7: Import of images (CT) , structure set and RT plans

## Slide 8: Treatment Planning System – TPS matRad
Photons: Base data for the photon dose calculation algorithm are obtained from the clinically approved photon dose calculation engine PDC++ and describes the decomposed lateral scattering kernels and depth dose components as detailed in for a 6 MV linear accelerator for multiple source to surface distances (SSDs).
Protons: Analytical calculations according are
used to approximate integrated proton depth dose profiles in water for 114 proton beam energies ranging from 31.72 MeV to 236.1 MeV which correspond to peak positions from 7 mm to 347 mm.
Carbon ions: Integrated carbon ion depth dose profiles
are based on FLUKA Monte Carlo simulations. Monte Carlo simulations were performed in water. In total, 121 carbon ion depth dose profiles linearly spaced from 115.23 MeV to 398.84 MeV depicting peak positions from 32 mm to 294 mm are part of the carbon ion base data file.

## Slide 9: How can you use the software?
For research purposes:
The program gives the possibility to use many parameters, for more realistic simulations.
- Uses the complete Mat Lab code for detailed analysis.
- Requires more computing power.
⚡⚡⚡⚡⚡⚡
+Computing Power
For educational use:
For educational use, the simplified form of the software on Windows, Linux, Mac is recommended.
Requires less storage space and computing power.
Does not require IDE (integrated development environment) for the use of the software.
⚡⚡⚡
-Computing Power

## Slide 10
Where is Matrad used today?
+30 INSTITUTES
With thousands of users worldwide.
For more information visit the map at the following link:
Link: https://bit.ly/MatRadUsers

## Slide 11: matRad cases for PTMC
The program installation package comes with 6 case studies::
  TG 119 or phantom C
  Liver
  Prostate
  Head & Neck (H&N)
  Box phantom
  Alderson case

## Slide 12: How is data processing carried out?

## Slide 13: How does MatRad work?
We enter the patient data
We set the parameters of the treatment plan (Radiation geometry etc.)
We calculate the dose of distribution to the cancerous tissue through algorithms
Visualization of the plan with the reverse planning technique (Inverse planning)
Completion of Simulation
Procedure
Data files:
Test Sample (C-phantom)
Liver
Head n Neck

## Slide 14: Graphical interface ot matRad
It can be used with Matlab or with matRad GUI

## Slide 15: Fundamental definition used by MatRad
GTV or gross tumor volume is defined as the macroscopic target tumor and is the exact location of the malignancy, as evidenced by imaging methods. It may consist of the inital tumor, metastatic lymphadenopathy or other meatastases.
CTV or clinical target volume is defined as the target clinical tumor, where the radio physicist assumes that cancerous tissue is still present. It consist of the tumor that is shown, if there is any, and any tissue with suspected tumor.
CTV = GTV + 1 cm – 2 cm,
PTV or "Planning Target Volume” is defined as the target volume for design. Includes CTV with an internal margin IM and an additional margin for placement which refers to patient movement and placement error.
OAR or “Organs At Risk", which are the organs that are more sensitive compared to healthy tissue. Organs in danger need adequate protection. Once the endangered organs are identifies an extra safety margin should be added to include their movement.
Gray (Gy) is a unit of measurement of energy absorption derived from ionizing radiation. Is equal to the energy absorption of one joule of matter with a mass of one kilogram 1Joule/kg

## Slide 16: Planes
Sagittal plane: It separates the body equally in left and right parts.
Coronal plane: It separates the body into two parts, anterior and posterior.
Transverse/Axial/Horizontal plane: It separates the body at the upper and bottom parts.
Source: https://bit.ly/3cZqM72
Source: https://bit.ly/3tY42v1

## Slide 17: Starting the program

## Slide 18: Panel: Plan
Bixel width: square size.
Gantry and couch angles: Set the angle values ​​for the Gantry and the couch (patient's bed). If 5 angles are used for the Gantry, then we will have 5 angles for the bed as well. These angles have values ​​from 0º to 359º.
Radiation mode: what particle will be used.
Isocenter: Always verify that “automatic isocenter” is active. It is the center where the radiation beam passes.
Fractions: Number of fractions = number of “slices” or slices that will be used to visualize 3D graphics.
Run sequencing: used to collimate the beam (in our case it is not active)

## Slide 19: Isocenter

## Slide 20: Panel: Workflow
Load > This PC> WIN (C)> program files>matrad>application
Load > My computer> (LOCAL DISK c)>program files>matrad>application

## Slide 21: Panel: Workflow
Here the program will look for the minimum radiation flux per bixel.

## Slide 22: Workflow – Exponential distribution
The optimizer optimizes a non-linear constrained optimization problem with an interior-point algorithm. The objective function and constraint functions are built from the specific objectives one can set in the table.
Objectives and constraints include the organs of interest (e.g target), as well as the organs at risk (e.g body, core etc.) that are about to be irradiated and also, we want to avoid obtaining more dose.

## Slide 23: Workflow: Save to GUI
This command save the set-up and requires to name it.. This step is important so the DVH can be shown.

## Slide 24: Visualization
Show DVH/QI: shows the volume-dose histogram.

## Slide 25: DVH for each case of study

## Slide 26: Summary of the processes
Choose a study case
Choose the plan settings
Repeat every time you change a setting
*

## Slide 27: TG119 Phantom case
Phantom TG119 or phantom C used by professionals to verify that equipment is functioning properly. They have standard shape and dimensions.
The purpose of use is to irradiate the “C” shaped area and avoid the central area
Irradiation part
Avoid the center

## Slide 28: Liver case
Axial view
Sagittal view
Coronal view

## Slide 29: Prostate case
Axial view
Sagittal view
Coronal view

## Slide 30: Head & Neck case
Axial view
Sagittal view
Coronal view