## Slide 1: Updates from the FCC-ee Layout & Optics Design WG
208th FCC-ee Accelerator Design Meeting
19/06/2025
S. Kostoglou, G. Roy, K. Skoufaris
Collecting information from all the speakers and
on behalf of the whole FCC-ee Layout and Optics Design e-group

## Slide 2: Introduction
Last summary from G. Roy, 3 meetings have taken place since then.
4th meeting on Reference points for machine layout from the BE-GM perspective (B. Weyer).
5th, 6th meetings focusing on:
  Goal: Enable a comprehensive comparison between GHC and LCC by gathering input from all relevant teams:
    Identify each team’s specific needs for the optics comparison and transmit information to optics experts.
    Facilitate exchange of information across various teams.
    Collect comparison criteria, expected deliverables and timelines from each team.
    Define which studies are most sensitive to optics choice.
    Transition from a conceptual to a technical design.

## Slide 3: Input received so far
At the moment, received input from:
  Collimation (R. Bruce)
  Injection (Y. Dutheil)
  Power converters (S. Pittet)
  Magnets (J. Bauche)
  Tuning (J. Keintzel)
  RF (I. Karpov)
  Beam instrumentation (R. Kieffer)
  Polarization (J. Wenninger)
Most common requests across teams:
  Complete lattice description for both optics, including technical and experimental insertions, for all operational phases  Reuse GHC insertions for LCC or develop dedicated ones.
  Lattice with errors and corresponding corrections for more realistic studies.

## Slide 4: Input received so far
At the moment, received input from:
  Collimation (R. Bruce)
  Injection (Y. Dutheil)
  Power converters (S. Pittet)
  Magnets (J. Bauche)
  Tuning (J. Keintzel)
  RF (I. Karpov)
  Beam instrumentation (R. Kieffer)
  Polarization (J. Wenninger)
Most common requests across teams:
  Complete lattice description for both optics, including technical and experimental insertions, for all operational phases  Reuse GHC insertions for LCC or develop dedicated ones.
  Lattice with errors and corresponding corrections for more realistic studies.

## Slide 5: Meetings summary
5th meeting
Magnets (J. Bauche):
Splitting of dipoles needs to be defined (max. length ~12m). Spacing between dipoles (~30cm) and between all magnets to be defined. This impact placement & number of SR shieldings and absorbers, structures.
Uniform dipole length and few families of quadrupoles to simplify production.
Main cost driver are the SSS magnets: LSS optics has fewer and shorter SSS magnets which positvely impact the cost. Additional cost optimization expected from powering sextupole families in series – sextupole tapering strategy to be defined.
Using same-polarity quadrupoles for the both beams requires 4 main coils and 4 embedded trims, simplifying production.
Overall power consumption cost similar between LCC and GHC: trade-off between increased consumption from same-polarity quadrupoles in LCC but shorter and fewer sextupoles.
Current baseline for correctors: trim coils embedded within sextupoles. Investigating option of including horizontal correctors in dipoles and dedicated vertical correctors if needed.
Option to transition from twin aperture to separate magnets if inter-beam distance must be increased beyond nominal 350 mm.

## Slide 6: Meetings summary
5th meeting
Tuning (J. Keintzel):
Sensitivity and tunability to mis-alignments and errors, correction efficiency between the two lattices and for all energy modes.
Path for gradual transition towards maximum performance: ballistic optics relaxed optics  baseline optics.
Strong interplay with other teams: tuned lattices will serve ascan starting point for many studies.

## Slide 7: Meetings summary
6th meeting
RF (I. Karpov):
  Integration constraints for 400 MHz and 800 MHz cavities.
  LCC estimated to result in 11% lower synchrotron radiation per turn  keeping constant luminosity, allows lowering total RF voltage requirements for ttbar with no impact on MA based on simulations, positive impact on integration.
  Z-pole: increasing RF voltage can improve beam loading, synchrotron tune spread and better tolerance to cavity trips  improved availability. To identify sweet spot between RF voltage increase and bunch length reduction.
  Evaluation criteria will include performance of SRF system (HOM power, power transients, availability), TFB efficiency and integration feasibility.

## Slide 8: Meetings summary
6th meeting
Beam Instrumentation (R. Kieffer):
  Main cost driver: number of BPMs as each quadrupole (or sextupole in LCC) will be instrumented with one.
  BLMs attached to girders.
  Transverse profiles at extraction line: optimal location identified for GHC, equivalent LCC location to be defined (large beam size, soft bending, extraction line)
  BS & luminosity monitors: Depend on SR leveld after which might be different between LCC and GHC due to placement and strengths of dipoles.
  IP-related diagnostics will be defined based on tuning requirements.
  BI specifications & tolerances expected to be similar between the two lattices.
  Space reservation in both lattices for diagnostics. Smaller beta-functions in LCC, exact impact on diagnostics, if any, to be studied.

## Slide 9: Meetings summary
6th meeting
Polarization (J. Wenninger):
  Main issue is the polarimeter integration: requires 100m field-free region (2.5 m laser chamber, 26m DS dipole resulting in ~2mrad kick, 70m drift). Currently, 2 quadrupoles in LCC breaking the field-free requirement.
  Exact location of depolarizing kickers, strength and bump configuration to be defined. Investigate if same kickers can be used for TFB .
  Comparison requires lattices for both optics including errors and corrections, solenoid and compensations.
  Main criteria will include acievable polarization levels in two lattices, performance and integration of polarimeter and feasibility of resonant depolarization.

## Slide 10: Open questions/next steps
Can GHC insertions be fully reused in LCC or dedicated insertions are required?:
  Several teams request flexibility to adjust the optics locally in technical insertions (e.g. injection, collimation) to study various schemes without impacting the global optics  at a first stage, matching will rely on expert knowledge, later to transiton to more automatic aproach.
  Some Insertions have strict requirements (phase advance, beta functions, dispersion constraints in collimation)
Are there integration issues that could be showstoppers for one lattice? (polarimeter, all stages of collimation, diagnostics etc)
Is there a larger inter-beam distance needed in some insertions? Shift from twin-aperture to separate magnets might be needed.
Hardware solutions (correctors, kickers) can be reused across lattices?
Solenoid scheme (local vs non-local)
Some teams require lattices for both electron and positron beams.
Discussion with Pantaleo et. al on how to address all of these issues.

## Slide 11: Next meetings
7th meeting (26/06/2024) will focus on collecting input from:
  Radiation (B. Humann, A. Lechner)
  Machine protection (D. Wollman, C. Wiesner, D. Domange, C. Hernalsteens)
  Beam-beam (X. Buffat)
Longer term we will also request input from other teams such as MDI, impedance, monochromatization..
Series of Master Classes on LCC optics by P. Raimondi (1 per week for ~4 weeks): Part 1 / 4 on the 25th of June.