## Slide 1: Radiation Effects on COTS Microcontrollers: Test Methodology, Qualification Results, and Mitigation Strategies
Alessandro Zimmaro
Rudy Ferraro
Salvatore Danzeca
BE-CEM-EPR
06/05/2025

## Slide 2: Agenda
Introduction
Radiation Effects on Microcontrollers
Microcontrollers Testing Results
Mitigation Schemes
Conclusions

## Slide 3: Introduction

## Slide 4: Microcontrollers in Particle Accelerators: Pros. and Limit.
Limited Speed
In terms of speed, the sequential operation of MCUs represents a significant bottleneck compared to the parallelism offered by FPGAs
Lowly costumizable
Compared to FPGAs, development on MCUs is limited by the available hardware peripherals.
EASILY COSTUMIZABLE
The various available peripherals, combined with libraries and drivers, enable Easy and Fast application development.
Compactness & Low Power
Ideal for distributed systems and tight spaces
Cost Effective
Affordable solution for specific tasks, even in redundant configurations.
SAMD21 : 4 € Vs M2GL025T : 70 €
Radiation Sensitivity
In commercial MCUs, implementing hardware-based Triple Modular Redundancy (TMR) is not feasible.

## Slide 5: Radiation Effects on Microcontrollers

## Slide 6: Radiation Effects on Microcontrollers: Cumulative Effects
Silicon
Oxide
e-
p+
+ + + + + + + + +
+ + -+- + -+- - -
Effect: electron-hole pair generation in silicon oxide
positive charge trapped
Units: Gray (Gy)  1 Gy = 100 rad = 1J/kg
Device Affected: MOSFET, Bipolar Junction Transistor (BJT)
Trapped
Electrons
Interface
Traps
Degradation in Microcontrollers
Increased Leakage Currents
GPIO Output State Degradation
Peripheral Malfunction or Degradation
Flash
Loss of Writability
Analog Performance Degradation
Greater Susceptibility to Corruption
Total Ionizing Dose (TID)

## Slide 7: Radiation Effects on Microcontrollers: Stochastic Effects
+N
Charged Particle
+N
+ -
+ -
+ -
+ -
+ -
+ -
+ -
+ -
Oxide
Effect: Create defect in crystal lattice by atom displacement
Metric: High Energy Hadron Fluence (>20 MeV) (HeH)
Unit: HeH.cm-2
Device Affected: MOSFET, BJT, Optoelectronic
Non- Destructive
Destructive
Bitflip in Configuration
Bitflip in SRAM stored variable
Failure in instruction Process (e.g. Program Counter (PC) Bitflip, Failure in Fetch-Decode-Execution Cycle, Wrong PC Increment)
Peripheral crash
Flash corruption
HARD (SEFI - Require RST)
SOFT ( May not Require RST)
Single Event Latchup
Single Event Effects (SEE)

## Slide 8: Radiation Effects on Microcontrollers: Test Methodology
The methodology can be divided in 3 Main Tests
  CPU+ALU performance is tested using Coremark  meaningful comparison of performance across different MCUs
  SRAM Sensitivity is evaluated through a specific Write/Read operation on part of the SRAM through an in-flux test.
  The Peripheral Test Part is normalized based on the project’s requirements  Can require more than 10 different tests according to the project.
  All Tests are carried out at PSI with 200 MeV Proton Beam
Dedicated designs are used to evaluate performance
This approach allows:
  Better observability
  Easier reconfiguration for failure investigation
The operational cross-section can only be tested through testing the project’s gateware.
Microcontrollers Test Methodology
CPU
SRAM
Peripherals
Coremark
- Performance Degradation (Score)
- Hard/Soft Failure Cross-Section
-SEL Cross-section
- Change Config (e.g. Cache, ECC)
Continous write-read
Hard/Soft Failure Cross-Section
Register Corruption
Lifetime
SEL Cross-section
Evaluate Mitigation Schemes
Dedicated Design
Hard/Soft Failure Cross-Section
Register Corruption
Lifetime
SEL Cross-section
Flash Writability: checked at the end of each run
Test Project Gateware
Test Strategies

## Slide 9: Microcontrollers Testing Results

## Slide 10: Microcontrollers Testing: TID Degradation
No CPU degradation has been observed on the different References Tested Except on the Apollo 3
No Current consumption increase
SAME54:
Programmability > 580 Gy
@580 Gy Flash Corruption  Near End of Life
SAMD21:
Longer lifetime
Low Programmability
Flash Not writable

## Slide 11: Microcontrollers Testing: CPU SEE Sensitivity
Configuration can impact the sensitivity  Operational cross-section cannot be known from component-level testing data
Usage of cache is not recommended
IWTD allows recovering most failures
  Still required additional Mitigation
  Additional Issues:
  IWTD TID degradation (SAMD21)
  Permanent Failure Induction (SAME54)
    If disabled, Ext RST was restoring MCU functionalities
    SEL can be mitigated only with Power Cycle
Different Config
Use of Cache
Use of ECC
Different Config
x10

## Slide 12: Microcontrollers Testing: SRAM SEE Sensitivity
In terms of SRAM SEE sensitivity, SAMD21G18 exhibited the highest sensitivity.
Although the ESP32 and ESP32-S2 share the same 40 nm technology node, the latter demonstrated better performance.
ESP32 exhibited similar performance to M2S010 (65 nm) FPGA
When available, such as in SAME54, ECC (type SECDED) should be enabled
  For this reference, ECC was always successful.

## Slide 13: Microcontrollers Testing: SEL Sensitivity
On most of the references tested no SEL were experienced except for SAME54 (Test Carried out with 200 MeV Proton Beam)
SAME54:
SELs observed: Not destructive and limited to 500 mA
If IWTD used  cannot be recovered via External Reset
SAMD21:
Extensively tested

## Slide 14: Mitigation Schemes

## Slide 15: Mitigation Schemes: Main Failure Detection Mitigation Schemes
An External Watchdog (EXTWTD) used to mitigate failures
Working principle:
  2 GPIOs are used by the Microcontroller (MCU) to feed EXTWTD
  If the EXTWTD receives no responses, it resets the MCU
Can the EXTWTD mitigate all failures? The answer is No!  Software Mitigation Schemes (SMS):
Developed and implemented in Microcontroller (MCU)
reset
Legend:
Data
Confirmed Uplink

## Slide 16: Software Mitigation Scheme: Software Watchdog
Bitflips in MCU’s SRAM or internal configuration registers  the MCU’s malfunctions
An Internal Software Watchdog (MCU-Real Time Clock Based) used to detect such failures
  A variable used to store the RTC time when the system wakes up or sleep
  MCU does not exit sleep mode or stays awake for longer time? Software Watchdog detects the fault and self-reset the MCU
reset
Legend:
Data
Confirmed Uplink

## Slide 17: Impact of Software Mitigation Schemes on BatMon
Other protection mechanisms:
  A management function via attribute instruction is assigned to all handler function definitions in the code and protects incorrect configurations that could result from SEEs.
  TMR applied to critical counters.
  Critical Variables stored internal MCU Flash and are only read.
  Protect mechanisms to fault reading are applied.
SEFI
SEFI
SEFI
Device | Downtime Period [Minute] | Downtime/Uptime [%] | Mitigation Used
BatMon 1 | 187 | 2.58 | All
BatMon 2 | 3517 | 48.82 | Ext Wtd

## Slide 18: Conclusions

## Slide 19: Conclusions
The Pros. and Limit. of using microcontrollers within the accelerator environment have been outlined.
Both cumulative and stochastic radiation effects on microcontrollers have been discussed.
A test strategy for MCU qualification has been presented.
Results from various tested references have been compared and analyzed.
  The SAMD21 currently represents the best parts both in terms of TID and Single Event Latch-up (SEL) Sensitivity.
  The use of the SAME54 is limited due to non-destructive SEL.
  The proposed test strategy, thanks to its enhanced observability, allowed identification of the root cause of permanent failures in the SAME54 (internal watchdog Reset triggered following SEL).
  It has been demonstrated that the use of an external watchdog (ExtWTD) is always necessary.
Mitigation schemes developed by the EPR section and currently adopted in the BatMon design provide alternatives to relying solely on the internal watchdog (IWTD).
Further tests are planned to investigate new references to expand the available resources.

## Slide 20
Thank you for your attention!

## Slide 21: Mitigation Technique for Hard/Soft Errors
An External Watchdog (EXTWTD) used to mitigate failures
Working principle:
  2 GPIOs are used by the Microcontroller (MCU) to feed EXTWTD If the EXTWTD receives no responses, it resets the MCU
Can the Ext WTD mitigate all failures? The answer is No!
SEFI
No Response
In normal conditions system passes through two operating modes feeding the Ext WTD.

## Slide 22: Mitigation Technique for Hard/Soft Errors
Bitflips in MCU’s SRAM or internal configuration register  the MCU’s malfunctions
An Internal Software Watchdog (MCU-Real Time Clock Based) used to detect such failures
  A variable used to store the RTC time when the system wakes up or sleep
  MCU does not exit sleep mode or stays awake for longer time? Software Watchdog detects the fault and self-reset the MCU
SEFI
Ext WTD still fed by MCU
SWTD Timeout

## Slide 23: Radiation Effects on Microcontrollers: Test Facility
Testing Microcontrollers can be trivial, requiring several qualification campaigns.
In terms of R2E effects, PSI Allows complete qualification of Microcontrollers
However:
  If B10  SEEs From Th  Test required at ILL
  Alternative solution: CHARM
  LDR Effects should be assessed  CO60
CERN Cobalt 60 Facility
Geneva, Switzerland
100 Tbcq Co60 Source
https://www.psi.ch/en/pif
Proton Irradiation Facility
Paul Scherrer Institute
Viligen, Switzerland
TENIS: Thermal And Epi-thermal Neutron Irradiation Station, Grenoble France
Microcontrollers
TID
SEE
ILL
PSI
Thermal neutrons
https://www.ill.eu/
CC60
Thermal neutrons
Thermal neutrons
LDR