## Slide 1: SOCRATES: System-On-Chip RAdiation Tolerant EcoSystem for ASIC designs and microcontrollers in HEP applications
R2EWG Workshop
6 May. 2025
Kostas Kloukinas
EP-ESE-ME

## Slide 2: Challenges in ASIC design @ HEP
Technology Challenges
  Complex deep-submicron silicon manufacturing processes
  Powerful, Flexible but highly Complex EDA Tools
Design Challenges
  Designs of increasing complexity and size
  Novel designs for scientific instrumentation
  Radiation Tolerance
Productivity Requirements
  Large, fragmented, multinational design teams
  Designers with different levels of expertise
  Work on common design projects
  Costly technologies
  Importance of 'first-time-right’ designs !
Technology scaling
130 nm
90 nm
65 nm
45 nm
Design Methodologies
EDA software Tools
28 nm
14 nm
Notes: After a couple of the years on the service I realized that the design teams (CERN and institutes) were facing significant challenges in their design work especially with the advent of HL-LHC electronics.

## Slide 3: EP R&D WP5 “IC TECHNOLOGY”
5.1 Technology Evaluation | 5.2 IP block development | 5.3 Intelligence on Detector (IoD) | 5.4 Powering solutions | 5.5 3D Interconnect solutions
G. Borghello | R. Balabriga | A. Caratelli, D. Ceresa | S. Michelis | K. Wyllie
K. Sarbandi | F. Bandi* | M. Andorno | P. Antoszczuk | M. Campbell
G. Termo* | T. Hoffman* | B. Denkinger | G. Bantemits | K. Kloukinas
G. Ciachera* | M. Piller* | M. Zahedi | S. Koseoglou | F. Piernas Diaz
 |  | J. Dhaliwal | G. Ripamonti | J. Alozy
 |  | A. Nookala | M. Macaluso | M. Kovacs
 |  | F. Brambilla K. Kloukinas | A. Ocarino | S. Al-Tawil X. Llopart
WP5: Research novel solutions for ASIC design, powering, and interconnects
Lead by K. Kloukinas, D. Ceresa (deputy)
NEW!
* Concluded their contract
Concluded
CERN EP department launched a strategic R&D programme on technologies for future experiments. https://ep-dep.web.cern.ch/rd-experimental-technologies

## Slide 4: On Detector Intelligence
CERN EP R&D activities
SOCRATES
RISC-V SoC
SOC Radiation Tolerance EcoSystem
Standardized Hardware IPs
Generate custom SoCs
Radiation Tolerant
Open Source
PixESL
Virtual Prototyping
Virtual Prototyping Framework for Pixel Detectors
Applying System Level modeling concepts on pixel detectors readout systems
Cycle-accurate simulations
From analog front-end to chip/system readout
Open Source
EP R&D WP5.3 “On Detector Intelligence” incorporates TWO COMPLEMENTARY R&D ACTIVITIES:

## Slide 5: PixESL - Methodology
For more details: Virtual Prototyping Framework for Pixel Detector Electronics in HEP,
F. Brambilla, DVCON Europe 25 (Best Research Paper award)

## Slide 6: PixESL - Methodology
 | Velopix | Proposed
Pixel | 256x256 | 256x256
SP | 128x128 | 128x128
Regions | 64x8 | 128x8 *
EoC | 64 (8 ch.) | 128 (16 ch.)
Arbitration | Round-robin | Back-pressure
Readout eff. | 90 % | 99 %
Avg. latency | ~100 cy. | ~30 cy.
A virtual prototype allows for exploring different architectures without defining the design details.
Network connection and hierarchy
Memory sizing
Arbitration
For more details: Applications of PixESL framework on pixel detectors for HEP experiments,
J. Dhaliwal, TWEPP 24 (Oral Presentation Award)

## Slide 7: The SOCRATES platform
HW/SW build system
(SoCMake )
Generate the top-level SoC
Integrate IP blocks
Infer interconnects (crossbars, adapters)
Fault tolerant interconnects
Automatic TMR of IP blocks
Invoke toolchain
Generate Hardware Abstraction Layer (HAL)
Generate linker scripts
Verification
Functional testing environment
SystemC-UVM environment
FPGA prototyping
Fault injection framework
Formal verification for TMR
Advanced
In progress
Future developments
DEVELOPMENT STAGE:
Pre-verified IP block library
Run synthesis and physical implementation flow on targets
Generate constraints
Constraints for fault tolerance
Radiation hardening
Implementation
Hardware composition
Software generation

## Slide 8: SoCMake build system
CMake-based HW/SW build system generator for SoCs
Supports SystemRDL as an input configuration
  Register Description Language extended for supporting SoC description
  Used as top-level architecture description
Rapid prototyping of SoCs:
  Quick composition of IP blocks into full systems
  Quickly build different architectures with different IP blocks, hardware accelerators or different CPUs
  Dependency management
Open-source
  SoCMake: github.com/HEP-SoC/SoCMake
  Toolkit and implementation: gitlab.cern.ch/socrates
SIMULATE
Verilator
Xcelium
VCS
IMPLEMENT
Cadence
...
FPGA
Vivado
Software application
Register file and Interconnections (*.v)
Documentation - website (*.html, *.md)
UVM testbench (SystemC) and SEE injection utilities
Hardware abstraction layer
Config files for synthesis and implementation (*.yaml, *.tcl)
Top level HDL (*.v)
Software application
IP blocks and hardware accelerators (*.sv)
Linker scripts generation
*.sv
*.cpp
*.rdl
RDL toolchain
Credits to Risto Pejasinovic, Benoit Denkinger, Alessandro Caratelli, Marco Andorno, Anvesh Nookala

## Slide 9: Towards System-on-Chips
Turning our custom ASICs into programmable SoCs will provide:
Quick prototyping
Smaller number of more capable ASICs
Faster design and verification turnaround time
Cost effective development
Where are SoC ASICs applicable for the HEP community?
Standalone Rad-Hard
microcontrollers
On-detector monitoring & control
Beam monitoring
Embedded controllers
in front-end ASICs
Pixel chip calibration
Control and monitoring
Back-end tasks on chip
Advanced on-detector
data processing
Data aggregation ASICs
Custom HW accelerators
Machine Learning appl.

## Slide 10: TriglaV: from SOCRATES to silicon
Goals:
  Build a radiation-tolerant microcontroller-like SoC with the SOCRATES tools
  Validate the toolkit and demonstrate the feasibility of using programmable logic inside front-end ASICs
  Validate the 28 nm CMOS technology Common Design Platform
  Test the radiation performance and gather experience on SoC designs
Specifications:
  Fully generated out of the SOCRATES platform
  Suitable peripherals and architecture for a pixel readout ASIC embedded controller applications
  Radiation-tolerant design up to CMS Inner Tracker levels, with testability features to trace faults under irradiation
  Implemented on 28 nm bulk CMOS technology
  Prototyped on an MPW November 27th 2024

## Slide 11: TriglaV architecture
D-MSPU
32 kB SRAM
RISC-V Ibex
CPU
I-MSPU
32 kB SRAM
Bootloader
JTAG debug unit
SoC control
PLIC
TIMER-0
TIMER-1
GPIO
APB-RT interconnect
OBI TMR crossbar
UART
Master port
Slave port

## Slide 12: TriglaV architecture
OBI TMR crossbar
APB-RT interconnect
D-MSPU
32 kB SRAM
RISC-V Ibex
CPU
I-MSPU
32 kB SRAM
Bootloader
JTAG debug unit
SoC control
PLIC
TIMER-0
TIMER-1
GPIO
UART
Open-source high-TRL RISC-V core by lowRISC[1]
  RV32IMC ISA
  2-stage pipeline
Full TMR at Flip/Flop level
  4x area overhead for TMR, ~6x final area including SEU observability circuitry
TMR formal verification[2] and fault injection[3]
[1] P. Davide Schiavone et al., Slow and steady wins the race? A comparison of ultra-low-power RISC-V69cores for Internet-of-Things applications, PATMOS (2017) pp. 1-8.70
[2] A. Pulli, M. Lupi, A simulation methodology for verification of transient fault tolerance of ASICs designed for high-energy physics experiments, 2023 JINST 18 C01038
[3] A. Nookala et al., Soft-error Reliability Analysis and Error Rate Estimation for RISC-V Processors in High Energy Physics Environments, NSREC (2024), draft for IEEE TNS 2025

## Slide 13: TriglaV architecture
D-MSPU
32 kB SRAM
RISC-V Ibex
CPU
I-MSPU
32 kB SRAM
Bootloader
JTAG debug unit
SoC control
PLIC
TIMER-0
TIMER-1
GPIO
APB-RT interconnect
OBI TMR crossbar
UART
Hardwired bootloader loads the memories through the UART
Memory Scrubbing and Protection Unit (MSPU) for instruction and data:
  Dual port foundry SRAM (2x 32 kB blocks)
  Physical bit interleaving
  ECC and SECDED: Hamming(13,8) at byte-level
  Periodic scrubbing with configurable period

## Slide 14: TriglaV architecture
RISC-V Ibex
CPU
JTAG debug unit
SoC control
TIMER-0
OBI TMR crossbar
UART
D-MSPU
32 kB SRAM
I-MSPU
32 kB SRAM
Bootloader
Open Bus Interconnect (OBI)
  Core-memory local fast bus
  Standard by OpenHW Group similar to AXI
  Full TMR for fault tolerance
  Multi-master crossbar
PLIC
TIMER-1
GPIO
APB-RT interconnect

## Slide 15: TriglaV architecture
RISC-V Ibex
CPU
JTAG debug unit
SoC control
PLIC
TIMER-0
TIMER-1
GPIO
APB-RT interconnect
UART
D-MSPU
32 kB SRAM
I-MSPU
32 kB SRAM
Bootloader
APB-RT
  Peripheral bus
  Radiation-tolerant version of the AMBA APB standard
  Data and address bytewise encoding with Hamming(13,8)
  Single Error Correction, Double Error Detection (SECDED)
  Triplicated control signals
OBI TMR crossbar
Propose this interconnect for adoption by all IP blocks developed within the HEP community.

## Slide 16: TriglaV architecture
RISC-V Ibex
CPU
JTAG debug unit
SoC control
APB-RT interconnect
OBI TMR crossbar
D-MSPU
32 kB SRAM
I-MSPU
32 kB SRAM
Bootloader
PLIC
TIMER-0
TIMER-1
GPIO
UART
Minimal set of peripherals:
  Platform-level Interrupt Controller (PLIC) - OpenTitan
  Timers - OpenTitan
  GPIO - PULP
  UART - OpenTitan

## Slide 17: TriglaV architecture
RISC-V Ibex
CPU
JTAG debug unit
SoC control
APB-RT interconnect
OBI TMR crossbar
D-MSPU
32 kB SRAM
I-MSPU
32 kB SRAM
Bootloader
PLIC
TIMER-0
TIMER-1
GPIO
UART
JTAG port for general software debug (non-TMR)
Triplicated SoC control unit with a dedicated I2C interface
  Provides a redundant booting mechanism
  SEU counters and decoding error count readout
  Stream out some key CPU signals to compare with a golden simulation during radiation testing

## Slide 18: What does SoCMake generate?
plic.sv
plic.rdl
CMakeLists.txt
any other IP block
PLIC
uart.sv
uart.rdl
CMakeLists.txt
UART
apb_subsystem.rdl
triglav_soc.rdl
CMakeLists.txt
Top SoC

## Slide 19
cmake ../

## Slide 20: What you get in output from the tools
Top SoC Verilog
TMR peripherals
Linker script
A nice block diagram
Peripheral HAL

## Slide 21: TriglaV: first SOCRATES silicon prototype
  Credits to: the current team Alessandro Caratelli, Anvesh Nookala, Benoît Denkinger, Davide Ceresa, Marco Andorno and past colleagues Risto Pejasinovic, Georgios Nikolaidis, Viktoriia Tarasenko
Physical implementation
  Area: 1 mm x 2 mm
  ~300k instances
  64kB SRAM memory
  Operating frequency: 250 MHz
  28nm CMOS MPW with an integrated DC/DC converter (2.3V to 0.8V)

## Slide 22: TriglaV silicon prototype
Before Tape Out Functional Verification
  FPGA emulation setup
    ~103 faster than simulation
    Increased confidence in the RTL to real HW
  Functional verification
    Random verification of peripherals
    Simulation of the top level
Evaluation of Silicon Prototype
  Functional Tests
  TID Tests
  SEU and SET evaluation Tests
  Lessons learned !

## Slide 23: Future Plans
EP R&D WP5.3 “On Detector Inteligence” framework & alocated resources
Evaluate the TriglaV prototype
SOCRATES platform developments
  Develop further SoCMake, augment Documentation and Ease of Use
  Develop Comprehensive Verification at the SoC level
  Support Data Processing applications (convergence of PixESL with SOCRATES)
Future Silicon Implementations
  Embedded μController for “PicoPIX” Pixel Readout ASIC (28nm CMOS)for LHCb Velo detector upgrade
  Standalone μController component (on 28nm CMOS or 65nm CMOS)
Participate in Rigoletto project HORIZON Chips JU 2025
  RISC-V generation of high-performance processors optimised and intelligent automotive platform
  Rigoletto aims at developing RISC-V intellectual property (IP) components, including processor cores, accelerators, interconnects, memory hierarchy and peripheral subsystems.
  CERN participates as beneficiary along with 64 other partners (Industry and Academia) with a budget of €60M
  Participation will enhance CERN's expertise and supply resources to speed up developments.

## Slide 24
Thank You
  Credits to the EP R&D WP5.3 Team