## Slide 1
E. Lamb, D. Amorin, S. Albright, R. Calaga, H. Demerau,
A. Grudiev, L. Thiele, U. Von Rienen
Thanks to: A. Pastinante, B. Karlsen-Baeck
Longitudinal beam dynamics
High energy muon acceleration

## Slide 2
Introduction
2
Short, intense proton bunch
Protons produce pions which decay into muons which are captured
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
Longitudinal beam dynamics for the RCS chain

## Slide 3
Challenges for RCS chain
Short muon lifetime – injection and extraction on accelerating buckets, and high synchronous tune
Small acceptance due to 1.3GHz Tesla cavity
Counter-rotating bunches with induced voltages that sum in the same cavities

## Slide 4: Contents
New optics
Realistic injection
Counter-rotating beams

## Slide 5: New optics

## Slide 6
Slide on why synchrotron tune matters for stable motion
High synchronous tune

## Slide 7
High accelerating gradient leads to large synchrotron tune, however, must be below a limit
If the RF is split in stations, the effective tune is smaller
Qs ∝ √|η0| RCS1 2.4e-3 → 4.7e-4, meaning the is smaller, and fewer stations are needed
New optics –
Single bunch, fundamental mode and higher order modes (longitudinal plane)
Notes: Zoom box

## Slide 8
New optics
Both the emittance and the bunch distribution are improved with a higher number of RF stations
Notes: Shading bigger, do the distribution in red and blue

## Slide 9
Previous assumption: matched distribution on each injection to RCS
Full chain simulation: propagate bunch from RCS1-4
Budget of 10% emittance growth can be achieved (using optimisation of)
New optics – emittance growth
Propagate distribution
Match at each injection

## Slide 10
Optimisation of
Single bunch, fundamental and higher order modes, propagation through machine
Momentum compaction factor is reduced
Previous assumption synchronous phases the same in all RCS
Bucket is mismatched: Optimisation of relative reduces the mismatch, can achieve ~10% emittance growth through whole RCS chain
Notes: Each rcs on own with same synch ohase = emittance blow up, compare buckets and impr

## Slide 11: Realistic injection

## Slide 12
RF Frequency of 1.3GHz – short bucket
Long distribution coming from RLA2
Injection of distribution from RLA2
Desired distribution
From RLA2
Notes: Frequency, make axes bigger , distribution for optimised phases

## Slide 13
Bunch compression is a single pass device
Contains an RF cavity to ‘chirp’ the bunch to give a correlation of position with momentum offset
In a linear approximation, can be modelled with a matrix
[4]
Cavity
Chicane
Bunch Compression

## Slide 14: Bunch Compression
Given a bunch length reduction
No energy chirp
TESLA cavities
After bunch compression matrix
From RLA2
Notes: How much length of cavities and chicane do we need (l1/l2), magnets also (eg bending radius of RCS1)

## Slide 15
Injection of distribution from RLA2
Assumptions:
Single bunch
Fundamental mode and higher order modes induced voltages
Propagation of beam distribution
Optimised
Notes: Change colours and line width/text size, 90% emittance

## Slide 16: Bunch rotation
Show one plot of phase jump and how can improve rla2

## Slide 17: Counter-rotation

## Slide 18
F. Batsch showed preliminary results for counter-rotating beams at IMCC 2024
QL = 0.94106
Counter-rotating beams
Notes: Showed how induced voltages chain

## Slide 19
Counter-rotating beams
Introduction to toy model and blond simulation for cr
Notes: Toy model, to check results and for a comparison with BLonD, frozen distribution, ring, difference in timing with animation, induced voltages sum because they arrive at the same phase

## Slide 20
oppositely charged bunches
travelling in opposite directions
arrive at the same phase
and induce voltages that add constructively
Counter-rotating beams

## Slide 21
Minimises generator current for steady state, assuming dc current
Passage 0: convolution with line density
Passage 1: shift array by time between bunch arrivals, sum to convolution with line density
Passage 0: analytical formula
Passage 1: shift array by time between bunch arrivals decay, sum to analytical formula
BLonD
Toy Model
Counter-rotating beams
Notes: Frozen in BLonD

## Slide 22
Minimises generator current for steady state
Toy Model
Toy Model
Counter-rotating beams
Notes: To remove 50khz, with the toy model can estimate the induced voltage with detuning

## Slide 23
Assumptions: fundamental mode only, optimised for the single bunch case
Ideal number of RF stations is smaller distance between stations is larger, leaving more time for voltage to decay
Not taking into account cavity-generator interaction or HOMs yet L. Thiele’s talk
Counter-rotating beams
Notes: RLA2 , add HOMs,

## Slide 24
Conclusions
New optics reduces the number of RF stations needed, but still on the order of 10
Synchronous phase optimisation is required to maintain matching along the RCS chain, but emittance requirements limits the optimisation, single bunch 10% emittance growth
A bunch compressor does not adequately improve the transmission from RLA2 to the end of RCS1
A semi-analytical model of counter-rotating beams agrees with BLonD simulations
Counter-rotating beams 100% emittance growth and 8 RF stations
Inclusion of transient beam loading and HOMs needed to simulate full emittance growth L. Thiele presentation

## Slide 25
References
CAS proceedings 1993
Analytical formula for Gaussian bunch and a resonator
http://blond-admin.github.io/BLonD/modules/impedances.html#module-blond.impedances.induced_voltage_analytical
Monopole, Dipole and Quadrupole Passbands of the TESLA 9-cell Cavity, R. Wanzenberg, DESY, Notkestr. 85, 22603 Hamburg, Germany, September 14, 2001
CERN, “Beam longitudinal dynamics code (blond).” http://blond.web.cern.ch.
A. Aaksoy, ‘Beam Dynamics for RLA2 for the Muon Collider’
https://indico.cern.ch/event/1456536/contributions/6131257/attachments/2955755/5197393/mucol_rla_28-10-24_aaksoy.pdf
Takuya Akiba, Shotaro Sano, Toshihiko Yanase, Takeru Ohta, and Masanori Koyama. 2019.
Optuna: A Next-generation Hyperparameter Optimization Framework. In KDD.
Wolski, A. (2016, October). Nonlinear dynamics: Part 1. CAS: Introduction to Accelerator Physics, Budapest, Hungary