## Slide 1
Qixuan Huang
5th DRD1 collaboration meeting, 19-June-2025
Preliminary results of Picosec-RGroove

## Slide 2: Deformation in picosec-MM
Non-uniformity on both gain and time resolution of picosec-MM mainly comes from the deformation of detector parts;
Make every detector part flatten can greatly improve the uniformity，Picosec-MM collaboration already did excellent work on 10cm×10cm and 20cm×20cm detectors !!!
However, to make everything flatten, ceramic materials and complex manufacturing techniques are required, which limited the applications；
Yue Meng, DRD1 - WP7 Timing Detectors, 10/June/2025

## Slide 3: Another possible solution
Use another single-stage MPGD without any inner tension to minimize the PCB deformation；
Avoid ceramic materials and complex manufacture；
Use small size MgF2 crystals to follow the deformation of the PCB;
Hard Frame
MgF2
MPGD+PCB
Hard frame
MgF2
MPGD+PCB
Soft cushion sheet
Not in scale

## Slide 4
Key points of the “small MgF2” solution
Use only horizontal metal trace for the HV supplying to all the photocathodes；
Gas passages are longer than the total width of crystals to allow the gas smoothly gas flow;
If we use 4mm width HV trace and 4cm×4cm crystal, the dead area is 10%, this number will not change when the detector size increase;
We can decrease the “trace width/crystal size” to “2mm/2cm×2cm” if the non-uniformity is still too large for a 4cm×4cm crystal;

## Slide 5: Why RGroove?
Single stage amplification, no inner tension, good to decrease the deformation of the PCB;
High collection efficiency of primary electrons, good for high drift field application;
USTC is able to make small size RGroove with 1d readout;
MgF2
Photocathode
e-
Drift gap
Charged particle

## Slide 6: Design of 12cm×12cm Picosec-RGroove
1. Stainless steel frame
2. Spacer
3. RGroove PCB
4. Inner FR4 frame
5. MgF2 Crystals
6. Hard fixer + soft cushion sheet
7. Window

## Slide 7: Readout of 12cm×12cm Picosec-RGroove
No spring contact pin used to avoid PCB deformation caused by the force of pins;
FPC connectors and flexible PCB are used for readout;
Board-To-Board connectors are used to fix the readout PCB;
FPC connectors
Board-to-board connectors

## Slide 8: Principle verification of Picosec-RGroove
Before the manufacturing of large detector, we should use small ones to do the principle verification;
Active area is 24mm×24mm, readout by a round pad with 10mm diameter;
75m APICAL used, the corresponding width of groove is 90m, pitch is 140m;

## Slide 9
Production of Picosec-RGroove prototype
@LICP, Lanzhou
@Yixing Fastprint
Readout PCB
1. Etching substrate
DLC-PI-Cu
3. Etching
@USTC
2. Lamination

## Slide 10
Micro-etching of Copper
Expect effect of Micro-etching：
smooth edges
Thinner thickness
Basically no effect on width
Low etching rate: 0.30.5 m/min
Discharge reduces after etching
Micro-etching

## Slide 11
Picosec-RGroove
Thickness: ~ 75 m
Groove width: ~ 98/34 m
Groove etching is not perfect
RGroove PCB
MgF2 crystal with
2nm DLC photocathode
175 m spacer
Hard fixer
Window

## Slide 12
Laser test setup with small prototype
PICOSEC-RGroove
MCP PMT
The setup of Laser test small prototypes :
Prototypes: single-pad PICOSEC-µRGroove
Reference timing detector: MCP-PMT (< 10 ps resolution)
Preamplifier: CIVIDEC
Readout: high resolution oscilloscope (20 GHz sample rate)
Single pad
Laser

## Slide 13: Waveform of Picosec-RGroove prototype
Abnormal
Photon feedback?

## Slide 14: Analysis of PICOSEC data
MCP-PMT
PICOSEC-RGroove
Sigmoid fit of signal
A sigmoid function is fitted to the leading edge of the electron-peak
The time corresponding to a 20% CF method applied to the sigmoid fit
Time walk correction is applied before subtracting from the reference time
Cuts according to peak time is used
Time walk correction
Time difference
Cuts according to peak time

## Slide 15: Preliminary results
The Polya distribution was not observed
Single photon time resolution achieves ~ 60 ps @ 850V cathode voltage
66 ps
prototype1
prototype2

## Slide 16: Summary & Outlook
Several picosec-μRGroove prototypes are produced;
~60ps time resolution for single-photon achieved;
The distorted waveforms limited the time resolution;
Detector optimization to reduce the distorted waveforms;
The picosec-RGroove prototypes will be tested in July beam.