## Slide 1: Rucio at the EST Data Centre
Current challenges and considerations

## Slide 2: SOLAR TELESCOPE AT CANARY ISLANDS
OT Observatorio del Teide Tenerife
Observatorio del Roque
de Los Muchachos La Palma
VTT 70 cm (Germany, 1989)
THEMIS 90 cm (France, 1996)
DOT 45 cm (Netherlands, 1997)
GREGOR 150 cm (Germany, 2012)
SST 100 cm (Sweden, 2002)
ORM
EST 420 cm
The construction of EST will represent a key reinforcement in the development of the European Solar Research Area and the Observatories of the Canary Islands.
A new generation
and revolutionary
solar telescope
Astronet Roadmap 2022-2035
Notes: The site was selected based on the excellent observation conditions, mainly during the local morning, verified along the years by the Swedish Solar Telescope.

## Slide 3: Timeline - status
Conceptual design
Project Office
Conceptual design consolidation
Preliminary Design
Detail design specifications
(ESFRI)
2016
Detail design and construction
APPLICATION FOR ERIC CREATION
Getting ready for construction
PDR

## Slide 4
Challenges
Amount of data
Data Transfer
  Physical
  Data loss
Data management
  Data access
  Data embargoes
  Reprocessing data

## Slide 5
Instruments
7 Instruments which can be operated simultenously
  TIS/FBIs
    Blue , Visible and Red Channel
  IFS-S
    EMBER
  IFS-M
    Blue, Visible and Red Channel

## Slide 6: Instrument data budget
Data Transfer |  | 
EST SIS | Data rate | LL
EMBER (1083-1565 nm) | 14 GiB/s | 6 GiB/s
IFS-M R (680-1000 nm) | 25 GiB/s | 11 GiB/s
IFS-M V (500-680 nm) | 47 GiB/s | 20 GiB/s
IFS-M B (390-500 nm) | 75 GiB/s | 33 GiB/s
TIS/FBI R (680-1000 nm) | 6 GiB/s | 3 GiB/s
TIS/FBI V (500-680 nm) | 11 GiB/s | 6 GiB/s
TIS/FBI B (390-500 nm) | 18 GiB/s | 9 GiB/s
∑ | 196 GiB/s | 88 GiB/s
Data Volume (4h) |  | 
EST SIS | Data rate | LL
EMBER (1083-1565 nm) | 0.20 PiB/d | 0.09 PiB/d
IFS-M R (680-1000 nm) | 0.35 PiB/d | 0.15 PiB/d
IFS-M V (500-680 nm) | 0.64 PiB/d | 0.28 PiB/d
IFS-M B (390-500 nm) | 1.03 PiB/d | 0.45 PiB/d
TIS/FBI R (680-1000 nm) | 0.08 PiB/d | 0.04 PiB/d
TIS/FBI V (500-680 nm) | 0.15 PiB/d | 0.08 PiB/d
TIS/FBI B (390-500 nm) | 0.25 PiB/d | 0.12 PiB/d
∑ | 2.70 PiB/d | 1.21 PiB/d
LL = Loss Less Compression

## Slide 7: Data LeveL & FLOW
L2 Data
L3 Data
L3 Excellent Data
L2 Excellent Data
RAW
L0 Data
Good/Excellent L1 Data
L1 Data
Other data streaming (Headers, Quicklook,..)
Excellent L0 Data

## Slide 8: Topology
The EST Data Centre will be built on a distributed architecture, incorporating three distinct types of nodes
  On-site data center is to store raw and calibrated science-ready data.
  The primary node will be responsible for coordinating and transferring the scientific data to the following nodes.

## Slide 9
Access – EMBARGOES - Reprocessing
Main concern is:
Embargoes:
  How to control the access to the data?
Reprocessing data:
  Request it.
  How long is going to be available?

## Slide 10
Considerations
FAIR Principles
Node draft definition
  Rucio
    Tokens
    Embargoes
  Reana
    Reprocessing
    Data access
Virtual Observatory
  Data discovery

## Slide 11: FAIR PRINCIPLES

## Slide 12
Technologies In a Node
Try to not move the data once is in its node.
Compute the data as near as possible.

## Slide 13
Technologies In a Node
Data Manager
Main concern is:
Embargoes.
Tokens.
Data discovery.

## Slide 14
Technologies In a Node
Virtual research environment (VRE)
Main concern is:
Tokens.
Rucio access and integration.
Access :
  to batch system
  to distributed storage

## Slide 15
Future lines
Prototype
  Tokens
  Find a way to implement embargoes
  Integrate diverse technologies

## Slide 16: Ángela Hernández Delgado
EST Software Engineer
angela.hernandez@iac.es