## Slide 1: PixESL An Open-Source Virtual Prototype Framework for Detector Electronics
Mahdi Zahedi, Francesco Brambilla, Jashandeep Dhaliwal,
Davide Ceresa, Xavi L. Cudie, Stefano Esposito, Kostas Kloukinas

## Slide 2
Introduction to PixESL
Context:
  EP R&D Programme on Technologies for Future Experiments: IC Technology Work-Package (WP5)
  Development started in 2023 in the EP-ESE-ME section
Project:
  Name: PixESL (virtual Electronic System-Level prototyping framework for Pixel detectors)
  GitLab repository: Core: https://gitlab.cern.ch/iod/pixesl-group/core
      Project Template: https://gitlab.cern.ch/iod/pixesl-group/pixesl-project-template
      Tutorials: https://gitlab.cern.ch/iod/pixesl-group/pixesl-4-school
Publications:
  [2024] Paper: Virtual Prototyping Framework for Pixel Detector Electronics in High Energy Physics
  [2024] Paper: SystemC framework for architecture modelling of electronic systems in future particle detectors

## Slide 3
Motivation
guidelines
limitations
Time-consuming
(~years)
NO structured feedback
Physics simulation
Specifications
Hardware design
Verification
Time-consuming
(~years)
Design flow improvement

## Slide 4
Motivation
guidelines
limitations
ref. model
ASIC limits
guidelines
limitations
Fast (~months)
Reference model
for verification and physical simulation
Validation
Verification
Specifications
Physics simulation
Hardware design
Verification
PixESL framework
Virtual prototype
Design flow improvement

## Slide 5
Motivation
Simulation flow
From the particle interaction
with the sensor
Chip output
Sensing element design
Charge deposition + collection (+ digitization)
Front-end architecture +
Readout architecture +
Post-processing
PixESL
The emphasis of PixESL is:
Modelling the behaviour of pixel detector circuits and complementing TCAD and Allpix² by bridging the gap between charge collection and electronic signal processing.
End-to-end simulation flow
Notes: Allpix² focuses on simulating the physical processes in silicon detectors, from particle interaction to digitized hits.
However, it lacks detailed modelling of circuit-level behaviour (e.g., readout, analog front-end).

## Slide 6
PixESL in CERN experiments
Example of design exploration for LHCb VELO Upgrade II
 | Velopix | Proposed
Pixel | 256x256 | 256x256
SP | 128x128 | 128x128
Regions | 64x8 | 128x8 *
EoC | 64 (8 ch.) | 128 (16 ch.)
Readout eff. | 90 % | 99 %
Avg. latency | ~100 cy. | ~30 cy.
Arbitration | Round-robin | Back-pressure
Baseline
Proposed

## Slide 7
Conclusion
PixESL, Allpix2, and TCAD together provide an end-to-end simulation of pixel detectors.
PixESL provides a template and basic implementation of modeling the circuits in pixel detectors.
PixESL is designed in a modular way, helping user to easily integrate their own model.
PixESL provides the community with the opportunity to have a library of circuit models.
PixESL facilitates early design space exploration for the designers of pixel detector circuits.