## Slide 1
BI Technical board on machines restart
M.Bozzolan as BI coordinator for L3 and LEIR
LINAC3 and LEIR 2025 startup
26th June 2025

## Slide 2
LINAC3 overview
M. Bozzolan - LINAC3 and LEIR 2025 startup
IST checklist partially filled
Is there a need to modify fields?
Oxygen run ongoing since mid April
L3 meeting on Monday morning

## Slide 3
LINAC3 BCTs and Faraday cups IST
M. Bozzolan - LINAC3 and LEIR 2025 startup

## Slide 4
LINAC3 main points
Major request was the improvement of ITF.BCT25 installed in 2024 (baseline drift) The new version installed this year is OK
ITF.BCT15 had an issue at the beginning of the run Amplifier replacement solved the issue (but still open in JIRA)
One SEM grids got stuck requiring intervention of the expert contacted after the weekend Probably not a risk for the SEMs in L3 but I asked to inform directly the expert and not only create the ticket that goes to the BI coordinator only.
BCT FECs moved to White Rabbit Timing and Debian OS
M. Bozzolan - LINAC3 and LEIR 2025 startup
Online beam energy measurement using LEIR injection BPM ToF now available for operation

## Slide 5
LEIR overview
IST checklist partially filled
Is there a need to modify fields?
XEI devices (EC, IPM not presents)
M. Bozzolan - LINAC3 and LEIR 2025 startup
Oxygen run ongoing since mid May
No weekly meeting

## Slide 6
LEIR main points
IPM amplifier (XEI) upgraded Now the NOMINAL (high intensity) beam readout is not saturated anymore
Electron cooler power converter (EPC) very noisy Old converter refurbished from LEP
M. Bozzolan - LINAC3 and LEIR 2025 startup

## Slide 7
Smooth machine restart
No LEIR operator  No IST check from OP side However let’s make use of the optool
Summary
M. Bozzolan - LINAC3 and LEIR 2025 startup