## Slide 1
Requirement for LSS4 bumpers:
One current monitoring interlock connected to the SPS extraction BIC (used for LHC extraction)
One current monitoring interlock connected to the NA extraction BIS (used only for NA extraction)
EPC’s side:
The LSS4 bumpers FGC3 can implement two hardware interlocks:
LHC users -> channel 1
FTARGET users -> channel 2
+LSS4 bumpers

## Slide 2
One concentrator option (proposed last time)
2x extraction sextupoles
8x LSS4 bumpers
SPS slow extraction
Slave BIC
SPS slow extraction
Master BIC
Issue: no possibility to distinguish these interlocks based on the cycle -> the LSS4 bumpers interlocks would have to be considered for all destinations
Question: can the FGC3 channel 2 provide a true interlock (using large thresholds) for non-NA users? And have a finer tolerance for NA users?
BA4
BA2
Two concentrators option
New concentrator installed in BA4, i.e. additional hardware + fibres
2x extraction sextupoles
8x LSS4 bumpers
SPS slow extraction
Slave BIC
SPS slow extraction
Master BIC
BA4
BA2

## Slide 3
General question on extraction sextupoles:
Because the extraction sextupoles are interlocked regardless of the cycle,
do they really have to be interlocked with the NA BIS in BA2?
Could they be connected to the SPS ring BICs in each individual point instead?
SPS ring BIC in BA1
SPS ring BIC in BA4
SPS ring BIC in BA5
SPS ring BIC in BA6

## Slide 4
List of LSS4 bumpers:
RPPAO.BA4.MPSV.41303
RPPAO.BA4.MPSV.42303
RPPBY.BA4.MPSH.41402
RPPAO.BA4.MPLV.41501
RPPAO.BA4.MPLV.42101
RPPBY.BA4.MPSH.42198
RPPBY.BA4.MPLH.41658
RPPBY.BA4.MPLH.41994