## Slide 1: Measurements with AC-LGAD at JSI
DRD3
16 May 2025
Bojan Hiti (JSI Ljubljana)

## Slide 2: Samples and readout
4 channel AC-LGAD investigated with IR Top-TCT
  IHEP V3 W11Q4-1
Mounted on 4-channel Chubut2 Front End Board (40 dB)
Read out with DRS4 digitizer
  700 MHz, 5 GS/s
First signals observed last week
Ch3
Ch4
Ch1
Ch2
Bias ring (GND)
-HV back plane

## Slide 3: First measurements with AC-LGAD (standard TCT)

## Slide 6: Future plans
Plan to study AC-LGAD performance in terms of hit rate:
  What is effect on signal shape by two simultaneous hits spatially ‘close’ together
  What is recovery time needed to observe no pile up effects?
Developing a new laser based test method
  Laser allows precise control of hit position/energy/time of hit
Measurement strategy:
  Inject two laser signals:
    Hit 1 (normal hit) comes first and is stationary
    Hit 2 (probe hit) is injected in different positions
    Hit 2 can be delayed by a few ns w.r.t. to Hit 1
  Read out the waveform containing both signals
Hit 1
Normal hit
Hit 2
Probe hit

## Slide 7: Double Beam TCT (DB-TCT)
Double Beam TCT – Two signal injections obtained by splitting an original laser beam into two beams and physically separating two beams
Laser source
1064 nm
300 ps
beam splitter
Sample
(not to scale)
DRS 4
  Fine alignment of both beams necessary
    Common focus and known point of entry
  Beams refract (favorably) on silicon surface
    Angle between beams in silicon about 10°
  Beam 2 can be moved independently of beam 1
  Delay by extending beam 2 fiber length (steps of 5 ns)
Beam 1
Beam 2
Beam 2 positioning stage
Beam size in focus 10 µm

## Slide 8: DB-TCT setup
Chubut 2
Motherboard
Chubut 2
Daughterboard
with sample
Beam splitter
Beam 2
Beam 1

## Slide 9: DB-TCT first results (with ATLAS HGTD LGAD)
Beam 2
5 ns delay
Beam 1
XY scan
Beam 1 stays at rest
Beam 2 moves
both beams well aligned w.r.t. each other