## Slide 1: AC-LGAD readout electronics based on FPGA
K. Hu
on behalf of the NEX group in SDU

## Slide 2: Front-End Readout electronics
Transimpedance Amplifier (TIA): Vout=Iin* R;
Voltage Amplifier (VA): Vout = (1+R2/R1)Vin;
Wideband Radio-Frequency Amplifier (RF): fixed gain.

## Slide 3: Readout electronics
LGAD detector & adapter board
LGAD front-end electronics (FEE)
PC

## Slide 4
2-ch test system to validate the time resolution measurement:
1. RF: ADL5545->6 GHz with integrated bias control circuit;
2. Ultrafast comparator: ADCMP572 with differential output;
3.Time-to-Digital Converter (TDC): KCU116 Dev-> Tapped delay time technology in the FPGA.
Currently, ~6 ps resolution can be achieved.
~11 ps
FEE Verification

## Slide 5
16-ch front-end board :
1. RF: ADL5545->6 GHz with integrated bias control circuit
2. Comparator: ADCMP572 with differential output;
16-ch electronics prototype
KCU116 dev
16-ch front-end board
KCU116 dev : TOT & TOA measurement
Thanks for your listening!

## Slide 6
backup

## Slide 7
backup
  FPGA-TDC
  1.Coase time：16-bit counter；
  2.Fine time：Time delay line is implemented CARRY8 primitive。