## Slide 1: Status of European Compact Light Sources: perspective for a CLS in Morocco Bridging to South-Europe
Luca Serafini , INFN-Milano, luca.serafini@mi.infn.it
Compact Light Sources are multiple bridges linking the classical world of radiation sources (synchrotron light sources, free electron lasers) to the quantum world of Compton: they also bridge the world of high energy physics with radiation sources
Because CLS are boosted mini-colliders (electron beams vs. photon beams) devoted to generate secondary beams instead of particle physics events: and they uniquely exploit the quantum nature of light to provide users with advanced photon beams
CLS are also extreme examples of compact research infra-structures that can be hosted in University Campus with modest investments (in the range 10-20 M$), opening the way to fundamental research and high social-impact applications

## Slide 2: Status of European Compact Light Sources: perspective for a CLS in Morocco Bridging to South-Europe
1-25 GeV
electrons
100-0.5 Å
X-ray photons
cm und. period lu
20-150 MeV electrons
1 m laser l
20-350 keV
X-ray photons
3 km
20 m
100 M$ - 1 G$
10 M$ - 20 M$
Synchrotron Light Sources/Free Electron Lasers (C.E.M. world)
vs.
Inverse Compton Scattering CLS (QED world)
virtual photons
real photons
Ew u = hc/lu

## Slide 3
In Synchrotron Light Sources and Free Electron Lasers the electron beam scatters off virtual photons, represented by magnetostatic fields of dipoles, undulators, wigglers EX = 2g2 hc/lund
Compact Light Sources are based on electron beams scattering off real photons carried by a laser pulse EX = 4g2 hc/llaser
Radiating same photon energy EX requires much larger g in synchrotron light sources (in the range of thousands, i.e. GeV) : size and costs are much larger
However brilliances are larger than ICS’s if photon energies considered are smaller than 100-150 keV, because beam currents in synchrotrons are 200-400 mA, while in ICS ranges from micro-A to a few mA. Nevertheless, above 200 keV ICS are out-performing synchrotron based light sources because critical frequencies, even with multi-GeV beams, do not overcome 150 keV .
Compact, high-brilliance X-ray sources based on Inverse Compton scattering, an option for the development of small, cost effective, advanced campus-based research infrastructures, tailored as test facilities or user facitlies

## Slide 4
Rivaling with Synchr. Light Sources for energies above 50 keV

## Slide 5
FLASH
12.4
1.24
0.124
l (nm)
Thomson/Compton Sources
Brilliance of Lasers and X-ray sources
BELLA
ELI

## Slide 6
Inverse Compton Scattering: why Inverse?
(direct) Compton Scattering is performed by an energetic photon (X-rays) interacting with an atomic electron (eV)
Inverse Compton Scattering is performed by an energetic electron (MeV-GeV) onto a visible (eV) photon (“inverse” refers to the reaction kinematics, not the dynamics)
I.C.S. : Inverse Compton Scattering

## Slide 7
ICS are the most effective “photon accelerators” (boost twice than FELs)
“4g2 boost effect”

## Slide 8
All radiation originated by a Lorentz Boost associated to relativistic emitting particles (electrons, heavy ions) is intrinsically poli-chromatic because of gq correlation (energy boost of scattered photons depends on scattering angle, at q=1/g photon energy is 50% of max photon energy at q =0 ) of single electron spectrum (on top of inhomogeneous effects)
True for all kinds of Undulatory and Collisional radiation (bremsstrahlung, wiggler/betatron, synchrotron, RRS, ICS), while resonant or amplified radiation (undulators, FELs), that are diffraction limited thanks to their beam quality, are not (or only partially) affected
The g2q2 issue/disease
quantum
nature of
light

## Slide 9
Courtesy I. Drebot

## Slide 10
Courtesy I. Drebot
psec and sub-psec radiation pulses – large, round field of view
full and variable polarization (shot-to-shot)

## Slide 11
Kinematics of
Inverse Compton Scattering
a Cartoon
Lab Reference Frame
incident electron
Ee = gmc2
incident photon Eph
Electron rest frame
E*e = mc2
incident photon E*ph = 2g Eph
Lab Reference Frame
after Scattering
scattered electron
E’e = gmc2 + Eph – E’ph
energy of scattered photon at q=0 E’0 = 2g E*ph = 4g2 Eph
q
scattered photon at q
E’ph =E’0 (1-g 2q2)
scattered photon at
q=1/g E’ph =E’0 /2
q=1/g
if E*ph << mc2 the photon is scattered
back elastically with same energy E*ph
(zero recoil, Thomson limit)
Lorentz transformation (gcm = g)

## Slide 12
Poli-chromaticity implies using mono-chromators of different kinds (bragg-reflectors, collimators) to select a narrow bandwidth line from a broad-band spectrum
ELI-NP-GBS g –beam
collimator (2-19 MeV)
X-ray monochromator

## Slide 13
ICS Sources: three paradigma
Linac based (low flux, easy operation)
(full access to beam particles and phase space)
b) Storage ring based (large flux, challenging)
(no access to beam particles, limited access to phase space)
c) Energy Recovery Linac based (very large flux, very challenging)
(no access to beam particles, full access to phase space)
Linac based ICS are easily extandable to MeV gamma rays
towards nuclear physics oriented research and applications
Linac based ICS are also compatible to laser-plasma driven acceleration modules

## Slide 14
Cost of STAR ICS = 18.5 M€ with 2 beam-lines and 2 hutches
Built inside Università della Calabria campus, South Italy, with EU funds for the development of research infra-structures in EU regions of convergence

## Slide 15
highly asymmetric compact*
electron-photon colliders
*10 m, 10 M$
MeV/GeV’s electrons
eV’s photons – more challenging and difficult to operate

## Slide 16
BriXS: an example of high sustainability. High power 2 MW beam delivered to user with only 200 kW power consumption/dissipation with outstanding beam quality (larger than storage rings, same current)

## Slide 17
ThomX, Orsay-LAL, Paris

## Slide 18
MuCLS: a Compact Light Source (ICS) in Germany (Munich)

## Slide 19
Conventional X-ray tube for mammography
Spatial resolution ~100 mm
High Flux ~107 g/(mm2s) equivalent to ~5.1011 g/s over 20x20 cm2 area.
65 cm
Great example of Radio-logical imaging applied to mass screening over population: mammography
Low energy photons in the spectrum are absorbed by tissue, delivering radiation dose without bringing informations to detector. Risk of inducing secondary tumors increases without increasing the benefit of detecting early tumors
Absent in
Thomson
Source
X-ray
spectrum!

## Slide 20
3 cm thick in vitro human breast tissue
a) SR digital image
Energy 17 keV
Scan step 100 mm
MGD 1 mGy
b) SR digital image
Energy 20 keV
Scan step 100 mm
MGD 0.33 mGy
Conventional
X-ray tube 26 kVp
MGD 1 mGy
Mammography with Mono-chromatic X-rays at 20 keV has been proven
far superior in Signal-to-Noise-Ratio w.r.t. conventional mammographic tubes,
with a considerably lower radiation dose to the tissue
8th African School of Physics - Marrakech (MO) - July 2024

## Slide 21
Compact Thomson X-ray Sources could be located inside hospitals to diagnose
and treat patients directly at the hospital site (unlike Synchrotrons…)
8th African School of Physics - Marrakech (MO) - July 2024

## Slide 22
ICS Sources: typical fields of research
3D MICRO-TOMOGRAPHY with/without phase contrast
medical, cultural heritage, paleontological fields, material studies
b) Nuclear photonics with Nuclear Resonance Fluoresence
remote detection of nuclear materials
c) Dual energy imaging (Linac based ICS)
advanced radio-graphy with contrast imaging
d) Spectroscopy (ERL based ICS – large fluxes)

## Slide 23
20-130 keV
100-350 keV

## Slide 24
STAR X-ray beamlines
foreseen applications
with mono-chromatic
hard X-ray (350 keV)
3D micro-tomography

## Slide 25
Courtesy R. Agostino

## Slide 26: Photonuclear Reactions with g-rays
g
What happens?
8th African School of Physics - Marrakech (MO) - July 2024
Increasing the energy of ICS electron beam up to
300-400 MeV with plasma boosting stages (see Andrea Mostacci)

## Slide 27
Courtesy C. Barty - LLNL

## Slide 28: Photonuclear Reactions
gs
´

Separation
threshold
AX
A´Y

Nuclear Resonance Fluorescence (NRF)
Photoactivation
Photodisintegration

Absorption
(-activation)
´
~ 8 MeV
8th African School of Physics - Marrakech (MO) - July 2024

## Slide 30
8th African School of Physics - Marrakech (MO) - July 2024

## Slide 31
Last but not least:
with ICS (Linac-based) we can do also fundamental research in
QED, plasma physics, astro-physics and quantum gravity
Full Inverse Compton Scattering
the way an electron emits photons of energy larger than its own

## Slide 33
1 TeV
10 TeV
100 TeV
1 PeV
100 PeV
Eph (MeV)
E’e (MeV)
e- at rest E’e=mc2
E’e
Eph =0.5mc2
0.5mc2 = 255.5 keV colliding photons will
stop relativistic electrons of any energy Ee !
100 GeV
Eph=1 eV
Eph=1 meV
Eph=1 meV
C.M.B.R.
Follin, Primakoff, etc
our study
FICS

## Slide 34
Last but not least - B:
with ICS (Linac-based) we can do also applied research in
Earthquake prediction preparatory tests

## Slide 35
Grazie per l’attenzione
Thank you for your attention
more details in:
and references therein

## Slide 37
BACKUP SLIDES

## Slide 38
20 & 150 MeV e- beam @ screen
38
Active pressure
No pressure
The beam shows a significant visible shift on the target!
@20 MeV beam deceleration is less the 10%.
Considering other value as in the following Tab:
Shifts are amplified at lower energy and reduced with lower field.
60 kpart @ 150 MeV
First investigation of nonlinear effects near fracture points
Zero prior literature
highly innovative research
Let’s do it asap

## Slide 39
More mechanisms play a role in the muon energy loss :
Ionization.
Radiation losses:
  Bremsstrahlung.
  Pair production.
  Photonuclear excitation.
1 - Energy loss
39
Muons in SiO2
MuAEGIS considers the average muon energy loss
given by the sum of these effect.
Reference case:
500 GeV muon beam propagates ~700 m in SiO₂ rock.
Rock and quartz approximated as pure SiO₂.

## Slide 40
2 - MCS
40
Multiple Coulomb Scattering (MCS) is the main transverse effect causing stochastic deflection by an angle ϑ.
Molière theory: for relativistic particles, angle ϑ follows a normal distribution with σ = 𝜃₀ .
ϑ
The radiation length for SiO2 is L0 = 12.3 cm
The particle momentum p is updated step by step considering .
L

## Slide 41
3 - PRW
41
Piezoelectric Random Walk (PRW): second effect on beam
transverse plane.
+ + + + +
- - - - -
Ep
Ep = 20 MV/m for P = 400 MPa (= 4 kbar)
Lc up to few cm
Crystals and Ep are randomly oriented over 4π.
    Transverse momentum evolves as 2D random walk
Notes: spiegare il random walk

## Slide 42
2D random walk
42
PRW and MCS affect transverse momentum like a 2D random walk.
Each momentum step has a random direction. Each particle follows a unique transverse path, but the bunch evolves with averaged, ordered behavior:
Visual example:
20,000 muons through 1 km of ground Periodic layers: 1 cm rock / 1 cm quartz (20 tracks shown)
N: number of steps
li: step length ()

## Slide 43
Reference case
43
We simulate muons into 600 m of ground -- Periodic layers: 1 cm rock / 2 cm quartz
Notes: Errore! Emittanzza e sigma sono riferiti ad x, controlla!

## Slide 44
Great benchmark
44
FLUKA – envelope
MuAEGIS: 2.243 m (+2%)
Same case simulated with FLUKA for comparison. Additional effects observed, but overall good agreement.

## Slide 45
Quality is not mandatory
45
What happens with a higher emittance (10x) beam?

## Slide 46
We can see the build-up
46
We simulated beam envelope enhancement (∆) under varying quartz pressures observing non-linear evolution.

## Slide 47
How to see the effect
47
Effect observed by comparing muon distribution on detector plane with ideal case (no pressure/quartz).

## Slide 48
Dream big, start small, keep going far…
but don’t forget that a project is a dream with a deadline
My conclusion and advice

## Slide 50
CLS grid around Diamond (UK)

## Slide 51
Light sources started being developed in the ’50s and went
through several generations (1st  4th with FELs and MBA)

## Slide 52
ICS started being developed in the late ’90s only after the technology of high brightness photo-injectors became mature (same as FELs):
they keep following new advanced accelerator development,
including laser-plasma wake acceleration

## Slide 53
Courtesy L. Rivkin

## Slide 56
1 TeV
10 TeV
100 TeV
1 PeV
100 PeV
Eph (MeV)
E’e (MeV)
e- at rest E’e=mc2
E’e
Eph =0.5mc2
0.5mc2 = 255.5 keV colliding photons will
stop relativistic electrons of any energy Ee !
100 GeV
*hadronic threshold (Ecm < 600 MeV) with 255.5 keV photons ≈ 360 GeV
the most extreme acceleration
achieved in the universe ??
Eph=1 eV
Eph=1 meV
Eph=1 meV
C.M.B.R.
Full Inverse Compton Scattering: amazing power
of 255.5 keV photons to stop ANY colliding electron
FCC-ee
EupraXia

## Slide 57
1 TeV
10 TeV
100 TeV
1 PeV
100 PeV
Eph (MeV)
E’e (MeV)
e- at rest E’e=mc2
E’e
Eph =0.5mc2
0.5mc2 = 255.5 keV colliding photons will
stop relativistic electrons of any energy Ee !
100 GeV
Eph=1 eV
Eph=1 meV
Eph=1 meV
C.M.B.R.
Follin, Primakoff, etc
our study
FICS

## Slide 58
1 GeV
Eph (MeV)
E’e (MeV)
Eph =0.5mc2
Ee = 50 MeV
E’e =511 keV , T’e=0
200 MeV
5 GeV
Eph = 1 eV
Eph = 1 keV
in vacuum electron-photon collision
FICS – Full Inverse
Compton Scattering
fFICS = 1 !!

## Slide 59
FICS Relay in the cosmo - a possible mechanism to
propagate very high energy electrons in the universe
FICS
Direct
Compton
FICS, etc, etc

## Slide 60
scattered electron
E’e = gmc2 + Eph – E’ph
q
E’ph - energy of scattered photon at q
X = recoil parameter – twice the energy of the photon seen
by the electron in its own reference frame normalized to mc2
red shift at q≠0
All I.C.S. X/g ray Sources work at X<1 and A » 1
STAR (350 keV) XSTAR < 2.6.10-3 ASTAR > 104
ELI-NP (20 MeV) XELI-NP < 0.026 AELI-NP > 2.4.105

## Slide 62
where is the Continental Divide
between
Compton Scattering
and
Inverse Compton Scattering?
when the electron becomes
a projectile (as in ICS)
instead of
a target (as in Compton)?
Does it depend only on electron energy?
No, it depends only on asymmetry in colliding momenta

## Slide 63
I.C.S. low recoil X<<1
I.C.S. large recoil X>>1
S.C.S. (A=0) or
quasi-SCS (A<<1)

## Slide 64
20% rms spread
Incoming e- beam 10-4 rms spread
2.10-4
rms spread
g -ray in-vacuum mono-chromatization, SCS at large Recoil
10-1 spread
no energy-
angular
correlation
C. Curatolo - Whizard
Electron
Cooling of
photons!!
e- beam
is heated

## Slide 65
Spread of incidence angle
(resembles emittance)
cooling of
photons still
effective
as well as
heating of
electrons

## Slide 66
Schematic recap of X/g Radiation Sources
(keV, MeV, GeV…)
Spontaneous undulatory radiation (synchrotron, wiggler, betatron, channeling, bremsstrahlung)
Resonant/amplified undulatory radiation (undulator, FEL)
courtesy B. Paroli, M. Potenza
courtesy L. Rivkin

## Slide 67
Collisional radiation
(Relativistic Rayleigh Scattering aka Gamma Factory, Inverse Compton Scattering, Large Recoil ICS, Symmetric Compton Scattering)
Gamma Factory
I.C.S.
deep recoil I.C.S.
EXMP
low recoil
I.C.S. - STAR

## Slide 68
To transform to the Lab ref. system we need to compute
Then apply a Lorentz transformation

## Slide 69: Deep Recoil I.C.S. helps attenuating the g2q2 problem through slowing down of Lorentz boost gcm<<g
X=0.13
X=13.
X=1300.
laser
7 GeV e- beam
UV FEL
X FEL
R. Hajima and M. Fujiwara, Narrow-band GeV photons
generated from an x-ray free-electron laser oscillator, Phys.
Rev. Accel. Beams 19, 020702 (2016). XFELO Project

## Slide 70: An invariant view at Compton effect - 1 (any inertial ref. frame)
Arthur Compton,
Nobel Prize 1927
I.C.S.
photon looses energy
electron looses energy
isolated e- cannot absorb a photon
Phys. Rev. AB (2018)
21, 030701
S.C.S.
A<0
A<0
A=0

## Slide 71: An invariant view at Compton effect - 2 (any inertial ref. frame)
Direct Compton
I.C.S.
photon looses energy
electron looses energy
S.C.S.
CM ref. frame = Lab ref. frame
A<0
A<0
A=0

## Slide 72
ICS
1 eV – O(100) MeV
E’ph
(keV)

## Slide 73: Symmetric Compton Scattering suppresses the g2q2 correlation Photons are scattered at same energy at any angle Lorentz Boost is damped Radiation emission is intrinsically mono-chromatic Poli-chromaticity of incident photon beam is transferred to the scattered electron beam and viceversa (photon cooling, electron heating)

## Slide 74
A look at 4-vectors (head-on collision)
Inverse Compton
Symmetric Compton
1
1
fixed target
collider

## Slide 75
S.C.S. Spectra at different Recoils

## Slide 76
Turning a radio-active Cobalt-60 fixed energy
gamma-ray source into a tunable sorce of gamma-rays

## Slide 77
2 spectral lines merged into a single tunable line

## Slide 78
Eph (keV)
Te (MeV)
S.C.S. – incident photon energy vs.
incident electron kinetic energy

## Slide 80
Inverse Compton Sources rivaling/overcoming
Synchrotron Light Sources at photon energies above 80-100 keV
I.C.S.
STAR
ELI-NP-GBS

## Slide 81: Inverse Compton Sources, Overview, Theory, Main Technological Challenges – Photonic Colliders
New Generation of X/g ray beams via electron-photon beam collisions for advanced applications in medicine/biology-material science/cultural heritage/national security and fundamental research in nuclear physics and high energy physics (e-g, g-g colliders, pol. e+ beams, hadron. physics, etc)
Inverse Compton Sources (ICS) are e-/photon colliders aimed at producing secondary beams of photons
Several Test-Facilities world-wide: after a decade of machine test&development we are entering the era of User Facilities in X-ray imaging and g-ray Nuclear Physics and Photonics

## Slide 82
Need of high peak brightness/high average current electron beams (cmp. FEL’s drivers) fsec-class synchronized and mm-mrad-scale aligned to high peak/average power laser beams
Main goal for Nuclear Physics and Nuclear Photonics: Spectral Densities > 104 Nph/(s.eV) photon energy range 1-20 MeV, bandwidths 10-3 class
Main goal for Medical Applications with X-rays: tunability in the 20-120 keV range, good mono-chromaticity (1-10 %), high flux (1011 min., 1012 for radio-imaging, 1013 for radio-therapy)
Challenges of electron-(optical)photon colliders as X/g beam Sources using Compton back-scattering

## Slide 83
Main goal for MeV-class g - g and TeV g - nucleon colliders: Peak Brilliance > 1021 Nph/(s.mm2.mrad2.0.1%) 109<Nph<1013 Source spot size mm-scale (low diffraction, few mrad) Tunability, Mono-chromaticity, Polarization (H,V,C)
Photon-Photon scattering (+ Breit-Wheeler: pair creation in vacuum) is becoming feasible with this new generation g-beams: a g-g low energy collider

## Slide 84: 3rd-4th Generation Light Sources
Synchrotron light sources: < 50 keV, > 50 ps (100 m, 300 M$)
X-ray FEL (LCLS): energy ≤25 (50?) keV, 1-100 fs (1 km, 1 G$)
New approach: inverse Compton scattering (ICS) 20-200 keV , sub-ps, (10 m , 10 M$) – sometimes called Laser Synchrotron since a laser pulse substitutes the magnetic undulators

## Slide 85
Photon / Particle Beams: diffraction, envelope, matching, co-propagation.
Example: TEM00 Gaussian Laser mode (circ. pol. M2=1 diffr. limited)

## Slide 86: LASER
PARTICLE BEAM

## Slide 87
with
electron recoil
without
electron recoil

## Slide 88: Large Recoil in ICS damps the effect of large bandwidth incident photon beams onto the bandwidth of scattered photons
collimation
angle
beam
emittance
beam
en. spread
incident
photons
en. spread
diffraction
non
linearity
equivalent to FELs Kim-Pellegrini crit. on 3D inhomogeneous effects on photon bandwidth

## Slide 89: Large Recoil in MPP damps the normalized emittance of the secondary generated muon beam
cmp. MAP norm. emitt. 2.5.104 nm.rad
after ionization cooling
muon beam norm. emittance

## Slide 90
MuCLS