## Slide 1: IAEA activities related to accelerators applications to healthcare
Valeriia Starovoitova, Aruna Korde, Celina Horak
International Atomic Energy Agency
Notes: logo

## Slide 2: Overview of the IAEA

## Slide 3
IAEA
Set up in 1957 to promote safe, secure and peaceful nuclear technologies
Currently includes 178 Member States
Over 2500 professional and support staff
Headquarters in Vienna
Two scientific laboratories and research centres
Liaison offices in New York and Geneva

## Slide 4
The “Three Pillars” of the IAEA
Safeguards
&
Verification
Safety
&
Security
Science
&
Technology
IAEA and SDGs
Notes: Better picture of SDGs

## Slide 5: Organizational Chart
Office of the Director General
Department of Management
Department of Nuclear Energy
Department of Nuclear Science and Applications
Department of Technical Cooperation
Department of Nuclear Safety and Security
Department of Safeguards
Division of Physical and Chemical Sciences
Division of Human Health
Radiochemistry and Radiation Technology Section
Dosimetry and Medical Radiation Physics Section

## Slide 6: What do we do?
Research and development
Production of radioisotopes and radiopharmaceuticals
Radiation technologies for healthcare, industry, environment and cultural heritage
Non-destructive testing and other uses of sealed sources
Implementation of technologies
Education and training

## Slide 7: How do we do it?
Technical Meetings, Consultancy Meetings & Conferences
Expert Missions
Publications
General Conference side-events and Scientific Forum
Collaborating Centres
Coordinated Research Projects (R&D)
Technical Cooperation Projects (implementation)
Regular program activities
https://www.iaea.org/services/coordinated-research-activities/how-to-participate

## Slide 8: Projects for Health Applications
Development of new Tc-99m radiopharmaceuticals for disease diagnosis
Production of Zr-89 and Development of Zr-89 Radiopharmaceuticals
Production of Cyclotron-based Gallium-68 and related Radiopharmaceuticals
Production and Quality Control of Actinium-225 Radiopharmaceuticals

## Slide 9: Projects for Health Applications
Enhancing the Beneficial Effects of Radiation Processing in Nanotechnology
Radiation Effects on Polymer Materials Commonly Used in Medical Devices
Biomaterials for sustainable health care
Radiation Sterilization of Biomedical Materials and Biological Tissues

## Slide 10: Databases
Cyclotrons used for Radionuclide Production Database:
https://nucleus.iaea.org/sites/accelerators/Pages/Cyclotron.aspx
IAEA Radiopharmacy Database:
https://nucleus.iaea.org/sites/NAPCRadiopharmacyDB

## Slide 11: Seibersdorf Laboratories
Already existing facilities:
  dosimetry
  spectroscopy
  gamma facility
  plant breeding facility
Mobile Electron Beam

## Slide 12: Accelerator-based production of medical radioisotopes and radiopharmaceuticals

## Slide 13: Beginning of nuclear medicine
George de Hevesy (1885 -1966)
Notes: George de Hevesy (1885 -1966) was a Hungarian radiochemist and Nobel laureate, recognized in 1943 for his key role in the development of radioactive tracers

## Slide 14: Uses of RI in medicine: SPECT
Short-lived (hours) gamma emitters: mostly Mo-99, mostly produced in reactors

## Slide 15: Uses of RI in medicine: PET
Short-lived (minutes to hours) positron emitters: F-18, O-15, Ga-68,etc, commonly produced in accelerators on-site

## Slide 16: Uses of RI in medicine: targeted therapy
Alpha and beta emitters: for example Ac-225

## Slide 17: Uses of RI in medicine: brachytherapy
Brachytherapy – solution for localized cancers (breast, prostate, eye, etc)
Seeds (iodine-125, iridium-192, etc) are implanted in the tumor

## Slide 18: Valley of Stability
Proton-rich isotopes typically:
Undergo β+ decay or electron capture
Produced by accelerators
Neutron-rich isotopes typically:
Undergo β− decay
Produced in reactors

## Slide 19: “Start the ball rolling…”
1927: Lord Rutherford requested a “copious supply” of projectiles more energetic than natural alpha and beta particles:
“What we require is an apparatus to give us a potential of the order of 10 million volts which can be safely accommodated in a reasonably sized room and operated by a few kilowatts of power. We require too an exhausted tube capable of withstanding this voltage… I see no reason why such a requirement cannot be made practical.”

## Slide 20: Electrostatic accelerators - X-Ray tube
Old, simple, and reliable technology
Energy and current limit due to anode heating

## Slide 21: RF Linacs
RF linac: the particles are accelerated multiple times, so the particle energy is not limited by the accelerating voltage.
Notes: The beampipe is divided into sections, with a gap between each: an alternating voltage is applied to the plates. The applied voltage is at its maximum when the particles reach the gap between these drift tube sections and is zero when the particles are right in the center of a drift tube.

## Slide 22: Cyclotrons
In 1929 Ernest Lawrence proposed a modification to a linac: bend the tubes and apply a magnetic field to bend the ion’s path

## Slide 23: Size does matter!
11-inch → 27-inch → 60-inch (16 MeV) → 100 MeV?!
Relativistic limits!
Notes: Theoretician Hans Bethe disagreed… Bethe calculated the upper limit of the cyclotron was 20 MeV for protons. Protons traveling any faster would become noticeably relativistic, thus gaining in mass. The increase in mass would cause the particle to fall out of sync with the magnetic resonance condition.

## Slide 24: Synchrotrons
The Synchrotron maintains a fixed orbital radius while adjusting the magnetic field to contain the accelerated beam.
Pre-acceleration is necessary, usually with a linac
Notes: Variations in the magnetic field compensate for the increasing relativistic mass of particles during acceleration.

## Slide 25: Fluorine-18
Short half-life means the typical shelf life is minutes to hours
High energy radiation (511 keV) necessitates heavy shielding
Each batch provides only a handful of patient doses
Closed system - pre-sterilized components

## Slide 26: 18O(p,n) 18F
- Hundreds of cyclotrons worldwide (10-18 MeV)
- Liquid H218O → liquid solution of18F-fluoride ion
- Gas 18O2 gas → 18F–F2 gas

## Slide 27: Molybdenum-99/Technicium-99m
- SPECT imaging
- Tc-99m is the most commonly used medical isotope!
- Mo-99 (T1/2 = 6 days) → Tc-99m (T1/2 = 6 hours)

## Slide 28: Moly cow
Mo-99 (T1/2 = 6 days) → Tc-99m (T1/2 = 6 hours)

## Slide 29: Tc-99m crisis in 2009

## Slide 30: Mo-99 production with accelerators

## Slide 31: Actinium-225: milking Th-229
~140 mCi of Th-229 at the ORNL for the provision of Ac-225
DOE produces 700-900 mCi/year
Similar amounts in Europe (JRC Karlsruhe) and Russia (JSC IPP)
Additional Th-229 by irradiation Ra-226 in the HFIR ( potentially hundreds of mCi/year)
233U (T1/2 = 1.6×105 a) → 229Th (T1/2 = 7.9×103 a) → 225Ra (T1/2 = 15 d) → 225Ac
Notes: The United States Department of Energy (DOE) recovered approximately 140 mCi of thorium-229 (Th229) from legacy uranium-233 processing solutions in the 1990s and stores the Th-229 in four fractions (cows) in a hot cell at the Oak Ridge National Laboratory (ORNL) for the provision of actinium-225 (Ac-225).

## Slide 32: Actinium-225: spallation
Natural thorium targets are bombarded with 100’s MeV protons
Several facilities worldwide are capable
Ac-227 impurities!

## Slide 33: 225Ac: Production with protons or electrons
Handling of Rn-222 gas (alpha decay from Ra-226)
Separation of Ac from Ra target

## Slide 34: Summary
First thought: treatment and diagnosis
  X-ray units and medical linacs
  Production of radioisotopes and radiopharmaceuticals
However, other applications:
  Sterilization of drugs, vaccines, tissues, medical devices, etc
  Development of biomaterials
  Drug development
  ???

## Slide 35: AccConf 2026
Accelerators for Research and Sustainable Development: first in series took place in May 2022, next in June 2026!
https://www.iaea.org/events/accconf2026

## Slide 36: ISTR 2027
Next one is in April 2027!

## Slide 37: Thank you! v.starovoitova@iaea.org