## Slide 1: The HEPiX IPv6 Working Group
David Kelsey
WLCG GDB, CERN 14 Nov 2012

## Slide 2: Outline
Update since the Jan 2012 GDB meeting
IPv4 address status
HEP/WLCG site IPv6 readiness survey
IPv6 testing news
News from the USA
Future plans

## Slide 3: IPv4 Addresses
From Geoff Huston (http://ipv4.potaroo.net)
IANA Unallocated Address Pool (Global) Exhaustion happened: 03-Feb-2011
Regional (RIR) Address Pool Exhaustion Dates:
  APNIC: 19-Apr-2011 (Asia Pacific - happened)
  RIPENCC: 14-Sep-2012 (Europe - happened)
  ARIN: 16-Sep-2013 (North America)
  LACNIC: 15-Jun-2015 (South America)
  AFRINIC: 02-Sep-2019 (Africa)

## Slide 4: HEP Site IPv6 Survey
Questionnaire sent on 26 Sep 2012
Survey of all WLCG sites, but include other HEP sites too – please reply if not yet done so
  WLCG GDB & CB, HEPiX-users, lcg-rollout
Questions
  Is your site already offering connectivity, routing and naming services for IPv6 end systems (i.e. is your site already connected to the worldwide IPv6 network and ready to support IPv6 end systems)?

## Slide 5: IPv6 site survey (2)
If so, have you already enabled IPv6 on some (all?) of the systems you manage - please provide some details (e.g. "yes, our external web server is running dual-stack IPv4/IPv6")
If your site is not yet IPv6-ready are there plans for this? If so what are the timelines?
Does your site currently have problems with lack of IPv4 addresses? Or foreseen in the near future?
Are there other issues you are aware of? Or interesting work going on in this area?
Any other comments?

## Slide 6: IPv6 site survey (3)
42 sites replied to date, in 20 countries
  Europe plus USA, Canada, China, South Africa, Brazil
Q1: 15 sites are already IPv6 enabled
  Some others report that University is, but HEP is not
Q2: Applications enabled include DNS, web servers, email servers, CAs, wireless, windows domain, testbeds
  Two sites report extensive use of dual-stack
  Lots of end-systems enabled by default, e.g. Windows 7 and associated tunnels (& perhaps rogue Router Adverts)

## Slide 7: IPv6 site survey (4)
Q3: another 10 sites have plans for the future
  Usually within next 12 months
  Others say: no pressure, no need, other more urgent tasks, why rush?...
Q4: Two sites (South Africa, FZU) report problems with lack of IPv4 addresses now. CERN predicts possible problems in 2014
  Several note lots of growth from virtualisation
  “Would be good to have real network addresses”

## Slide 8: IPv6 site survey (5)
Q5 and Q6
  Concerns about IP Address Management
  Concerns about IPv6 security
  Memories of DECnet Phase V transition
    We succeeded there, we can do it again!
  Several concerns about applications, tools, middleware not being ready
  One site proposed a new simpler architecture for IPv6!

## Slide 9: Observations from survey
IPv6 is happening – working group should continue!
  End systems and core networks are ready
  Applications, tools and sites are not, but are working on it
  Cannot ignore IPv6
    E.g. need to manage IPv6 on Windows clients and look for RAs
Some evidence of IPv4 address shortage at sites
  But no great pressure reported
Quote from one country:
  “So far, there have been no reported requirements or requests from experiments or collaborations for IPv6”
“non notum requisitis ipv6 pro scientia”

## Slide 10: HEPiX IPv6 Testing
We have deployed a distributed testbed
  CERN, DESY, FZU, GARR, INFN, KIT and USLHCnet
  Should expand soon, e.g. UK joining
Connected to IPv6 and IPv4 networks
  IPv6-only/IPv4-only names also registered in DNS
  e.g. hepix-v6.desy.de & hepix-v4.desy.de
https://w3.hepix.org/ipv6-bis/doku.php?id=ipv6:testbed
Have tested several middleware components and tools, mainly in data management
EGI and EMI testbeds are testing other things
  E.g. Information systems and batch systems

## Slide 11: Tests for IPv6
Does the service break/slow down when used with IPv4 on a dual-stack host with IPv6 enabled?
Will the service try using (connecting/binding to) an IPv6 address (AAAA record), when available from DNS?
Will the service prefer IPv6 addresses from DNS, when preferred at the host level?
  Does this need to be configured?
  How?
Can the service fall back gracefully to IPv4 if needed?

## Slide 12: Data tests – summer 2012
Already reported that GridFTP and globus_url_copy can be made to work
FTS can be made to work
  see Francesco Prelz talk at HEPiX April 2012
Several FTS channels defined and used over IPv6
Successfully installed IPv6 DPM on several nodes
Successfully transferred data to a dual-stack DPM server over IPv6

## Slide 13: Software & Tools IPv6 Survey
An “Asset” survey is underway (BUT SLOW!)
  A spreadsheet to be completed by sites and the LHC experiments
  Includes all applications, middleware and tools
  Tickets to be entered for all problems found
If IPv6-readiness is known, can be recorded
Otherwise we will need to investigate further
  Ask developer and/or supplier
  Scan source code or look for network calls while running
  Test the running application under dual stack conditions

## Slide 14: IPv6 problems found
Problems include...
OpenAFS, dCache, UberFTP
FTS & globus_url_copy (but can be made to work)
MyProxy (now fixed)
ISC dhcp on Scientific Linux (Red Hat like) v5
ARNES/Slovenia – EGI testing
  No LRMS system works (ARC) – SLURM, Torque, PBS, …
Many IGTF CA CRLs not available on IPv6
netboot/dhcp/pxe
Work ongoing – lots not yet assessed (many storage solutions)

## Slide 15: IPv6 readiness *an example* we will maintain such a table with more details stored elsewhere
Component | Version
LFC | 1.8.3
DPM | 1.8.3
StorRM | 1.8.2
UI | 3.2.11-1
VOBOX | 3.2.15-1
WMS | 3.3.7
WN | 3.2.12-1
Works
Rebuild or reconfigure
Does not work
Unknown
Component | Version
Argus | 1.4.0
GridFTP | 
BDII | 1.0.2
CASTOR | 2.1.13-5
CVFMS | 2.0.13
dCache | 1.9.12
FTS | 2.2.8

## Slide 16: Recent news
CERN Tier 0 and NDGF Tier 1
  IPv6 peering established via LHCOPN
    For testing of dCache
IPv6 @ CERN going well
LFC being tested at GARR
  Also FTS V3

## Slide 17: News from the USA
Presentation at IPv6 WG 4th Oct 2012
  Phil DeMar (FNAL)
US Government mandate: Public facing services to support IPv6 by 30 Sep 2012
  But no enforcement element – certainly not yet complete
  DOE National Labs are not in scope (but have made good progress)
  Does not include scientific computing
  http://fedv6-deployment.antd.nist.gov/cgi-bin/generate-gov
  http://my.es.net/sites/ipv6
  Next steps: concentrate on client IPv6 issues
    Auto-config, tunneling, dual-stack, unique local addresses (ULA)

## Slide 18: IPv6 testing plans
CMS tests
  Install and test PhEDEx between several end points
LHCb tests
  Glasgow & RAL
  Test job submission and CVFMS
Ongoing data component testing
  dCache, STORM, CASTOR?, …
Merge HEPiX and EGI/EMI Testbeds
  Install BDII (just one top-level or also site BDII?)
Expand site resources
  Install WNs
  Install other Grid services
  Test WMS and batch systems
  using standard Grid installation

## Slide 19: Future plans
Continue WLCG/HEP site readiness survey
Continue asset survey and testbed/testing
Review status early in 2013
Produce plans for LHC LS1 and/or later
Need to perform tests on the production infrastructure
  involve WLCG Tier 1 centres
Plan several HEP IPv6 “Days” (for LS1?)
  turn on dual stack for 24 hours on production infrastructure and test/observe
Earliest date for production support of IPv6-only systems is (currently) Jan 2014
  Could well be later than this

## Slide 20: Further info
HEPiX IPv6 wiki
https://w3.hepix.org/ipv6-bis/
Working group meetings
http://indico.cern.ch/categoryDisplay.py?categId=3538

## Slide 21: Summary
MUCH work still to be done during the next year or three & effort is difficult to find
  Further volunteers welcome to join
  Please contact me
not able to support IPv6-only systems in WLCG before 2014 (at earliest – could be later?)
  Decision on timetable to be made during 2013
  And needs to be jointly made with EGI, NDGF, OSG etc.