## Slide 2
FCC damping ring circumference considerations
H. Damerau, H. Bartosik, I. Karpov
20/05/2025

## Slide 3
FCC pre-injector complex
Sources and linacs  damping ring at 2.86 GeV  high energy linac: 2.86 GeV to 20 GeV  booster  FCC collider
Paolo Craievich, Chamonix 2025

## Slide 4
Introduction
FCC requires flexible top-up filling schemes, e.g. to mitigate e-cloud, see Hannes’ slides
Assumptions:
  Injection possible into any bunch position in booster/FCC
  Damping ring damps multiple batches (four bunches spaced by 25 ns) simultaneously
Cog-wheeling between damping ring and booster/FCC
Impact on choice of damping ring size?
Number of batches orbiting at the same time in damping ring?
Consequences for pulsing the linacs?

## Slide 5
Damping ring operation
Multiple batches circulating simultaneously
Hannes Bartosik, FCC Week 2024
Paolo Craievich, Chamonix 2025 and Feasibility Study Report
FIFO principle
storage time ~95 ms

## Slide 6
Integer ratio of circumferences
Integer ratio, r = CFCC/CDR of circumferences
  Only r azimuthal positions can be reached
  Transfer possible at each turn of the FCC booster
  Displacement or cogging/rephasing in the damping ring by up to  180

## Slide 7
Rational ratio, r = CFCC/CDR = m/n of circumferences
  About n times more azimuthal positions can be reached
At expense of transferring only every n turns of booster
  ‘Jitter’ from zero to n turns  pulse linacs non-periodically
  Displacement in damping ring reduced to ~ 180/n
Rational ratio of circumferences

## Slide 8
Cogging applied for transfer between PS and SPS as injectors for LEP
Transfer of two sets of bunches with re-phasing in-between
Orbit displacement due to RF frequency ‘modulation’
Not suitable for low-emittance damping ring
Cogging during LEP era
114 MHz cavity tuner
10 KHz tuning range
B. J. Evans, et al., PAC87, p. 1901

## Slide 9
Fixed RF frequency schemes
Constant RF frequency in damping ring, booster and FCC
Coarse positioning of bunches by cog-wheeling
Fine positioning by displacing batches in damping ring
Clean solutions allow fRF,FCC = fRF,DR and 25 ns spacing
Assume hFCC = 12120  hRF = 121200/10  bunch position units
12120 = 23∙3∙5∙101 must be dividable by numerator of CFCC/CDR

## Slide 10
The closest circumference ratio options
Options close to present damping reference circumference: 373.46 m
Not many options in the relevant circumference range

## Slide 11
Flexibility of placing batches in damping ring
Inject each batch in the damping ring with pre-determined bunch position offset
Cog-wheeling then reaches final bucket in booster/FCC
Cogwheeling can reach every hDR/Denominator(CFCC/CDR)th bucket position
  For example: CFCC/CDR = 4040/17  hDR = 51  Every 3rd position reachable
Remainder must be set by displacing batches in damping ring
  Example sub-patterns: bbbbssk, sbbbbsk or ssbbbbk (k: kicker gap, 50 ns)

## Slide 12
How many batches do fit into the damping ring?

## Slide 13
Consequences for linacs
Damping ring  booster transfer cannot take place every turn
Cog-wheeling in correct only every Denominator(CFCC/CDR)th turn
Although average repetition rate can be 100 Hz, linacs must pulse non-periodically
Simplified model for time between two transfers/linac pulses
10 ms
n booster/FCC turns
Transfer linac pulse
Time
Preliminary
Example: CFCC/CDR = 4040/17
Random bucket positions

## Slide 14
(Preliminary) conclusion and outlook
Circumference of damping ring in present scheme
  Very much constrained by synchronization scheme
  Not much freedom also for number of batches
Two-step process: Cog-wheeling and pre-positioning in damping ring
Constant RF frequency and orbit in damping ring
Flexible filling scheme pre-calculable from source (bucket counting)
Reduced number of maximum batches in damping ring
Non-periodic pulsing of linacs
Flexibility of damping ring circumference? Range?
Consequences for linac design?
Alternative options?