## Slide 1: WP3 Proton Complex
23/05/2025

## Slide 2: Code benchmarking
Code Benchmarking is really needed (specially for compression). Which codes to use? how to benchmark?
3 main codes in used already by people in the collaboration:
  Xsuite (CERN, Fermilab, ESS) 2.5D/3D
  PyOrbit (SNS, Fermilab) 2.5D (2 methods) /1D (long)
  Simpsons (STFC) 2.8D
  Impact T (Fermilab) 3D code (boundaries)
Start from simple lattice
Sofia and I can start looking on what have been done after commissioning is over and we restart after summer some meeting on benchmarking (July)
Adaptive mesh (or a way to do it in the codes)

## Slide 3: From Shinji: Code benchmarking
Step 1: Set of tentative baseline parameters with relatively short discussions. One thing I want to fix a priori is the harmonic number. That should be 1 to avoid merging before the target.
Step 2: Benchmarking with available codes. I see that there are already three codes which are used. Xsuite (Sofia), PyOrbit (Austin) and Simpsons (Shinji).
Step 3: Start detailed study for each aspect of the design. We may need to double check whether all codes give similar answer for some critical parameters.
Step 4: Update the proton driver design from time to time.
Repeat Step 3 and 4 until we satisfy the design.

## Slide 4: Next Steps: Natalia
Accumulator/Compressor lattices and ideas
  Combine 2 rings in one? What do we need to look at. Pros/Cons
  High slip factor vs low slip factor?
  Do we need barrier bucket RF?
  How to achieve the voltage needed (2-4 MV) in the compressor at such low RF freqs? Feasibility today. How much real state in the ring is needed?
  Acceleration post-linac: what are the issues? can we estimate the effects on energy spread? How adiabatic it needs to be in order to work for us? Can this be tested anywhere?
Parametric scan of our baseline parameters needed in order to evaluate performance.
  Are the parameters too unrealistic? How to move forward?
  Ideas for changes? How to recover performance?
For the RF cavity length, I found that J-PARC main ring uses a MR cavity which can be both for a barrier bucket and single sinusoidal. The cavity length is 2087 mm and the total voltage is 60 kV (max) and 54 kV (operational). This gives ~30 kV/m. If 2 MV is required, the real estate space for the cavity including flange and everything is 37 m. On a test bench, 50 kV/m is already achieved so that 20 m could be also possible in the near future.
Measurements, measurements, measurements….

## Slide 5: Proposed Experiements

## Slide 6: Next Steps: Shinji
Lattice questions:
  A single or separate ring for accumulation and compression.
  Large or small slippage factor.
  Zero or finite dispersion at the straight.
  Barrier bucket or alternative way (e.g. isochronous ring) to keep a short bunch.
  Single sinusoidal RF or with higher harmonics to increase the linear region of the RF waveform for compression.
  Optimum initial emittance
  Optimum initial momentum spread
  Optimum initial bunch length
  Optimum rotation time (I realised a high Q RF cavity needs time to ramp up its voltage. A few 10 turns rotation may not be compatible if we assume one ring).
  Acceleration post linac is feasible. Is Jeff's idea of 3 in 1 ring feasible.
  Can induction acceleration be an option of post linac acceleration?
  Space charge, beam loading and coherent instabilities.
In parallel, possible demonstration using an existing accelerator should be considered. I think observations we expect from the real accelerator is similar to what we try to get from code benchmarking, for example, bunch length as a function of beam intensity and initial momentum spread.
Beam loading in RF specially in the compressor ring might be an issue. How similar the experiments can probe on terms of beam loading and if they can give us some input for the issues the muon collider will face.

## Slide 7: More questions
Bunch merging (if impossible to avoid):
  Target constraints: one single bunch on target with 5 rms mm round and 2 ns rms long. The beam will be tilted with respect to the center of the target (improve yield). Cannot deliver multiple bunches with different angles. I have no constraint on divergence but it will come. From MAP up to 10 mm mrad (unnormalized) it was acceptable.
  Food for thought: transverse or longitudinal recombination, pros and cons of each. Avoid recombination at all costs?
  Do the bunch merge in the accumulator?
Do we need to worry now about injection now, or can we wait longer? Foil vs laser option -> we forget foil for now and focus on laser injection