## Slide 1: p-Pb MD plans J.M. Jowett, R. Alemany, P. Baudrenghien, R. Versteegen and many others
Preliminaries?
  RF rephasing test with protons, P. Baudrenghien Radial loops for two p beams separately, R. Steinhagen
MD Block 4, November 2011
  Establish circulating Pb as Beam 2 (1 bunch).
  Establish circulating p as Beam 1 with 100 ns filling scheme, 10% of Nominal bunch intensity.
  Separate RF frequencies in the two rings.
  Inject one Pb bunch into Beam 2, measure many beam parameters, especially lifetime, emittance.
  Study measures (transverse damper, tune changes, etc) to deal with any intensity limits, emittance blow-ups, etc.
  If time, attempt ramp of Pb.
  If still time, attempt ramp of two beams with unlocked RF systems.
  Dump (no squeeze or collisions).
  If even more time, repeat with higher p intensity, possibly more Pb bunches.

## Slide 2: After MD Block 4
Ion beam setup of 4-6 Nov
  Inject, ramp, squeeze for Pb-Pb physics
Technical Stop
  Discuss, adapt plans, no. of bunches, etc.
Feasibility test p-Pb in week of 14 Nov
  Inject and ramp both beams
  Rephase RF for proper collision points
  Squeeze, collide (probably another fill)