## Slide 1: Design of FFA magnet for LhARA
Ta-Jen Kuo
Supervisor: Jaroslaw Pasternak, Jean-Baptiste Lagrange
Imperial College London, STFC
18/09/25

## Slide 2
Content
What is LhARA
Target field
Magnet and coil geometry
Optimisating of current
Adjusting fringe field
Final tune result

## Slide 3
What is LhARA

## Slide 4
Laser target: Up to 15 MeV proton beam at 10Hz
FFA: Variable extraction energy 15-127 MeV
LhARA
Laser-hybrid Accelerator for Radiobiological Applications, dedicated to radiobiology research

## Slide 5
Combine beams of different energy to
create a spread out Bragg peak
Injection energy and total B field
varied for different extraction energy
Verify behavior at 2 different extraction
energies 127 Mev and 57 MeV.
Variable extraction energy

## Slide 6
2.Target field

## Slide 7
, k(r)
Scaling law:
Instead we make the integrated field scaling
This is the same as making the average B field scaling if it’s a singlet.
Slightly different for doublet (FETS-FFA magnet talk tomorrow)
To first order the horizontal tune roughly constant
Vertical tune variation will need to be investigated later on
Integrated scaling law

## Slide 8
3.Geometry of magnet and coils

## Slide 9
Spiral angle 53.9 degrees
10 fold symmetry
Full gap of iron 96 mm
Field gradient generated by radially dependent trim coils, each with a different current setting
Clive Hill, Daresbury lab
Geometry of the magnet

## Slide 10
Geometry of the clamps
Clamps placed at constant angle away from the pole
Connected magnetically with the pole improves efficiency

## Slide 11
The match the scaling law, the constant radius area should be as large as possible
The return part shaped accordingly to the pole to minimize space taken up
Geometry of a trim coil
Modelled in Opera 3D via Metaopera1
1 (T. Planchet, H.W.Koay, J-B Lagrange and T.J.Kuo)

## Slide 12
Cross the pole face at different radius, returns stack longitudinally
Two vertical layers slot into each other
Geometry of trim coils stacked together
Clive Hill, Daresbury lab

## Slide 13
4.Optimisation of currents

## Slide 14
127 MeV extraction energy: BL0 : 1.44 Tm , r0 :3.477m, k : 5.23
Oscillation in residuals due to the discretization of trim coils
Field error, 127 MeV extraction energy

## Slide 15
Part of the pole reaching 2.66T
Flat top of field distorted at higher radii due to
saturation and will have an impact on the tune
Saturation level
(Plotted in a coordinate that undoes the spiral angle)

## Slide 16
Setting BL0 to of the original value
57 MeV extraction energy : BL0 : 0.96 Tm , r0 :3.477m, k : 5.23
Field error, 57 MeV extraction energy

## Slide 17
Ring tune
127 MeV extraction energy
57 MeV extraction energy
Some variation of horizontal
tune at 127 MeV
Vertical tune variation to be
minimized by shaping the field
clamps

## Slide 18
5. Adjusting fringe field

## Slide 19
Spiral angle of the magnet may not be the same as the spiral angle of the B field.
Calculate the integrated average gradient of the field to define magnetic field boundary
, =
Spiral angle =
For entry and exit sides of magnet separately
Spiral angles

## Slide 20
This describes the fringe field length of the magnet at the entrance and exit separately.
The larger C1 is the shorter the fringe field
Tanh model of fringe field
: Gap height of the pole
: Max B field
: Spiral angles from the previous equations
to fit
: Describes the fringe field length
: Describes the effective field boundaries

## Slide 21
Vary the clamp height to achieve better tune spread. Iterations were done with tune
spread as the target.
Clamp height optimisation

## Slide 22
Clamp shaped with tune as target
Fringe field parameters calculated for sanity check
Comparing the coefficients before and after clamp shaping
Fringe field parameters, 127 MeV extraction energy

## Slide 23
Ring tune, 127 MeV extraction energy
(Not all the resonances plotted are systematic)

## Slide 24
Fringe field parameters, 57 MeV extraction energy

## Slide 25
Ring tune, 57 MeV extraction energy

## Slide 26
Final results

## Slide 27
Conclusion
+/- 0.035 variation in k achieved with the trim coils set up
Clamp shape optimized to reduce vertical tune variation at 127 MeV extraction energy
Working tune for two different extraction energies (57, 127 MeV) stay at the same point
Tune spread in both cases are small enough to avoid any resonance up to fourth order