## Slide 1: Procurement of Nb3Sn strand for coils assembled at CERN
A. Ballarino, L. Bottura, L. Oberli
11 T Dipole Meeting, 4/10/2011

## Slide 2
Status of R&D Development - Preamble
RRP® : Strand  = 0. 7 mm
NbTa 108/127
Filament   46 µm
RRR > 60
Jc(12 T) > 2650 A/mm2
Non-Cu% = 45 %-49 %
Strand twist pitch = 12-16 mm
“Standard” wire:
PIT : Strand  = 1 mm
NbTa 192
Filament   50 µm
RRR > 150
Jc(12 T)  2400 A/mm2
Cu-Non Cu ratio = 1.25
Strand twist pitch = 24 mm

## Slide 3
Specification for “final” wire – Price Enquiry June 2011:
Status of R&D Development - Preamble
Strand  = 0. 7 mm
Filament  < 30 µm
Strand twist pitch = 17 mm
RRR > 100
Ic(12 T) > 474 A
Jc(12 T) > 2650 A/mm2
n(15 T, 4.2 K) > 30
Development aiming at reaching targets of Jc, RRR and filament size as needed
for an accelerator-type conductor

## Slide 4
What do we have today ?
27 km of “standard” RRP® 108/127 – 46 µm filament size – ordered in June 2010 and delivered
in July 2011. Qualification of the strand in process
In addition:
20 km of “standard” RRP® 108/127 – 46 µm filament size.
Delivery expected by December 2011/January 2012
1 km of PIT, 0.7 mm  and 44 m filament size, Jc  2500 A/mm2 – from a development billet
processed by Bruker at the request of CERN in 2010.
To be delivered in the next coming weeks (first delivery of 0.7 mm diameter PIT strand)
 47 km of strand available by January 2012

## Slide 5
Answers to Price Enquiry DO-26957/TE
(Sept 2011)
Request for 45 km of strand addressed to OST, Bruker and Luvata
Luvata - Declined
OST - Offer for 45 km for strand of which:
30 km with filament diameter of about 36 m (meeting Jc and RRR specification)
15 km with filament diameter of about 32 m (R&D development, best effort Jc and RRR)
Bruker – Offer for 45 km of strand (offer in negotiation):
45 km with filament size of about 44 m (meeting Jc and RRR specification)
NB Not yet a “standard” strand, but still a development product
+ 90 km of strand available by November 2012
Tot  137 km of strand by November 2012

## Slide 6
Strategy for procurement of Nb3Sn strand
Future Orders
Large quantity of “standard”
qualified conductor for
prototype coil production
Smaller quantity of R&D
conductor developed with the goal
of meeting the “final” Jc, RRR and
filament size requirements

## Slide 7
Strategy for procurement of Nb3Sn strand
Proposal: by beginning 2012: call for tender for the procurement of 200 km of strand
– “standard conductor”- to be delivered by end 2012. Filament diameter: 40-50 µm
Tot  337 km of strand by end 2012
To be followed by call for tenders for the procurement of the strand for the series
production

## Slide 8
Oct 2011
27 km
Jan 2012
20 km
Nov 2012
2*45 km
Dec 2012
200 km
100 km
200 km
47 km
137 km
337 km
Total length