## Slide 1
LDG, CERN, June , 2025
Muon Collider
D. Schulte, S. Stapnes
On behalf of the International Muon Collider Collaboration
Funded by the European Union (EU). Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the EU or European Research Executive Agency (REA). Neither the EU nor the REA can be held responsible for them.

## Slide 2: ESPPU Submission Content
2
Assessment
Present green field designs and technologies
International collaboration
Parameters, lattice and component designs, beam dynamics, cost, …
R&D plan
Including scenarios and timelines
Magnets, muon cooling, detector, …
The muon cooling technology and test facility is critical for this
Implementation Considerations
Civil engineering studies/considerations (for CERN and for FNAL)
Cost and power consumption scales
Parameter tables, scaled from green field
  Will develop detailed lattice designs after ESPPU
Schedule (strongly linked to R&D Plan)
Aim for initial stage by around 2050
Back-up document (406p, 450 signatories)

## Slide 3: Site Specific Designs
Started studies for concrete site at CERN and Fermilab, looks very promising
Fermilab:
One RCS in Tevatron tunnel,
three RCS in one site-filler tunnel
CERN:
One RCS in SPS and two in LHC
Construct facility on CERN land
Adjusted parameters (3.2 and 7.6 TeV, 10 TeV maybe possible)

## Slide 4: Key Parameters
4
Param. | Unit | Site independent |  | CERN 2 tunnels |  | CERN 1 tunnel | 
Sqrt(s) | TeV | 3 | 10 | 3.2 | 7.6 | 3.2 | 7.6
L/IP | 1034 cm-2s-1 | 1.8 | 17.5 | 2 | 10 | 0.9 | 7.9
Int L | ab-1 | 1 | 10 | 1 | 10 | 1 | 10
Accumulation time | years | 2+2.8 | 2+2.9 | 2+2.5 | 2+5 | 2+5.6 | 2+6.3
C | km | 4.5 | 11.4 | 4.8 | 8.7 | 11 | 11
Bdipole | T | 11 | 14 | 11 | 14 | 4.8 | 11
Collider dipole technology |  | Nb3Sn | HTS | Nb3Sn | HTS | NbTi | Nb3Sn or HTS
Accumulation time: Time to obtain the integrated luminosity with two IPs.
Ramp-up over the first three years 5%, 205%, 70% of nominal.

## Slide 5: Timeline and R&D Programme Proposal
Timeline is driven by R&D
Most ambitious example to define R&D programme priorities
Assumes firm commitment to enable the muon collider as next flagship after HL-LHC
Other options
In Europe after a higgs factory
In the US to become leader at the energy frontier
Decision on demonstrator
Initial final demonstrator

## Slide 6: LDG Mid-term Review – Feb. 2025
Recommendations:
Develop a Start-to-End Performance Simulator: Create a comprehensive simulation framework to assess the robustness of key parameters, including luminosity, cost, and energy consumption. This tool should enable performance optimization, sensitivity analysis, and risk mitigation across the entire collider complex.
-> this is (one of) the most urgent and crucial parts of the R&D plan (see slide 10)
Define and fund a High-Field HTS and RF Development Strategy: Establish a clear roadmap for the development of the high-field HTS magnet and the RF systems, including well-defined specifications and performance targets. Securing dedicated funding is essential to advance these critical technologies.
-> also for this point, see R&D plan below - slide 14 (and 15 for impact outside HEP)
Conduct an Independent Review of Scope, Schedule, and Costs: An urgent, independent evaluation is needed to assess the overall scope, timeline, and budget of the Muon Collider R&D program for the period 2026-2036. This review will be crucial to ensure that funding requests for this R&D phase are well-justified and aligned with project objectives.
-> Initial review by our International Advisory Committee next week (see slide 9), more details in future reviews
Found good progress for Roadmap implementation
Estimated that 75% of Roadmap goals have been achieved

## Slide 7: R&D Plan Deliverables and Resources

## Slide 8: R&D Plan Deliverables and Resources
Totals:
Duration 10 years
Accelerator: 300 MCHF material, 1800 FTEy
Detector: 20 MCHF material, 900 FTEy

## Slide 9: R&D Plan Review and Refinement
Review by the International Advisory Committee (IAC), 17.6 and 20.6 (each day: 13:30-16:00)
Beyond this review further work by R&D task force (leaders: Emilio Nanni (SLAC), Federico Meloni (DESY)) to refine priorities and to harmonise resource requests
Additional experts confirmed: Pierre Vedrine, Stephen Gourlay, Lyn Evans, Alessandro Gallo, Barbara Dalena

## Slide 10: Start-to-end Model
This is an important part of the proposed R&D plan
Due to resource limitations we had to set priorities in the LDG Roadmap:
Design of the collider areas that were considered challenging and contained Critical Technology Elements
Address the key challenges such as neutrino flux and bema-induced detector background
Development of missing critical simulation tools
Development of realistic performance targets for the components
As promised at the review now available:
Initial cost model
Initial power consumption model
With increased resources can:
Design missing connecting systems
Further improve existing system designs
Refine cost and power consumption model
Optimise for risk and cost
Are introducing a formalized configuration management for the overall optimisation

## Slide 11: Cost and Power Scale
Design of many collider areas/components has progressed
but some uncertainties remain
No overall optimisation
HTS cost model
Cost is mixture of bottom-up (e.g. fast-ramping magnet systems) and based on scaling from known cost (e.g. from ILC for superconducting 1.3 GHz cavities)
Power estimate is also based on conceptual designs and scaling from know components, e.g.
Simulations of fast-ramping magnets and power converter
Detailed scaling for RCS cavities

## Slide 12: RF and High-Field HTS Development Strategy
For the RF development:
The key challenge is the normal conducting RF in the muon cooling section
Attempt to remain within state of the art for the other parts
This might change once the commitment to a muon collider becomes stronger
This is therefore a part of the muon cooling technology development
Had good discussions with the LDG RF panel
SLAC is investing into an RF test stand
Also efforts at INFN and in the UK
A clear Roadmap for the development of HTS magnets exists and funding needs to be secured
The LDG should play an important role
The HTS solenoid technology is of high importance for societal applications
We can profit from developments driven by society
We can contribute to society
We see that this is leading to additional support for R&D
The power converter for the fast-ramping magnets are of high relevance for society

## Slide 13: Muon Cooling Demonstrator
Key conclusions:
Installation of demonstrator at CERN appears possible with limited cost (O(10kW)) proton beam
Expensive solution with O(80 kW) would allow future upgrade
Fermilab has approved a study
RF test stands are critical and urgent
Consistent with implementation timeline
Achieved:
Defined the scope and concept, made initial cost estimate, investigated three promising locations at CERN
Staged timeline to implement demonstrator
SLAC is moving forward building a 3/1.3 GHz test stand
Challenge:
Demonstrate muon cooling technology in stages
Critical for timeline
Construction
Project
preparation
R&D plan

## Slide 14: Magnets
14
Normal-conducting RCS pulsed magnets
HTS pancakes 4 mm tape
HTS final cooling solenoid mechanical design
First HTS winding tests
Target HTS solenoid
Achieved:
Systematic dipole/solenoid performance prediction (LTS and HTS)
  Aperture, field, cost, stress, loadline, protection, …
HTS solenoid designs (6D cooling, final cooling, target)
Normal-conducting fast-pulsed dipoles (HTS as alternative)
Technically limited R&D timeline developed
REBCO, 20 K
MuCol HTS conductor
Operating current: 61 kA
Did adjust collider ring field
Key conclusions:
Design work is basically done
Opportunity to ramp up effort (engineering designs, building models, …)
With sufficient resources HTS solenoids and Nb3Sn dipoles could be ready for decision in 10-15 years, consistent with implementation timeline
HTS dipoles likely take longer

## Slide 15: R&D impact examples
Fusion for Energy (ITER EU Domestic Agency)
  Framework agreement and first addendum in final negotiation
  Contribution to the design of the HTS target solenoid, relevant to the central solenoid of DTT
EUROFusion (next step European fusion reactor)
  Framework agreement signed in 2023, first addendum signed in 2024
  Contribution to the design of the HTS target solenoid, relevant to the magnets of a Volumetric Neutron Source proposed as next step in the European fusion strategy
Gauss Fusion (one of the leading EU fusion start-ups)
  Consultancy agreement signed in 2023
  CERN contribution to the design of the LTS/HTS GIGA stellarator magnets, based on advances in the HTS target solenoid
ENI (oil and gas energy giant)
  Framework agreement and first addendum signed in 2024
  Collaboration on the conceptual design and project proposal for the CERN construction of a large bore HTS solenoid (20@20 model coil) relevant to the muon collider and fusion
Infineon Technologies Bipolar (world leader bipolar high-power semiconductors, focus on green grid)
  IFAST-2 proposal to INFRA-2025-TECH-01-02 (CERN, INFINEON, PSI)
  Proposal of fast pulsed power cell + magnet system sent to IFAST-2 coordination for ranking at TIARA
  Industrial interest in rapidly pulsed and large energy/power supplies
Modified from L. Bottura

## Slide 16: MuCol Mid-term Review
With an external reviewer
Very good presentations of the workpackage leaders
Technical progress was considered very good
Managed to submit to ESPPU in spite of earlier deadline
Some administrative details needed to be corrected, e.g.
New deliverable (MuCol policy brief document) had to be written
Explain why one University is late with hiring a post doc
…
Comment from CERN EU office: That went better than normal…
All comments should be all solved
Main comment for improvement: Target policy makers more strongly

## Slide 17: US Development
National Academy of Science Recommendation has been published:
Recommendation 1: The United States should host the world’s highest-energy elementary particle collider around the middle of the century. This requires the immediate creation of a national muon collider research and development program to enable the construction of a demonstrator of the key new technologies and their integration.
A collider with approximately 10 times the energy of the Large Hadron Collider (LHC) is crucial
for addressing the big questions of particle physics and making discoveries. A 10-TeV muon collider on
the Fermi National Accelerator Laboratory (Fermilab) site would have similar discovery reach as a 100-
TeV proton collider. A muon collider combines the physics advantages of an electron-positron and a
proton-proton collider, with a much smaller size. A machine that collides unstable elementary particles
has never been attempted before and requires significant research and development (R&D), international
coordination, and a demonstrator project to establish its feasibility. Developing a U.S.-hosted muon
collider—an unprecedented machine requiring considerable research, development, and a feasibility
demonstrator—would solidify U.S. leadership in particle physics and drive accelerator innovation. The
“middle of the century” timeline reflects the project’s inherent complexities, which are elaborated in
Chapter 2, and underscores the need for global coordination.
Several grants have been secured in the US to support the muon collider R&D

## Slide 18: IMCC Partners
18
IEIO | CERN
FR | CEA-IRFU
 | CNRS-LNCMI
 | Ecoles des Mines St-Etienne
DE | DESY
 | Technical University of Darmstadt
 | University of Rostock
 | KIT
UK | RAL
 | UK Research and Innovation
 | University of Lancaster
 | University of Southampton
 | University of Strathclyde
 | University of Sussex
 | Imperial College London
 | Royal Holloway
 | University of Huddersfield
 | University of Oxford
 | University of Warwick
 | University of Durham
 | University of Birmingham
 | University of Cambridge
NL | University of Twente
FI | Tampere University
 | HIP, University of Helsinki
LAT | Riga Technical University
CH | PSI
 | University of Geneva
 | EPFL
 | HEIA-FR
BE | Univ. Louvain
AU | HEPHY
 | TU Wien
ES | I3M
 | IFIC/CSIC
 | ICMAB
China | Sun Yat-sen University
 | IHEP
 | Peking University
 | Inst. Of Mod. Physics, CAS
 | University of CAS
KO | Kyungpook National University
 | Yonsei University
 | Seoul National University
India | CHEP
IT | INFN
 | INFN, Univ., Polit. Torino
 | INFN, LASA, Univ. Milano
 | INFN, Univ. Padova
 | INFN, Univ. Pavia
 | INFN, Univ. Bologna
 | INFN Trieste
 | INFN, Univ. Bari
 | INFN, Univ. Roma 1
 | ENEA
 | INFN Frascati
 | INFN, Univ. Ferrara
 | INFN, Univ. Roma 3
 | INFN Legnaro
 | INFN, Univ. Milano Bicocca
 | INFN Genova
 | INFN Laboratori del Sud
 | INFN Napoli
Mal | Univ. of Malta
EST | Tartu University
PT | LIP
SE | ESS
 | University of Uppsala
CA | Université Laval
US | Iowa State University
 | University of Iowa
 | Wisconsin-Madison
 | University of Pittsburgh
 | Old Dominion
 | Chicago University
 | Florida State University
 | RICE University
 | Tennessee University
 | MIT Plasma science center
 | Pittsburgh PAC
 | Yale
 | Princeton
 | Stony Brook
 | Stanford/SLAC
 | …
DoE labs | FNAL
 | LBNL
 | JLAB
 | BNL
Brazil | CNPEM
Signed MoC (61), requested MoC, contributor

## Slide 19: Conclusion
Excellent technical progress has been made
Supported by LDG and MuCol reviews
An R&D programme for ten years has been defined and will be refined in the coming months
Further refinement and prioritization is ongoing
Will focus on preparing its implementation
Will continue and further increase effort to secure resources
Identifying partners from particle physics and society
Very strong recommendation in the US for a muon collider
Creates collaboration and competition
Initial grants have been obtained in the US
Continued strong support from LDG is important

## Slide 20: Reserve

## Slide 21: Magnet R&D Impact
L. Bottura

## Slide 22: European Accelerator R&D Roadmap
22
http://arxiv.org/abs/2201.07895
Reviews in Europe and the US found muon collider promising
Requires important innovation
European Strategy for Particle Physics Update (ESPPU) supported muon collider R&D in 2020
CERN Council charged Laboratory Directors Group (LDG) to develop Accelerator R&D Roadmap
Directors of institutes, e.g. INFN Frascati, PSI, DESY, RAL, CERN, …
LDG formed five panels, one on Muon Collider
Muon Collider panel developed an R&D Roadmap with the help of the global community until end of 2021

## Slide 23: Muon Collider Roadmap CT
23
Short, intense proton bunch
Protons produce pions which decay into muons which are captured
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
- Proton driver
bunch compression
- Graphite target
- Target solenoid
- Muon cooling design
- 6D cooling solenoids
- 6D cooling RF cavities
- Final cooling solenoids
- Pulsed magnets and
power converters
- RCS RF system
- Collider ring dipoles
- Final focus quadrupoles
- Machine-detector interface
Identified and prioritized with community
Other areas need now also to be addressed
(some work started)

## Slide 24: MuCol Timeline
LDG anticipated input to next ESPPU by 2026
The ESPPU has been advanced to early 2025
2026
2024
2025
2023
2027
ESPPU submission
ESPPU recommendation

## Slide 25: Muon Cooling Challenges
25
Energy loss = cooling
Multiple scattering = heating
High field solenoids minimise beta-function and impact of multiple scattering

## Slide 26: ESPPU Submission March 2025
Collaboration produced ESPPU input:
Short, ten-page report (10p)
Addendum to answers specific questions from ESPPU (18p)
Back-up document (406p, 450 signatories)
  Assessment of collider status based on progress of R&D
  R&D Plan
  Final polishing is ongoing, you Urgently sign up to support

## Slide 27: IMCC International Muon Collider Collaboration
27
Roadmap: http://arxiv.org/abs/2201.07895
Develop high-energy muon collider as option for particle physics:
Implement globally defined accelerator R&D roadmap (2022) to justify CDR phase
Mid-term roadmap review found 75% of goal achieved
Provided ESPPU with
Assessment of muon collider concept, technologies and work progress
An R&D plan for the next 10 years
Implementation considerations (including site, timeline, …)
Back-up document (406p, 450 signatories)
Will inform other strategy processes
Focus on feasibility of 10 TeV with 10 ab-1 (site independent)
Explore initial stage by 2050, maybe around 3 TeV with 1 ab-1 or lower luminosity 10 TeV
Explore implementation at specific sites reusing infrastructure
Param. | Unit | 3 TeV | 10 TeV
L/IP | 1034 cm-2s-1 | 1.8 | 17.5
Int L | Ab-1 | 2.2 | 1.8
fr | Hz | 5 | 5
C | km | 4.5 | 11.4
Bdipole | T | 11 | 14
Collider techn. |  | Nb3Sn | HTS

## Slide 28: Muon Cooling Technology
MAP proved gradient
Initial RF designs
More RF design ongoing
Challenges:
NC RF cavities in magnetic field (30 MV/m)
HTS magnets (up to 40 T in final cooling)
Bright beam hard on absorbers and windows
  Can evaporise liquid hydrogen
MuCool demonstrated >50 MV/m in 5 T
H2-filled copper
Be end caps
40 T final cooling solenoid conceptual designs exist
55 T might be possible
Key conclusions:
Ready to ramp-up effort, in particular prototyping and experimental work, also beamdynamics
First window tests performed with protons
Use of H2 gas where required

## Slide 29: Muon 6D Cooling Cell
Key conclusions:
Key challenge is force from magnetic field
Concept to connect flanges developed
Iterations to improve overall and components design also considering beam dynamics is required/ongoing
Conceptual design ready in a few months
Achieved:
Cooling cell engineering design almost ready
Solenoid models for use in beamdynamics optimisation
Challenge:
Integrated 6D cooling cell
HTS solenoid designs
STEP 6: Connect 6x Coils with pins (half Cold Mass)
L. Rossi et al.
L Bottura et al.

## Slide 30: RCS Designs
Key conclusions:
1.3 GHz TESLA-type cavities work
Emittance transport is OK
Need to connect to initial linacs
Achieved:
Lattices for all site independent RCSs
  Strong synchrotron motion
  Including hardware specifications
Beam propagation through complex works
Challenge:
Uses fast-pulsed normal magnets
5 Hz pulses of O(1-10ms)
6-35 km circumference
Cost and power efficient acceleration
High bunch charge
Maintain beam quality
Lattice: A. Chance et al.
Long. dynamics: H. Damerell et al.
RF: Alexej Grudiev et al.
Power converter: F. Boattini et al.
Magnets: L. Bottura et al.

## Slide 31: Fast-ramping RCD Dipoles
Key conclusions:
High recovery efficiency for RCSs (98-99%)
Ready for experimental optimization/models/protoypes
Achieved:
Conceptual design of magnets and power converters
Optimised design together with RF
Power converters can switch sign of magnets without changing direction of voltage on capacitors
Challenge:
Fast ramping normal magnets (1-10 ms) with efficient energy recovery in power converter (200 MJ stored in magnets)
RCS | E [J/m] | Eiron [J/m] | Ecopper [J/m] | Loss [%] | P [MW]
SPS 1 | 5447 | 10 | 52 | 1.1 | 1.9
LHC 1 | 5678 | 9.2 | 80.6 | 1.6 | 12.8
LHC 2 | 5752 | 63.4 | 298 | 6.3/2 | 26.6
Energy in magnets, losses per cycle and total power at 5 Hz including cooling
Power converter: F. Boattini et al.
Magnets: L. Bottura et al.

## Slide 32: Collective Effects
Key conclusions:
Impedances in RCSs and collider ring can be taken care of by design
Beam-beam can be handled by 20 turn feedback
Resistive wall in muon cooling is OK
Further key detailed studies: beam loading, longitudinal and transverse space charge in 6D cooling, impedance of cooling absorbers
Achieved:
Initial studies for proton complex
Assessed impedances (beam screen and RF cavities) in RCSs and collider ring
  Studying counter-rotating beam impedance
Studies started on muon cooling
Goal:
Identify collective effects intensity bottlenecks

## Slide 33: Lattice Designs
33
Lattice design is progressing well

## Slide 34: Collider Ring Magnets
Challenge:
High-field collider ring magnets with large aperture
Key conclusions:
Dipoles appear feasible:
  NbTi at 4 K, 4.8 T, 16 cm aperture
  Nb3Sn at 4 K, 11 T, 16 cm aperture
  HTS at 20 K, 14 T, 14 cm aperture
Quad in dipole best combined solution
Experimental programme is now essential
Achieved:
New method developed to identify field limit, depending on technology, temperature, cost, aperture, considering current, stress and protection (quadrupoles, dipoles, combined function magnets)
Different conceptual dipole designs (block coil, cos-theta)
Combined function design ongoing

## Slide 35: Site
Challenge:
Obtain negligible neutrino flux
Achieved:
Detailed modelling
First good orientation found
Mover system concept
FLUKA and RP studies
Mover system design
Arc mitigation concept
Site study at CERN for experimental insertion
Key conclusions:
Are close to a solution
More work to be done
Fermilab site study
t1
t2

## Slide 36: Physics and Detector Concepts
Two detector concepts are being developed
MUSIC
(MUon Smasher for Interesting Collisions)
MAIA
(Muon Accelerator Instrumented Aperatus)

## Slide 37: Beam-induced Background
Challenges:
Muon decay can give important background
40 000 muons/m/bunch crossing
1/3 of energy in electrons and positrons
Detailed studies with FLUKA
Conclusions:
Can do the physics
  Also thanks to HL-LHC technology
But room for improvement
Radiation level similar to HL-LHC
Achievements:
Two conceptual detector designs
Simulation studies with background also from machine
Studies of different lattices
Reconstruction algorithms
Physics studies

## Slide 38: Proton Complex
Challenge:
2 MW, 5 GeV, 5 Hz,
5 x 1014 protons/pulse
Proton pulse accumulator and compressor rings
Achieved:
Accumulator and combiner ring lattices
First collective effects studies promising
One or two bunches in compressor, to be decided
Key conclusions:
Can compress 2 MW, 5 GeV proton beam to two 2 ns bunches, then merge them
  Optimisation in compressor ring for collective effects ongoing
For 4 MW need 10 GeV beam
Cool beamline to avoid ion loss from black body radiation

## Slide 39: Target
Achieved:
Initial 2 MW graphite target conceptual design, pion yield optimised
HTS solenoid and shielding concept developed
Study of proton removal ongoing
Challenges:
2 MW, 5 Hz, 400 MJ/pulse target
Can we replace mercury with graphite?
Key conclusions:
Yield, magnet shielding, target stress, cooling, radiation are OK
Components survive 2 MW beam
Higher power alternatives to study:
  Graphite
  Liquid metal

## Slide 40: High-field Magnet Technology
NbTi (niob-titanium, operating at 2-4 k)
is standard, used in LHC limited to O(8 T)
Nb3Sn (niobium-tin, operating at 2-4 K)
Can reach O(16 T)
Difficult technology, needs to mature further
Expensive
Used in some points for HL-LHC
Foreseen for FCC-hh also in arcs
HTS (high-temperature superconductor, operating up to 20 K)
Different options exist, e.g. REBCO
In solenoids > 30 T demonstrated
Still expensive and technology challenges
Applications in other fields, e.g. medical, fusion reactors, power generators for wind energy, engines, …
Cut through a cable with superconductor embedded in copper, so some remains conductivity in case of a quench
REBCO Tape
Superconducting magnets reach highest fields, three main technologies for the cables

## Slide 41: Magnets
41
20 T large aperture target solenoid
6D cooling solenoids
- Pulsed magnets and
power converters
14 T, 14 cm HTS collider ring dipoles
40 T small aperture final cooling solenoids

## Slide 42: Muon Cooling Lattice Design
better
better
Previous design (MAP)
Goal
Achieved
Challenge:
Novel, complex lattice with cavities and absorbers in solenoids
Achieved:
Much improved lattice design
Improved simulation tools: BDSIM and RFtrack
Key conclusions:
Can in principle reach or exceed performance target
Much improved longitudinal, may be useful for collider ring
Study of collective effects important

## Slide 43: Muon Cooling Technology
MAP proved gradient
Initial RF designs
More RF design ongoing
Challenges:
NC RF cavities in magnetic field (30 MV/m)
HTS magnets (up to 40 T in final cooling)
Bright beam hard on absorbers and windows
  Can evaporise liquid hydrogen
MuCool demonstrated >50 MV/m in 5 T
H2-filled copper
Be end caps
First window tests performed with protons
Use of H2 gas where required
Key conclusions:
Ready to ramp-up effort, in particular prototyping and experimental work, also beamdynamics

## Slide 44: RCS Designs
Key conclusions:
1.3 GHz TESLA-type cavities work
Emittance transport is OK
Cost and power is OK
Need to connect to initial linacs
Achieved:
Lattices for all site independent RCSs
Beam propagation through complex
Conceptual design of magnets and power converters
Optimised design together with RF
Challenge:
Uses fast-pulsed normal magnets
5 Hz pulses of O(1-10ms)
6-35 km circumference
Cost
Recover energy from magnetic field
High bunch charge
Maintain beam quality
RCS | E [J/m] | Loss [%] | P [MW]
SPS 1 | 5447 | 1.1 | 1.9
LHC 1 | 5678 | 1.6 | 12.8
LHC 2 | 5752 | 6.3/2 | 26.6

## Slide 45: Collider Ring
Key conclusions:
Should improve energy acceptance should somewhat
OK with energy spread predicted in muon cooling
Mover system does not compromise beam in regular arcs
Achieved:
Magnet shielding design
Magnet conceptual designs
Cryogenics concept
Lattice reaches target beta-functions but not yet full target energy acceptance
First studies of mover system impact on beam
Challenges:
500 W/m loss, magnet strength, lattice design with beta 1.5-5 mm, 0.1% beam energy spread
Cryogenic loads at different temperatures
Shielding (30-40 mm)

## Slide 46: IMCC Develoment
46
Collaboration formed 2022, currently hosted by CERN
61 full partner institutes, more in the process
From all regions
EU co-funded design study MuCol started 2023
Strong recommendation from P5 «This is our muon shot»
Interest in hosting at FNAL
US partners are in the process of joining
US Muon Collider Inauguration Meeting in August 2024 at Fermilab (about 300 participants)
Forming national organisation to participate
Addendum to CERN-DoE agreement in preparation
Already strong US contribution to IMCC ESPPU documents
Work at universities started
Obtained several grants also at labratories
IMCC will carry out the R&D together and develop options to host the collider at CERN or at Fermilab and potentially also other sites

## Slide 47: Way Forward
Continue to execute the Design Study
Defined R&D plan, with deliverables and resources estimates for the next 10 years
Identify resources, sharing of work between partners
Synergy with other particle physics and accelerators
Muons, neutrinos, …
Strong synergy with societal applications exist
HTS magnets for fusion reactors, wind power generators, motors, material science, health applications
Power converter
RF in magnetic field can be relevant for fusion
…
Design of 10 MW HTS wind generator
Early career experts are very motivated by the required and possible innovations
Examples:
Collaboration on target solenoid/fusion with F4P, ERUOFusion, GaussFusion, ENI
Common EU request with Infineon for power converter

## Slide 48: Muon Collider CTEs
48
Short, intense proton bunch
Protons produce pions which decay into muons which are captured
Ionisation cooling of muon in matter
Acceleration to collision energy
Collision
- Proton pulse accumulation and compression
- Graphite target
- Target solenoid
- Muon cooling design
- 6D cooling solenoids
- 6D cooling RF cavities
- Final cooling solenoids
- Pulsed magnets and
power converters
- RCS RF system
- Collider ring dipoles
- Final focus quadrupoles
- Machine-detector interface
- Neutrino flux
Identified and prioritized with community
Other areas need now also to be addressed
(some work started)

## Slide 49: Cost and Power Scale
Design of many collider areas/components has progressed
but some uncertainties remain
No overall optimisation
HTS cost model
Power estimate based on conceptual designs and scaling from know components, e.g.
Simulations of fast-ramping magnets and power converter
Detailed scaling for RCS cavities