## Slide 1: HL-LHC Task 2.2 news
R. De Maria, K. Skoufaris, Y. Angelis

## Slide 2: Optics Tasks
On going:
2025-Q4 Full round optics cycle (Yannis) and Flat optics cycles (Kyriacos)
2026-Q2 Operational cycles for testing in IT String (Riccardo)
2025/9 Contribution to String day (Riccardo)
Urgent but not started yet:
Reduction aperture analysis LHCb upgrade (MBW 42 mm and D1 70mm)
Verify implication in Q11R8 reduction of current + MQ refurbishment
ECRs on aperture models (see later)
Other items:
Optics optimization for CLIQ suspended waiting on models from WP7.

## Slide 3: Xsuite-LSA implementation of triplet circuits
mqxfa.a1r1: k1:= kqx1a.r1/lqx1a.r1, l:=lqx1a.r1, fringe=...
mqxfa.b1r1: k1:= kqx1b.r1/lqx1b.r1, l:=lqx1b.r1, fringe=...
mqxfb.a2r1: k1:=-kqx2a.r1/lqx2a.r1, l:=lqx2a.r1, fringe=...
mqxfb.b2r1: k1:=-kqx2b.r1/lqx2b.r1, l:=lqx2b.r1, fringe=...
mqxfa.a3r1: k1:= kqx3a.r1/lqx3a.r1, l:=lqx3a.r1, fringe=...
mqxfa.b3r1: k1:= kqx3b.r1/lqx3b.r1, l:=lqx3b.r1, fringe=...
#Using individual magnet transfer functions of the integrated gradient
klqx1a.r1:=i_to_bl_q1ar1(iqx.r1+itqx1.r1+itqx1a.r1)/brho
klqx1b.r1:=i_to_bl_q1br1(iqx.r1+itqx1.r1)/brho
klqx2a.r1:=i_to_bl_q2ar1(iqx.r1)/brho
klqx2b.r1:=i_to_bl_q2br1(iqx.r1)/brho
klqx3a.r1:=i_to_bl_q3ar1(iqx.r1+itqx3.r1)/brho
klqx3b.r1:=i_to_bl_q3ar1(iqx.r1+itqx3.r1)/brho
LSA needs a energy independent variables to control the circuits
Differently from LHC, operational optics will be matched using measured transfer functions (speed up convergence of OMC iterations)
Xsuite model
iqx.r1 = "RQX.R1/I" = b_to_i_q2ar1("MQXFB.2AR1/K"*BRHO)
itqx3.r1 = "RTQX3.R1/I" = b_to_i_q3ar1("MQXFA.3AR1/K"*BRHO) - "RQX.R1/I"
itqx1.r1 = "RTQX1.R1/I" = b_to_i_q1br1("MQXFA.1BR1/K"*BRHO) - "RQX.R1/I"
itqx1a.r1 = "RTQX1A.R1/I" = b_to_i_q1ar1("MQXFA.1AR1/K"*BRHO) - "RQX.R1/I" - "RTQX1.R1/I"
where
i = b_to_i_q2ar1( i_to_bl_q2ar1(i)/ lqx2a.r1)
i = b_to_i_q3ar1( i_to_bl_q3ar1(i)/ lqx3a.r1)
i = b_to_i_q1br1( i_to_bl_q1br1(i)/ lqx1b.r1)
i = b_to_i_q1ar1( i_to_bl_q1ar1(i)/ lqx1a.r1)
LSA Parameters
L. Fiscarelli (WP3) to provide the transfer functions from current to integrated gradient and magnetic length for individual magnets in the form of parameters of the Fidel model and/or tabulated functions. R. De Maria (WP2) provide scaled gradients for the HL-LHC cycle. M. Hostletter (OP) uploads transfer functions and scaled gradients in LSA. To be tested in Q2/2026 in the String OP test.
R. De Maria, L. Fiscarelli, M. Hostletter, S. Yammine

## Slide 4: IT String Day

## Slide 5: ECR - on aperture
Title | Deadline | Actions
Vacuum Layout LSS5 LS3 1.8 | 2025-07-22 EC | Validate new aperture models in LDB/optics
ATLAS experimental beam vacuum layout configuration for RUN 4 | EC expired | Validate new aperture models in LDB/optics
B5L4.B Layout change | 2025-07-18 APP | Followed-up with impedance, e-cloud