## Slide 1: Beam Interlock System P0survey consolidation: pre-2031, post-2031, post-LS4
Antoine Colinet
01/07/2025

## Slide 2: New BIS architecture
Two matrices
Two actuators
8 BICs before 2031
1 more after 2031
2 (or?) more after LS4
BA2
BA80
BA81
BA82

## Slide 3: Actuators
Two actuators are connected to the BIS:
  M2 TAX
  P4 beam stoppers
When the interlocks downstream these elements report a fault, then the BIS sends a beam permit to FALSE to them. The aim is to insert these stoppers in the beam so that operation can be resumed asap.
Review of BID interlocks 07/03/2025: https://indico.cern.ch/event/1528963/
Technical implementation:
  BIS side: two RS485 differential pairs (for redundancy) to provide the beam permit
  BIS side: expects feedback from the BID controls (though no action taken if not correct)
  BID side:
    When BEAM_PERMIT is TRUE -> no interlock raised downstream the BID
    When BEAM_PERMIT is FALSE -> interlock raised downstream the BID -> need to move the TAX in-beam to restart operation

## Slide 4: Operation between the end of LS3 to 2031
Interlocks up to P42 dump taken into account
If an interlock is raised downstream the P4 stoppers, then the BIS requests the P4 stoppers to be moved in-beam
Before 2031, these interlocks are:
  WIC for the magnets downstream the P4 stoppers (from BA80)
  Access system covering TCC8 and ECN3 (this interlock should probably be disabled before 2031)
  Current monitoring of the PCs downstream the P4 stoppers
    RPOLC.BA80.RBT.X0430069.M
    RPOLC.BA80.RBH.X0430082
    RPOLC.BA80.RBT.X0430089.M
  P42 dump cooling on the TIDVG4
  BLMs downstream the P4 stoppers (both from BA80 and BA81)

## Slide 5: Operation between 2031 and LS4
Interlocks up to ECN3 taken into account
If an interlock is raised downstream the P4 stoppers, then the BIS requests the P4 stoppers to be moved in-beam
After 2031, these interlocks are:
  WIC for the magnets downstream the P4 stoppers (from BA80)
  Access system covering TCC8 and ECN3 (now enabled!)
  Current monitoring of the PCs downstream the P4 stoppers
    RPOLC.BA80.RBT.X0430069.M
    RPOLC.BA80.RBT.X0430089.M
    RPOLC.BA80.RBH.X0430082
    Question: BA81 + BA82 PCs are connected in series to provide a single interlock. This could be connected to the BIS in BA82, while waiting for NACONS phase 2
  P42 dump cooling on the TIDVG4
  BLMs downstream the P4 stoppers (both from BA80 and BA81)
  All BDF/SHIP interlocks (BIC in BA82)
Reference: EATM 05/09/2017

## Slide 6: Operation post-LS4
Interlocks up to ECN3 taken into account
If an interlock is raised downstream the P4 stoppers, then the BIS requests the P4 stoppers to be moved in-beam
After LS4, these interlocks are:
  WIC for the magnets downstream the P4 stoppers (from BA80, BA81, BA82)
  Access system covering TCC8 and ECN3 (now enabled!)
  Current monitoring of the PCs downstream the P4 stoppers
    RPOLC.BA80.RBT.X0430069.M
    RPOLC.BA80.RBT.X0430089.M
    RPOLC.BA80.RBH.X0430082
    … all selected PCs on P42 powered from BA81 and BA82
  BLMs downstream the P4 stoppers
  All BDF/SHIP interlocks (BIC in BA82)