## Slide 1
Post-processing, Assembly, and interconnection at MPG HLL: Status and Plans
Who we are
Hetrogenous integration
Interposer PilotProject
Christopher Roth
for the team at the Semiconductor Laboratory of the Max Planck Society

## Slide 2: The Semiconductor Lab of the Max Planck Society – MPG HLL
Central facility of the Max Planck Society
with ~40 employees
scientists, engineers, technicians, and students
2000 – 2023 @ Siemens Campus Neuperlach Munich
1000 m2 of clean room area
330 m2 of ISO 3 area
Full 6 inch silicon process line
From 2024 @ Research Campus Garching
1500 m2 of cleanroom area
600 m2 of ISO 3 & ISO 4 area
8 inch silicon process line
sensor design and fabrication
interconnection, assembly
system/camera design and test
Process and Device simulation, 2D and 3D
State-of-the-art layout tools
System assembly
System test and evaluation
In-house fabrication

## Slide 3: A selection of large detector projects - past and present
Silicon Drift Detector
pnCCD
DEPFET

## Slide 4: Inside HLL – 1500 m2 lab space
ISO 4 - 6
  1: R&D Lab and post-processing of external wafers
  2: Singulation, wire bonding and assembly
  3: Cu Lab (UBM and RDL)
  4: Wafer-level test and characterization
  5: Vertical integration (flip-chip and wafer bonding)
  6: Quantum Lab – MQV (shared with WMI/TUM)
Electronics and Laser Lab
ISO 8
  System development and test
ISO 3
  “CMOS line” adapted to fully depleted double-side processed silicon radiation sensors
    implantation, thermal, metallization, lithography, wet/dry etching, cleaning, inspection ....
  Access only by qualified personnel
  Strict control of material inside
1
2
3
4
5
6

## Slide 5: Post-processing and interconncet capabilities
R&D Lab
  Complete process line for small and experimental (test) projects
    Pilot development of ”non-standard” technologies with and on “non-standard” materials
    Thermal processes, lithography, cleaning and wet etching, metrology
    ICP-DRIE for TSVs and micro-channels being installed
    Experimental sensors, test structures, micro-mechanics ...
Backend-of-line and interconnect Lab
  Cu (and Al) redistribution layer (RDL), under bump metallization (UBM)
  Wafer dicing, chip handling
  Interconnect to read-out ASICs
    Electrical: flip-chip, wire bonding, conductive adhesives
    Mechancial: precision assembly of modules
    Thermal: utilization of suitable materials (metals, ceramics, composite materials..)
    Low temparature W2W, C2W, C2C bonding in preparation
Wafer format
  All process tools set up for 6” wafers as baseline
  4” wafer processing possible, smaller wafers and even single chip processing with customized adapter wafers
  8” wafer processing after tool re-configuration, possible on most of the tools

## Slide 6: A few pictures from past projects

## Slide 7: the DEPFET all-silicon module for Belle II PXD
Thin pixel array operated in „rolling shutter” mode, 20µs/f
  Only 4/768 rows active a time  low power in active area
module design starts on wafer level
module is one piece of silicon
  Sensitive area (APS)
  High density interconnect (HDI)
HDI as board for non-sensor parts
  UMC 180, TSMC 65, IBM/AMS/TSI 180
  Passive components
  On-module solder interconnect
Off-module interconnect with flex
  Solder and wire bonds
“MCM-D”, “2.5 D”, “SoC” ... We call it ASM
All-Silicon Module

## Slide 8: the DEPFET all-silicon module for Belle II PXD
x-ray picture of fully assembled module
0.21% of X0
module design starts on wafer level
module is one piece of silicon
  Sensitive area (APS)
  High density interconnect (HDI)
HDI as board for non-sensor parts
  UMC 180, TSMC 65, IBM/AMS/TSI 180
  Passive components
  On-module solder interconnect
Off-module interconnect with flex
  Solder and wire bonds
“MCM-D”, “2.5 D”, “SoC” ... We call it ASM
All-Silicon Module

## Slide 9: how to make thin DEPFETS
thickness of the sensitive area is an (almost) free parameter
thin area supported by a monolithically integrated silicon frame

## Slide 10: module assembly overview
Flip Chip of ASICs (~240°C):
  Bumped ASICs have (almost) the same solder balls (SnAg)
    DHP bumping at TSMC, DCD bumping via Europractice
    SWB bumping on chip and wafer level as post-process
  Bump bonding on customized support plates
  Initially at IZM, then at HLL
SMD placement (~200°C):
  Passive components (termination resistors, decoupling caps)
  Dispense solder paste, pick, place and reflow
Kapton attachment (~170°C), wire bonding:
  Solder paste printing on kapton, vapor phase soldering
  Wire-bond, wedge-wedge, 32 µm Al bond wires

## Slide 11: SMD assembly
Each module has about 100 capacitors and resistors of various formats (0402, 0201, 01005)
  Very small footprint, no screen printing of solder possible, delicate handling of module ...
  Adapted SMD technology installed at HLL
Automated micro assembly tool, the same as for flip-chip
  Additional dispense system
Process flow
  Condition module, dispense solder, place SMD parts, reflow in process chamber

## Slide 12: Process qualification
Extensive tests and QC/QA: shear tests, cross section, metallurgy, thermal stress tests ...

## Slide 13: The way forward: overview
Extend sputtering capability on existing sputter system
  targets are easy to exchange
     new metals possible
  replace 2/4 DC sputter guns with RF biased ones
     sputtering of isolators (SiO2, Al2O3 .. )
  software upgrade for co-sputtering and reactive sputtering
Improve lithography capability
  Use of e-beam lithography system installed by MQV partner
  HLL contribution: installation and qualification of required photo resist systems suitable for e-beam
Extend structuring capability
  Installation of ICP-DRIE for silicon
    TSV, Si wave guides
Extend interconnect capabilities and post-processing of ASICs and/or PICs
  Install CMP of Cu and SiO2 as preparation for wafer bonding
  Install and W2W and C2W direct and hybrid bonding
    Low temperature bonding <350 °C mandatory

## Slide 14
Main Objectives of the DRD7
project
facilitate a distributed lab for heterogeneous integration (HI) of radiation detectors
  interconnections/assembly of chips of various technologies/types:
    analogue + digital + memory + sensor + photonics + RF + MEMS ...
integration technology survey and development
  align currently available technologies within DRD7.6b labs
  identify required new process steps, install and qualify these steps (or find and qualify external suppliers)
define, practice, and qualify distributed process flow
provide HI ”service” to detector community

## Slide 15: heterogenous integration
Technology building blocks overview
Interposer
  single sided
  double sided  TSV
  interposer with micro-channels
  optical interposer
Assembly preparations
  Thinning of CMOS, Sensor, and/or interposer
  Post-processing on Wafer level and chip level
    std. solder bumps (“C4”)
    µ-bumps w/ different metallurgy
    Cu or Sn ep for SLID or hybrid bonding
Assembly
  SMT passives
  conventional bump bonding (flip-chip) – C2C
  Bump-less interconnect
    SLID - C2W, W2W
    Hybrid bonding – C2W, W2W
Lee et al.: IEEE Transactions on Electron Devices (March 2011), DOI: 10.1109/TED.2010.209
Everything, all at once
Very active field of R&D in industry
  Players are foundries and OSATs (Outsourced Semiconductor Assembly and Test)
    Intel/AMD/TSMC/Samsung.. and ASE/SPIL/Amcor...
    See IEEE EPS Heterogenous Integration Roadmap
  Large variety of technologies, solutions, techniques (and acronyms..)
    Mostly proprietary, limited accessibility or expensive (for low volume production)
There are extreme examples, mostly experimental:
Attempt to break it down in smaller pieces - easier to digest

## Slide 16: the next steps – more realistic
Joint project: complex silicon interposer
  Interposer 1 – “ip1”
    Single sided metal Al/Cu
    Bumped dummy chips with Al/Cu - “dc”
      small, high melting solder bumps, or Sn cap for SLID
      thinned to ~100 µm
    Bump bond or SLID dummy chips to ip1
  Interposer 2 – “ip2”
    Single sided metal Al/Cu
      big, low melting solder bumps
  Flip and assemble ip1 and ip2 - “ipx”
    Evaluate daisy chains, process characterization ....
pretty ambitious!
  need thin dummy chips, two different solder alloys ....
  takes quite some time to get results!
intermediate step: heterogenous integration of existing chips on interposer
  “only” tasks would be interposer production and bump bonding
  add a few passives maybe

## Slide 17: Interposer Process sequence I
Thermal Oxidation
  ~500nm wet or dry thermal oxide
Al sputter
  1 µm Alu
  sheet resistance ~30 mOhm/sq
Litho alu1
  spin-on std. thin photo resist
  expose mask 1, develop
Etch Al
  std. acid
resist strip (solvent)

## Slide 18: Interposer Process sequence II
Interlevel Dielectric ILD1
  deposition temp < 350 °C
  LTO or similar
  BCB - photo sensitive polymer (preferred)
    coat 3 µm, expose mask 2, develop
    hard bake at ~200 °C
    descum contact holes in CF4 plasma
    eps_r (BCB) = 2.65 @1 MHz
Ti:W /Cu sputter seed layer
  100 nm/200 nm
ep Litho
  spin-on thick ep photo resist, ~7-9 µm
  expose mask 3, develop

## Slide 19: Interposer Process sequence III
Through mask electro-plating
  Cu, about 5 µm
  sheet resistance for 1µm Cu ~17 mOhm/sq.
resist strip
  solvent
seed layer etching
  Cu and Ti:W etch, selective to Al
  Interposer design and layout started by Michele

## Slide 20
SEMICONDUCTOR LABORATORY
OF THE MAX PLANCK SOCIETY
Thank you for your attention!