## Slide 1: Target cooling station and Target complex ventilation
F. Dragoni, N.Zaric/ EN-CV , HI-ECN3 WP4 – TARGET COMPLEX – COORDINATION MEETING #13 – 18.06.2025.

## Slide 2: Agenda
Thermal loads
EL loads
Model integration
Pressure cascade levels
F. Dragoni, N. Zaric | Target cooling station and Target complex ventilation
18.06.2025.

## Slide 3: Thermals loads summary
Thermal loads assumed for ventilation design (preliminary calculations):
Heat loss: 240kW
Heat gains: 120kW – will be corrected, assumed at about 200kW, calculations in progress
F. Dragoni, N. Zaric | Target cooling station and Target complex ventilation
18.06.2025.

## Slide 4: Power requirements (preliminary)
General services – two possibilities:
  Multiple 3P+N+E supplies from EN/EL switchboard:
    Cooling: 1 x 320 A + 1 x 63 A + 1 x 32 A
    Ventilation: 1 x 250 A
    Secure network: One 250 A 3P+N+E to CV ABB Switchboard (cooling and ventilation)
  Multiple 3P+N+E supplies from EN/EL switchboard:
    Cooling: 1 x 320 A + 1 x 63 A + 1 x 32 A
    One 630 A 3P+N+E to CV ABB Switchboard fed from General services (cooling and ventilation)
    Secure network: One 250 A 3P+N+E to CV ABB Switchboard (cooling and ventilation)
Not including power needs in BA82 or back-up chiller
F. Dragoni, N. Zaric | Target cooling station and Target complex ventilation
18.06.2025.

## Slide 5: Model integration
F. Dragoni, N. Zaric | Target cooling station and Target complex ventilation
14.05.2025.
Currently 2 ST numbers (ventilation part is correct on ST1A45429_01)  This will be corrected into 1 ST number
Cooling part – in progress
Ventilation part changes:
  Grouping of equipment on the roof
  Solved clashes
  Ductwork grouping for possible shafts positions

## Slide 6: Pressure cascade levels
F. Dragoni, N. Zaric | Target cooling station and Target complex ventilation
14.05.2025.
Pressure cascade options to be discussed on the meeting (23.06.2025.)