## Slide 1
Scaling of IR3 losses from operational fills
Sara Morales Vigo and Belen Salvachua
106th BLM Thresholds WG meeting
18/06/2025

## Slide 2: Decomposition of losses during injection and start of ramp
BLM decomposition calibration at injection energy from 2025 scraping tests
  Calibration applied at the start of the energy ramp to obtain proton impacts on IR3 (left and right jaws) and IR7 primary collimators
However, we have observed in 2025 the hierarchy breakage in IR7 B1 at the start of the ramp, with the TCSG.6R7.B1 acting as primary and leaving a different loss pattern in the machine
  Are the BLM ratios to dump representative of a nominal situation?
  Analysed fill 10678, where the peak of losses appears to be mainly in IR3
  Analysed also fill 10709, where the peak of losses is shared between IR3 and IR7, for comparison
Scaled the BLM ratios to dump recorded around the LHC to 200kW in IR3
  Do we expect BLMs in other LHC areas to dump before we reach 200kW?

## Slide 3: Decomposition of losses during start of ramp – Fill 10678
Around 20kW peak loss in IR3 (B1 and B2) -> Using RS09 calibration

## Slide 4: Peak BLM signals during start of ramp – Fill 10678
RS09 BLM signals around the ring at the moment of peak loss in IR3
RS09 BLM ratio to dump around the ring at the moment of ~20kW peak loss in IR3
Hierarchy breakage
30% warning

## Slide 5: Scaled ratio to dump during start of ramp – Fill 10678
RS09 BLM ratio to dump around the ring scaled to 200kW peak loss in IR3
Dump limit
BLMTI.04R2.B2E10_TCTPV.4R2.B2 82% BLMQI.06L3.B2E10_MQTL 239% BLMTI.06L3.B1I10_TCP.6L3.B1 107% BLMQI.05L3.B2E30_MQWB.5L3 104% BLMQI.05L3.B1I10_MQWB.5L3 98% BLMTI.05L3.B1I10_TCSG.5L3.B1 86% BLMQI.05L3.B2E20_MQWB.5L3 93% BLMTI.05L3.B2E10_TCLA.B5L3.B2 109% BLMTI.05L3.B2E10_TCLA.A5L3.B2 119% BLMQI.04L3.B1I10_MQWA.E4L3 109% BLMQI.04R3.B2E10_MQWA.E4R3 105% BLMTI.05R3.B1I10_TCSG.B5R3.B1 105% BLMTI.05R3.B1I10_TCLA.A5R3.B1 180% BLMTI.05R3.B1I10_TCLA.B5R3.B1 127%
BLMQI.06R3.B1I10_MQTL 180% BLMQI.06R3.B1I20_MQTL 144% BLMTI.04L5.B1I10_TCTPV.4L5.B1 143% BLMTI.06R7.B1E10_TCLA.C6R7.B1 82% BLMTI.06R7.B1E10_TCLA.D6R7.B1 111% BLMQI.06R7.B1E10_MQTL 167%
BLMs above 80%
Hierarchy breakage

## Slide 6: Decomposition of losses during start of ramp – Fill 10709
Around 7-8kW peak loss in IR3 (B1 and B2) -> Using RS09 calibration

## Slide 7: Peak BLM signals during start of ramp – Fill 10709
RS09 BLM signals around the ring at the moment of peak loss in IR3
RS09 BLM ratio to dump around the ring at the moment of ~7kW peak loss in IR3
Hierarchy breakage
30% warning

## Slide 8: Scaled ratio to dump during start of ramp – Fill 10709
RS09 BLM ratio to dump around the ring scaled to 200kW peak loss in IR3
Dump limit
BLMTI.04R2.B2E10_TCTPV.4R2.B2 118%
BLMQI.06L3.B1I20_MQTL 90%
BLMQI.06L3.B2E10_MQTL 345%
BLMTI.06L3.B1I10_TCP.6L3.B1 110%
BLMQI.05L3.B2E30_MQWB.5L3 112%
BLMQI.05L3.B1I10_MQWB.5L3 106%
BLMTI.05L3.B1I10_TCSG.5L3.B1 93%
BLMQI.05L3.B2E20_MQWB.5L3 103%
BLMTI.05L3.B2E10_TCLA.B5L3.B2 140%
BLMTI.05L3.B2E10_TCLA.A5L3.B2 161%
BLMQI.04L3.B1I10_MQWA.E4L3 122%
BLMQI.04R3.B2E10_MQWA.E4R3 140%
BLMTI.05R3.B1I10_TCSG.B5R3.B1 110%
BLMTI.05R3.B1I10_TCLA.A5R3.B1 190%
BLMTI.05R3.B1I10_TCLA.B5R3.B1 137%
BLMQI.05R3.B1I20_MQWA.C5R3 85%
BLMTI.05R3.B2E10_TCSG.5R3.B2 83%
BLMQI.05R3.B2E10_MQWA.D5R3 106%
BLMQI.05R3.B1I30_MQWA.E5R3 105%
BLMTI.06R3.B2E10_TCP.6R3.B2 90%
BLMQI.06R3.B1I10_MQTL 198%
BLMQI.06R3.B1I20_MQTL 160%
BLMTI.04L5.B1I10_TCTPV.4L5.B1 158%
BLMTI.04R6.B1E10_TCDQA.B4R6.B1 114%
BLMQI.04R6.B1E10_MQY 92%
BLMTI.06R7.B1E10_TCSG.6R7.B1 157%
BLMTI.06R7.B1E10_TCSPM.6R7.B1 200%
BLMTI.06R7.B1E10_TCLA.C6R7.B1 313%
BLMTI.06R7.B1E10_TCLA.D6R7.B1 429%
BLMQI.06R7.B1E10_MQTL 637%
BLMQI.06R7.B2I20_MQTL 99%
BLMQI.06R7.B1E20_MQTL 109%
BLMTI.07R7.B1E10_TCLA.A7R7.B1 176%
BLMs above 80%
Hierarchy breakage

## Slide 9: Summary
BLM decomposition calibration at injection energy from 2025 scraping tests used to obtain proton impacts on IR3 and IR7 primary collimators at the start of the energy ramp
Hierarchy breakage in IR7 B1 observed at the start of the ramp, with the TCSG.6R7.B1 acting as primary and leaving a different loss pattern in the machine
  Analysed fill 10678, where the peak of losses appears to be mainly in IR3
  Analysed also fill 10709, where the peak of losses is shared between IR3 and IR7, for comparison
Scaled the BLM ratios to dump recorded at the moment of peak IR3 loss to 200kW -> Whole ring
  Main limitations in IR3, cells 4, 5 and 6, as expected
  BLMTI.04R2.B2E10_TCTPV.4R2.B2 and BLMTI.04L5.B1I10_TCTPV.4L5.B1 also limiting
  Limitations found in IR6 and IR7 BLMs are expected to be linked to the operation with broken hierarchy -> not expected to limit if the nominal operation is restored