## Slide 1: Status and plans on: _ _ 3D Electromagnetic Time-Domain wake and impedance solver
Elena de la Fuente1,2 &
Wakis team: Lorenzo Giacomel, Giovanni Iadarola1, Carlo Zannini1, Manuel Cotelo2
@CEI Section Meeting – 24th July 2025
1CERN (BE-ABP-CEI), Geneva Switzerland
2IFN-GV, Polytechnic University of Madrid, Madrid, Spain

## Slide 2: Other useful presentations since last CEI…
  21st April 24 @ CEI: Introduction to Wakis & FIT
  9th Aug 24 @ EMWSD #20: PML implementation
  2nd Oct 24 @ ICAP conference: Introduction to Wakis + GPU
  31st Oct 24 @ABP-GIM: Introduction to Wakis
  28th Feb 25 @MLCF: PIML Wake extrapolation in Wakis w/ IDDEFIX
  5th Mar 25 @WUM #1: Wakis community & Hands-on
  2nd April 25 @WUM #2: Wakis MPI implementation
  8th May 25 @ABP-GIM: Wakis status, community and IDDEFIX
  1st – 6th June @IPAC 25: Wakis poster, paper & flash slides
  11th July @CAP: Wakis CI/CD, status and Hands-on

## Slide 3: Outline
Introduction:
  Beam-coupling impedance simulations
  Finite Integration technique (FIT)
Status:
  The ImpedanCEI code suite & pipeline
  Hands-on time!
Plans:
  User community plans and applications
  Development plans
    + Extra slides on of some of Wakis features:
      CSG, CAD geometry import & snappy mesh (WIP)
      MPI implementation & Multi GPU
      Wake extrapolation w/ IDDEFIX
Hands-on
python notebooks
@ImpedanCEI/
CEI-meeting-hands-on

## Slide 4: Introduction to beam-coupling impedance
Accelerator device
Change in geometry
Change in electromagnetic properties
Passing beam current
Electromagnetic wakefields are generated as the particle beam traverses the different accelerator devices with discontinuities in the geometry (cavities, transitions…) or the electromagnetic properties
These will affect the trailing particles/bunches and can generate instabilities and beam-induced heating

## Slide 5: Introduction to beam-coupling impedance
Accelerator device
Electromagnetic fields
Wake potential & Impedance
Change in geometry
Change in electromagnetic properties
Passing beam current
Electromagnetic wakefields are generated as the particle beam traverses the different accelerator devices with discontinuities in the geometry (cavities, transitions…) or the electromagnetic properties
These will affect the trailing particles/bunches and can generate instabilities and beam-induced heating
The beam-coupling impedance is a frequency-dependent property of each accelerator device, used to quantify the wakefields’ effects

## Slide 6: Importance of beam-coupling impedance
Impedance model of the accelerator
Beam stability
Beam induced heating
The impedance of all relevant accelerator components is gathered in each accelerator's impedance model
And used in beam-dynamics codes (e.g., pyHeadtail, Xsuite) to predict beam behaviour and stability
Assess beam-induced heating of individual accelerator components and propose mitigation solutions
LHC Warm Vacuum modules Power lost map [3]
Transverse position growth
SPS transverse impedance model[1]
SPS Head-Tail mode zero instability [2]
[2] E. de la Fuente et al., THAFP01, HB’23
[1] C. Zannini, MOPJE049, IPAC’15
[3] C. Antuono et al., TUAN3, IPAC’24
Intrabunch motion (mirrored)
map

## Slide 7: Impedance assessment workflow
map
/
LHC Warm vacuum modules, 2023
Transverse position growth
pyWIT
xwakes
*Workflow from C. Antuono, M. Neroni et. al.,@JAP Workshop’24

## Slide 8: How to compute beam-coupling impedance?
Analytical calculations
Numerical computations
Beam-coupling impedance can be derived analytically for simple geometries and material configurations[4]:
e.g., cylindrical pillbox cavities, pipe transitions, single-layer resistive wall
For more complex accelerator devices, the numerical solution of Maxwell’s equations in frequency or time-domain is required.
In frequency domain:
  2D models for vacuum chamber multi-layered elements e.g., ImpedanceWake2D[5]
  Commercial CST® Eigenmode solver loss-less resonant modes of general 3D structures without excitation + impedance in post-processing
In time-domain:
  Time-domain allows for full-wave electromagnetic simulations including losses and excitation bunch. Several codes available following different approaches e.g.:
    ABCI (axi-symmetric), CST® Wakefield solver (3D), GdfidL®, PBCI, ECHO-3D (3D, moving window) not open-source
[4] Wake fields and impedance,
L. Palumbo, V.G. Vaccaro, CERN-1995-006.331
[5] ImpedanceWake2D,
N. Mounet, TUO1C02 HB’10
https://gitlab.cern.ch/IRIS/IW2D

## Slide 9: How to compute beam-coupling impedance?
Analytical calculations
Numerical computations
Beam-coupling impedance can be derived analytically for simple geometries and material configurations[4]:
e.g., cylindrical pillbox cavities, pipe transitions, single-layer resistive wall
For more complex accelerator devices, the numerical solution of Maxwell’s equations in frequency or time-domain is required.
In frequency domain:
  2D models for vacuum chamber multi-layered elements e.g., ImpedanceWake2D[5]
  Commercial CST® Eigenmode solver loss-less resonant modes of general 3D structures without excitation + impedance in post-processing
In time-domain:
  Time-domain allows for full-wave electromagnetic simulations including losses and excitation bunch. Several codes available following different approaches e.g.:
    ABCI (axi-symmetric), CST® Wakefield solver (3D), GdfidL®, PBCI, ECHO-3D (3D, moving window) not open-source
[4] Wake fields and impedance,
L. Palumbo, V.G. Vaccaro, CERN-1995-006.331
[5] ImpedanceWake2D,
N. Mounet, TUO1C02 HB’10
https://gitlab.cern.ch/IRIS/IW2D
Traditionally handled only by
commercial / closed-source software such as
Well-stablished & robust
Flexible / extendable for new accelerator challenges

## Slide 10: Outline
Introduction:
  Beam-coupling impedance simulations
  Finite Integration technique (FIT)
Status:
  The ImpedanCEI code suite & pipeline
  Hands-on time!
Plans:
  User community plans and applications
  Development plans
    + Extra slides on of some of Wakis features:
      CSG, CAD geometry import & snappy mesh (WIP)
      MPI implementation & Multi GPU
      Wake extrapolation w/ IDDEFIX
Hands-on
python notebooks
@ImpedanCEI/
CEI-meeting-hands-on

## Slide 11: How to compute beam-coupling impedance?
…with a passing beam current
on each accelerator device geometry…
, ,
Time-domain Maxwell’s equations….
To obtain figures of merit…
Wake potential in time-domain
Beam-coupling impedance in frequency-domain
Deconvolution with charge line distribution
beam source path
ntegration path

## Slide 12: Finite Integration Technique
, ,
, ,
Maxwell Equations (Integral form)
Maxwell Grid Equations
Operators
Grid areas and lengths
Material tensors
Domain discretization
1st approximation
z
x
y
Hexahedral cells

## Slide 13: Finite Integration Technique (II)
, ,
Maxwell Grid Equations
Domain discretization
With Yee grid
Time-stepping scheme (leapfrog)
2nd approximation
Time-evolution in timestep
Primal grid
Dual Grid
Symplectic integrator, 2nd order
No matrix inversion needed during time loop
Can pre-compute most of the quantities: speed
  Taste of speed: 20M cells, 22.3 it/s on Titan V GPU, ~8 Gb memory
CFL stability condition
Gauss Laws (for and ) considered satisfied* for no charges

## Slide 14: Finite Integration Technique (III)
Operators
Curl operator: [3Ncell x 3Ncell] sparse matrix that relates the E and H fields and defines PEC, PMC or Periodic boundary conditions (BCs)
: 3Ncell diagonal matrices containing the grid (primal and dual) discretization in terms of cell lengths and areas
Materials
3Ncell diagonal matrices for the anisotropic inverse permittivity and permeability rank-2 tensors
3Ncell diagonal matrix for the anisotropic electric conductivity rank-2 tensor. The current can be computed as:
Fields
,
scipy.sparse
scipy.sparse
Fields: saved in memory as [3Ncell] 1d lexicographic arrays, updated every simulation timestep.
Fully-exposed, modifications on-the-fly (e.g. addition of sources or initial conditions)
wakis E.inspect3d() method

## Slide 15: Outline
Introduction:
  Beam-coupling impedance simulations
  Finite Integration technique (FIT)
Status:
  The ImpedanCEI code suite & pipeline
  Hands-on time!
Plans:
  User community plans and applications
  Development plans
    + Extra slides on of some of Wakis features:
      CSG, CAD geometry import & snappy mesh (WIP)
      MPI implementation & Multi GPU
      Wake extrapolation w/ IDDEFIX
Hands-on
python notebooks
@ImpedanCEI/
CEI-meeting-hands-on

## Slide 16: Wakis code overview
Wakis is the 1st open-source time-domain electromagnetic solver tailored for wakefield simulations to compute beam-coupling impedance.
It computes the integral general form of Maxwell’s equations using the Finite Integration Technique (FIT)

## Slide 17: Wakis GitHub repository
Benchmarks against CST studio®
Open source code
Nightly tests
CI/CD pipeline
Documentation with Sphinx
Complete
impedance workflow playground notebooks
Check the repository
@ImpedanCEI/wakis
CPU-GPU-MPI
Simulation examples
⏳~2’ to 20’

## Slide 18: ImpedanCEI code suite
reuse
refactor
integrate
Actively maintained, documented, pip-deployed packages
Modular for flexibility, easy maintenance/development
100% python, PEP8 compliant, CI/CD practices
Encapsulate expertise of legacy codes over the years
🔗slides@MLCF
🔗slides@CEI by E. Vik
🔗slides@CEI
w/ L. Sito
w/ S. Joly

## Slide 19: Deployment pipeline in ImpedanCEI
Code development is tracked with GitHub releases
On each release (CI/CD pipeline):
  All the tests are run with GitHub Actions
  Main branch is tagged with a version e.g. #v0.5.1
  Create a summary of features, bugfixes and contributions and changelog
  Deploys a stable version to PyPI
  Updates documentation on ReadTheDocs
  Generates a Zenodo DOI that hosts a snapshot of the code at that stage in a .zip file
The work in progress is tracked in a release draft `release.md`
> pip install wakis

## Slide 20: Release example: Wakis #v0.6.0
Differentiation between:
Major releases 0.X.0 can include substantial changes in the code and the API (legacy breaking)
Minor releases 0.X.x include small features and bugfixes in the code.
  Usually, the releases solve some GitHub Issue that has been opened by a user
✨ Automated with Copilot from commit messages

## Slide 21: Wakis benchmarks
Ongoing benchmark campaign to improve code robustness @ImpedanCEI/wakis-benchmarks
Wakis comparison with CST simulations, available in the repository
Every challenge is an opportunity to develop!

## Slide 22: Results & benchmarking
Benchmarking campaign conducted on a lossy Pillbox cavity:
For different conductivities
1 Tesla T4 GPU
16-core CPU
5h 20’ 11’’
56’ 10’’ x5 faster
Above cutoff
Wake potential
Impedance
*presented at
Using the PML

## Slide 23: Results & benchmarking (II)
Benchmarking campaign conducted on a lossy Pillbox cavity:
For low-
beam source
regime
3D E-field distribution
*presented at

## Slide 24: Wakis Documentation
New!
Powered by Sphinx, hosted on ReadTheDocs

## Slide 25: Outline
Introduction:
  Beam-coupling impedance simulations
  Finite Integration technique (FIT)
Status:
  The ImpedanCEI code suite & pipeline
  Hands-on time!
Plans:
  User community plans and applications
  Development plans
    + Extra slides on of some of Wakis features:
      CSG, CAD geometry import & snappy mesh (WIP)
      MPI implementation & Multi GPU
      Wake extrapolation w/ IDDEFIX
Hands-on
python notebooks
@ImpedanCEI/
CEI-meeting-hands-on

## Slide 26: Wakis user community
Some ongoing projects
The user community is growing by the day:
  Weekly questions / requests of features
  Participation is encouraged through GitHub issues/pull requests
users
Soleil impedance model: Tapers and beampipe
(S. Thakur, A. Gamelin)
CERN FCC: beampipe with absorber
(P. Krotick)
Challenges due to PML reflections at high frequency
Need for surface impedance
EIC-ESR flanges (Xiaofeng Gu)
Helped testing MPI on servers

## Slide 27: Users and applications
Collaboration with C. Barbagallo (SY-RF)
Beryllium windows
Study of the voltage of the muon collider cavities
challenging with CST due to Be windows that forced to use
“Add space open boundaries”
CST
Wakis
Study of correction of direct space charge from time-domain simulations with low-beta

## Slide 28: Users and applications
Collaboration with E. Lamb (SY-RF)
Study of the modes excited by two counter-rotating beams w/ Wakis
  Completely autonomous user/developer
  Already contributed through pull request
  Implementing Frequency domain monitors: already on Ellenor’s Wakis fork
First results, preliminary

## Slide 29: Users and applications
Goal: compare 3D EM simulations with model derived from resistive-wall theory by E. Métral
  See his presentation at IMCC annual meeting
Setup:
Cylinder 1 cm radius, 1 m long
X,Y,Z number of mesh cells: 50/50/1000
  Total 2.5 106 mesh cells
PEC background, PML on z axis (100 cells each side)
Cylinder material
  Vacuum
  Lossy material: εr=1 / µr=1 / σ=10-3 S/m
  Lossy material with dielectric constant (Lithium Hydride): : εr=10 / µr=1 / σ=10-1 S/m
Collaboration with D. Amorim:

## Slide 30: Possible users and applications
Simulation of metamaterials (Leonardo Sito)
Impedance model for FCC-ee
(Dora Gibellieri + Elena Macchia + Jintao Li)
Impedance model for (HL-)LHC (Chiara Antuono + TECH)
Already using
IDDEFIX

## Slide 31: Development plans: challenges
Impedance in matter
Simulations with
non-ultrarelativistic (low beams
Model & correction of direct space charge impedance
Simulations with very short bunches
Accurate meshing of geometry
Slowly decaying wakefields
Dense meshes > 1000 M cells
Simulation length & stability
Physics models development

## Slide 32: Development plans: still a lot to do!
Done
FIT based on numpy & scipy
BCs: PEC, PMC, Periodic, PML
Wake potential and impedance
Anisotropic materials
CAD geometry import
State of the art 2d, 3d plotting
Automatic testing & CI/CD
EM Sources & beam current with
Parallelized & GPU accelerated
Wakefield extrapolation with EA
To do:
Smart refinement for grid (WIP)
Lossy metal approximation (surface impedance)
Dispersive materials
Improve robustness of PML at high-frequency
Correction of direct space charge for low- simulations (muCol) (C. Barbagallo)
Short-bunches (FCCee), moving window like ECHO3D?
Impedance in matter (D. Amorim, E. Kvinke)
Ports and field monitors in frequency domain (E. Lamb)
Differentiable simulations & adjoint methods (synergy w/ R. De Maria, A. Lasheen)
Correct for numerical dispersion (longitudinal and transverse) like PBCI
+ maintain and support users of the ecosystem 

## Slide 33: Conclusions
We’ve come a long way!
Now focus on:
Benchmark & validation, application to limit cases (FCC, MuCol)
Engaging the user/developer community
Continue developing key features: mesh refinement, surface impedance
BE seminar
12th December
19-24th October

## Slide 34: Acknowledgements
+ extended thanks to:
Giovanni Rumolo, Chiara Antuono, Elena Macchia, Szymon Lopaziuck (CERN),
Jean Luc Vay, Weiqun Zhang (LBNL), Erion Gjonaj (TU-Darmstadt)
& Eduardo Oliva (UPM)
for the very useful discussions
Wakis team: Lorenzo Giacomel, Giovanni Iadarola, Carlo Zannini, Manuel Cotelo
Iddefix team: Malthe Raschke Nielsen, Sébastien Joly, Bernardo Figueiredo
BIHC team: Leonardo Sito, Francesco Giordano, Jintao Li, Benoit Salvant, Carlo Zannini
Neffint team: Eskil Vik, Nicolas Mounet
Code development is a big collaborative team effort:
Thanks to contributors (code or expertise):

## Slide 35
Thank you for the attention 
Elena de la Fuente García
elena.de.la.fuente.garcia@cern.ch

## Slide 36: Bibliography sources
S. Joly, ”Resonator impedance extrapolation of a partially decayed wake” presentation @ CERN ABP-CEI section meeting link
S. Joly,”Recent advances in the CERN PS impedance model and instability simulations following the LHC Injectors Upgrade project” PhD Thesis, Sapienza Universita di Roma, link
M. Raschke, ”Evolutionary Algorithms for Wakefields” @ CERN ABP-CEI section meeting link
N. Mounet, “The LHC Transverse Coupled-Bunch Instability” PhD Thesis EPFL, link
T. Weiland and R. Wanzenberg, “Wake fields and impedances,” Lect. Notes Phys., vol. 400, pp. 39–79, 1992, doi: 10.1007/3-540-55250-2_26
I. Zagorodnov and T. Weiland, “TE/TM field solver for particle beam simulations without numerical Cherenkov radiation,” Phys. Rev. ST Accel. Beams, vol. 8, p. 042001, 2005, doi: 10.1103/PhysRevSTAB.8.042001
M. C. Balk, R. Schuhmann, and T. Weiland, “Open boundaries for particle beams within fit-simulations,” Nuclear Instruments and Methods in Physics Research, vol. 558, no. 1, pp. 54–57, 2006, doi: https://doi.org/10.1016/j.nima.2005.11.076.
K. Klopfer, “Computation of Complex Eigenmodes for Resonators Filled With Gyrotropic Materials,” PhD thesis, Technische Universität Darmstadt, Darmstadt, 2014. [Online]. Available: http://tuprints.ulb.tu-darmstadt.de/4210/
J. A. Moreno, E. Oliva, and P. Velarde, “EMcLAW: An unsplit Godunov method for Maxwell ’s equations including polarization, metals, divergence control and AMR,” Computer Physics Communications, vol. 260, p. e107268, Mar. 2021, doi: 10.1016/j.cpc.2020.107268.
U. Niedermayer, “Determination of Beam Coupling Impedance in the Frequency Domain,” PhD thesis, Technische Universität Darmstadt, Darmstadt, 2016. [Online]. Available: http://tuprints.ulb.tu-darmstadt.de/5157/
IDDEFIX

## Slide 37: Outline
Introduction:
  Beam-coupling impedance simulations
  Finite Integration technique (FIT)
Status:
  The ImpedanCEI code suite & pipeline
  Hands-on time!
Plans:
  User community plans
  Development plans
    + Extra slides on of some of Wakis features:
      CSG, CAD geometry import & snappy mesh (WIP)
      MPI implementation & Multi GPU
      Open boundaries: PML
      Wake extrapolation w/ IDDEFIX
Hands-on
python notebooks
@ImpedanCEI/
CEI-meeting-hands-on

## Slide 38: CAD geometry import w/
Using capabilities, wakis can:
Read CAD geometry and bounds:
geometry = pv.read(CAD_file)
domain_bounds = geometry.bounds
Generate the domain grid from numpy.meshgrid
grid = pv.StructuredGrid(X, Y, Z)
Find the domain cells inside each CAD solids with optimized collision filters
Assign material properties to each cell inside solid
SotA interactive plotting in ipython/ipynb

## Slide 39: Towards smart meshing (work in progress)
Example:
LHC unshielded bellows
Snap points in XZ plane
Snap points in XY plane
Mesh refinement strategy adopted by OpenFoam & Ansys:
  Find STL surface edge features geometry.extract_feature_edges()
  Project points to XZ, YZ, XY planes to get snap points
  Refine mesh around snap points using an optimizer:
  Penalties: small cell sizes, abrupt changes, spread
Small cell sizes decrease max. stable timestep
(CFL)

## Slide 40: Outline
Introduction:
  Beam-coupling impedance simulations
  Finite Integration technique (FIT)
Status:
  The ImpedanCEI code suite & pipeline
  Hands-on time!
Plans:
  User community plans and applications
  Development plans
    + Extra slides on of some of Wakis features:
      CSG, CAD geometry import & snappy mesh (WIP)
      MPI implementation & Multi GPU
      Wake extrapolation w/ IDDEFIX
Hands-on
python notebooks
@ImpedanCEI/
CEI-meeting-hands-on

## Slide 41: MPI implementation
The major feature in the #v0.6.0 release will be the possibility to run parallel simulations using several cores, leveraging CERN resources like
the Openstack impedance machines and the HTCondor cluster
This is handled through MPI: Message Passing Interface protocols

## Slide 42: MPI: How does it work?
Single core
Core 0
Core 1
Core 2
Any computer with an OpenMPI installation can run parallel jobs:
> python myscript.py
> mpiexec –n 3 python myscript.py

## Slide 43: MPI: How does it work?
Single core
Core 0
Core 1
Core 2
However, to properly optimize the resources, each core should compute 1 slice of the domain:
> python myscript.py
> mpiexec –n 4 python myscript.py
Core 3
mpi4py

## Slide 44: MPI implementation in Wakis
Using mpi4py, we can tell each core what to do separately:
GridFIT3D splits the domain in slices among z-dir and imports the geometry to each slice
SolverFIT3D computes the material tensors and Curl matrices for each slice: ,
Time-stepping routine* needs the information of the other slices  need to sync the fields
  Need to communicate each slice efficiently:
    Minimum memory share: send only boundary info
    Minimum operations
  mpi4py.MPI.Comm.SendRecv paired Sync and Recv in 1 sync and avoids deadlocks + is CUDA-aware
* Time-stepping routine solves:
mpi4py

## Slide 45: MPI implementation in Wakis
* Time-stepping routine solves:
mpi4py
No need for duplicate classes! See commits #543-#576

## Slide 46: MPI implementation in Wakis
To make everything work, we need to add some overlap between slices, we do that through Ghost cells
Without ghost cell overlap (ghost_cell =0)
With ghost cell overlap (ghost_cell =1)
Many thanks to Manuel Cotelo for his help 

## Slide 47: MPI implementation in Wakis
To make everything work, we need to add some overlap between slices, we do that through Ghost cells
Without ghost cell overlap (ghost_cell =0)
With ghost cell overlap (ghost_cell =1)
Many thanks to Manuel Cotelo for his help 

## Slide 48: CUDA-aware MPI

## Slide 49: Outline
Introduction:
  Beam-coupling impedance simulations
  Finite Integration technique (FIT)
Status:
  The ImpedanCEI code suite & pipeline
  Hands-on time!
Plans:
  User community plans and applications
  Development plans
    + Extra slides on of some of Wakis features:
      CSG, CAD geometry import & snappy mesh (WIP)
      MPI implementation & Multi GPU
      Wake extrapolation w/ IDDEFIX
Hands-on
python notebooks
@ImpedanCEI/
CEI-meeting-hands-on

## Slide 50: Impedance assessment challenges
Impedance in matter
Simulations with
non-ultrarelativistic (low beams
Model & correction of direct space charge impedance
Simulations with very short bunches
Accurate meshing of geometry
Slowly decaying wakefields
Dense meshes > 1000 M cells
Simulation length & stability
Physics models development

## Slide 51: Wakis+IDDEFIX simulation workflow
Partially decayed wakefield simulation
(e.g. -30dB)
Resonator fitting with IDDEFIX
Fully decayed, analytically represented impedance & wake
Acc. Device’s beam-induced power loss
Acc. Impedance model
Beam dynamic simulations
Verification with longer simulation (-60dB) if needed
Table of resonator parameters
Acc. Device under study
pyWIT
xwakes

## Slide 52: IDDEFIX partially decayed resonator formalism
Parameter T: Accounts for truncated wakelength
Derivation of the resonator formalism for partially decayed wakefield simulations by S. Joly, N. Mounet and N. Shipman
here
Longitudinal
Transverse

## Slide 53: IDDEFIX working principle:
Obtain the fully-decayed resonator parameters (), from a partially decayed impedance
Minimize SSE:
Assess
fitting SSE error
Courtesy of
M. Raschke @ABP-CEI
Partially decayed impedance with 2 resonators
}
Fitting the resonator formalism for partially decayed , wakefield simulations derived by S. Joly, N. Mounet and N. Shipman (equations in backup)
*Evolutionary algorithm used in IDDEFIX
*CMA-ES also available thanks to B. Figueiredo

## Slide 54: IDDEFIX in action: user cases
BPMs impedance & wake reconstruction by fitting most relevant modes up to 35 GHz
Courtesy of Jintao Li
Courtesy of Leonardo Sito
@WUM#2 - 2nd April
Study of metamaterial insertions in cavities
Fully decayed wake computationally inaccessible (and unstable), made possible with IDDEFIX

## Slide 55: Impact on impedance assessment
map
/
*
*
* Python packages developed in ABP
Individual resonator () contribution to beam-induced
Drastically cut simulation time for slowly decaying wakes
Represent each component’s
impedance analytically
by (, …)
Analytic wake function
from (, …)
*
*