## Slide 1: Characterization of losses in a new septum magnet
Thibaut LEMERCIER
7 August 2025

## Slide 2: Beam Transfer — A Short Introduction
Key Components of Beam Transfer
Kicker
  Perform fast, time-critical deflection
  Select specific bunches at the right moment
  Provide a small but rapid kick to initiate separation
  2. Septum
  Provide larger, spatial beam deflection
  Operate at slower speeds than kickers
  Direct the beam to the new path after the kicker deflection

## Slide 3: A new magnetic septum for PS Extraction
Why Do We Need a New Septum?
  Existing septum is exposed to intense radiation due to beam-blade interactions.
  Current septum needs replacing every ~2 years, increasing maintenance and radiation exposure to personnel.
  The project aims to develop an alternative topology: the eddy current septum
  What Is an Eddy Current Septum?
  Powered by high-current pulses :
  28.5 kA, 2500 Hz, 1.2 s between pulses
  Fast pulses generate eddy currents in a conductor
  These induced currents oppose the magnetic field (via Lenz's Law), shielding the field-free region

## Slide 4: Losses in a Pulsed Magnet
Copper Losses
  Caused by the electrical resistance of copper in the windings and the septum blade
  At high frequency, the skin effect increases the copper losses.
  Iron Losses (Occur in the magnetic yoke)
  Eddy Current Losses : Comparable to how induction cooktops heat metal
  Hysteresis Losses : Due to the non-linear magnetization properties of iron
  Mechanical Losses
  Magnetic forces induce small vibrations
  Since displacement is minimal, mechanical work is considered negligible
Skin Effect
Eddy currents
Hysteresis Loop

## Slide 5: FEM Simulations
  Developed a COMSOL model to simulate magnetic and thermal losses
  COMSOL uses Finite Element Method (FEM): meshes the geometry, solves physics equations numerically
  Iron laminations too thin for full resolution → use loss models instead
  Applied the Steinmetz model to estimate hysteresis and eddy current losses →
  Validated simulation using manufacturer data via a virtual Epstein Frame test in COMSOL
Epstein Frame Model

## Slide 6: Results
The Epstein Frame simulation matched experimental results → Steinmetz model validated for loss prediction
The total loss is approximately 262 J
A thermal model was also developed → Heating is primarily influenced by the thermal contact resistance between the magnetic core and the copper blade

## Slide 7: Electrical Measurements
Losses measured by integrating the product U*I over one pulse period
In magnets, active energy = real power losses, since reactive energy is returned to the supply over a full cycle
Measured losses: 2300 J → 10× higher than simulation results !

## Slide 8: What’s Next?
  Build a test stand for thermal and loss characterization
  Study heat distribution inside the magnet
  Characterize thermal contacts to refine the thermal model
  Test the effect of mechanical pressure on the lamination stack → Investigate potential insulation breakdown
  Develop a 3D COMSOL model → More accurate simulation of geometry and loss mechanisms
3D COMSOL Model
CAD of the test bench

## Slide 9
Thank you for your attention! I’m happy to answer your questions.