## Slide 2: WP5 collimation update
Stefano Redaelli, BE-ABP, on behalf of WP5 & LHC Collimation teams
with R. Bruce, F. Carra, M. Di Castro, A. Perillo Marcone, F.-X. Nuiry, A. Rossi
15th HL-LHC Collaboration Meeting
29 September — 2 October 2025
CERN, Geneva, Switzerland

## Slide 3: WP5 upgrade scope
IR collimation: Completely new layouts and collimator designs: IR1+IR5: incoming and outgoing.
Full remote alignment system (FRAS)
Dispersion suppressor collimation: Secondary beams from ion physics
Impedance reduction: low-impedance, high robustness secondary collimators: coated MoGr and coated Gr
Un-coated MoGr primary collimators.
Crystal-assisted collimation (Pb ions)
4-8 bent crystals, 50 μrad bending
IP7 (betatron cleaning)
LS2+LS3
LS2
LS2
LS3
LS2+LS3
LHC collimation upgrade to ensure safe and efficient operation at higher beam currents and luminosity!

## Slide 4: Some WP5 numbers
Description | Name | LS2 | LS3 | Tunnel
Dispersion suppressor | TCLD | 5 |  | 2
Low-impedance primary | TCPPM | 5 |  | 4
Low-impedance secondary–V1 | TCSPM | 10 |  | 8
Low-impedance secondary–V2 | TCSPM |  | 12 | 10
Crystal primary | TCPC | 6 |  | 4
Two-beam tertiary H | TCTPXH |  | 4 | 4
Two-beam tertiary V | TCTPXV |  | 5 | 4
Two-beam physics debris | TCLPX |  | 5 | 4
Single-beam tertiary/debris | TCTPM |  | 10 | 8
Physics-debris fixed masks | TCLM |  | 15 | 12
 |  | 26 | 51 | 52
The successful deployment of the first installation provided crucial benefits to the Run 3 performance, in particular for ions
It also allows collecting feedback for the LS3 upgrades (designs, materials, …)
Upgrades in the second long shutdown (LS2)
- First phase of the low-impedance upgrade of IR7
- Dispersion suppressor collimation (ion beams)
- Crystal collimation for betatron cleaning (ion beams)
Upgrades in the third long shutdown (LS3)
- Second phase of the low-impedance upgrade of IR7
- New collimation layouts in IR1/5
R&D, validation, studies and first deployment
Final deployment, Run 4 scenarios preparation

## Slide 5: Table of contents
Introduction
Run 3 collimation upgrade performance
Limitations for HL-LHC under study
Upcoming for Run 4
Conclusions

## Slide 6: Recap. of 2024 Pb performance and WP5 role
WP5 deliverables successfully deployed: - TCLD collimator task (was task 5.2: many thanks I. Lamas, O. Aberle): absorbers around ALICE to protect dispersion suppressors from collisional losses
- Crystal collimation (sub-WP5.4): 4 devices in IR7. Many thanks to M. Di Castro
One goal of the HL-LHC project successfully delivered!
✅
R. Bruce et al.
Up to +30% above target without beam-induced quenches

## Slide 7: Crystal collimation of lead ion beams
Outstanding: Consolidate system for runs beyond LS4, not in initial HL-LHC scope
Crystal collimation scheme
IR7
Used since first ion run in 2023
Peak performance 5-13 times better than standard system
ML-assisted tools to optimise and monitor channeling
D. Mirarchi et al.
N. Triantafyllou

## Slide 8: Spinoffs of WP5 developments with bent crystals
M. Zielinska
Crystal studies with Ne and O beams in special runs in 2025, up to 6.8 Z TeV.
Not “needed” as intensities were low, but demonstrated improvements up to x10 times!
Unique database for crystal performance data in the TeV scale, for p, Pb, Ne, O, Xe.
Know-how developed for collimation was key to these concept
HL-LHC supported with hardware!

## Slide 9: LHC Run 3 — proton beam intensity and luminosity
Chart: Fill number in 2025
β*+ separation levelling → ±1.5% control
Xing 160 μrad → 120 μrad
12h-14h
As reported to the LHCC meeting in Sep.2025
Record 2025: 440 MJ (64% of HL-LHC target)
Optimised cleaning performance to operate efficiently and with low backgrounds
Complex IR collimator gymnastics in levelling
Controlled disposal of physics debris in IR1/5
New in Run 3: background optimization of forward physics experiments (dedicated talks on Wed., WP2/WP5/WP6B/WP10)

## Slide 10: Collimator gymnastics during levelling
TCT settings down to 8.5σ at the smallest the β* values, margin to aperture of about 1σ.
Excellent stability throughout the run, but needs regular monitoring.
Big improvements also in IR7 (not shown): ML-assisted angular alignment!
Works reliably and safely at the LHC!
The HL-LHC upgrade ensures better performance (2 more TCTs per IP side) and flexibility, with BPMs in all devices.
Process will remain challenging even if larger aperture margins are expected in Run 4.
Collimator centres and gap during levelling in IR1/5
D. Mirarchi

## Slide 11: Collimation cleaning and loss patterns
Peak cleaning performance excellent and stable throughout the runs.
Run 3 showed anomalies in loss patterns from various effects under study: orbit distortion and β-beating from beam- beam effects, spurious dispersion, BB resonances and machine non-linearities.
To be studies further as critical regimes for HL-LHC.
N. Triantafyllou, F. van der Veken
Dedicated discussions on Thu., WP2/WP4/WP5

## Slide 12: Table of contents
Introduction
Run 3 collimation upgrade performance
Limitations for HL-LHC under study
Upcoming for Run 4
Conclusions

## Slide 13: Developments and some issues being followed up
IR7 cleaning performance for different HL-LHC setting scenarios Both “TDR” and “relaxed” settings are larger than Run 3 ones New IR7 optics, tested in 2025 with high intensity
Hierarchy violations / concerns in presence of spurious dispersion and non-linearities
Evolution of beam halo and predicted impact on HL-LHC (lifetime, failures)
Continued studies of beam stability and collimation impedance.
Vacuum spikes at news TCLD and scaling to HL-LHC beam parameters
Long-term lifetime of edge-welded bellows
Beam losses in presence of vacuum activities from fingers
…
✅
✅
✅

## Slide 14: Status of new IR7 optics and configurations
The principle feasibility, addressing cleaning and impedance improvements, already assesses in MDs until 2024.
In 2025: full integration in the operational cycle for validation at high beam current.
Results obtained in MD1 and MD2 are very promising.
  Lifetime in “combined ramp&de-squeeze” comparable to operational fills
Still considering to propose it for 2026, with minor caveat on TCT losses.
300h
Beam 2 lifetime vs time
See talk by B. Lindstrom, L. Bertolozzi

## Slide 15: Update on LHC beam halos
Improved analysis: established new reference models for LHC halo population
Although present operation is smooth, halo content consistent with Run 2 and could pose concerns at HL-LHC.
Upcoming post-doc to study impact of Run 3 findings to collimation system, machine and including experiments for relevant failures
Plan to gather more data but not yet included if 2025 MD schedule.
Plan to measure with pushed beams in any high-intensity opportunities in 2026.
See talks P.Hermes, M. Rakic

## Slide 16: “Soft landing” of hollow e-lens project
HW deliverables: Gun, collector and BPMs
Produced target 5 A at 8kV (design: 10kV)
Calibration / mapping BTV vs BPM for hollow beam
We will be ready in case the Run 4 performance is affected by halo issues.
A. Rossi

## Slide 17: Table of contents
Introduction
Run 3 collimation upgrades
Limitations for HL-LHC under study
Upcoming for Run 4
Conclusions

## Slide 18: WP5 master schedule
Issues with a “slow start” of the contractor, same one that produced the collimators in LS1 and LS2 - unique design & challenges for TCLPX & TCTPX. Focus now is to maintain the schedule & quality.

## Slide 19: Recap.: Collimation systems for LS3
Tertiary collimators to protect against incoming beam losses + physics debris collimators, all with BPMs
Two-in-one design for H collimators to fit the tight space at the re-combination region between TAXN and D2.
Other “TCT” and “TCL” devices in cells 5 and 6 use a more conventional single-beam design
Low-impedance + BPM design in IR7
R. Bruce

## Slide 20: From CERN prototypes to pre-series in industry
Courtesy F.X. Nuiry& D. Baillard
See the HL-LHC news on collimation string, Sep. 2023
F.X. Nuiry, T. Parmentier
See also talk by L. Puddu

## Slide 21: Pre-series collimators: TCTPXV
F.X. Nuiry, T. Parmentier

## Slide 22: Pre-series collimators: TCSPM
F.X. Nuiry, T. Parmentier

## Slide 23: Getting ready for the series production
F.X. Nuiry, T. Parmentier

## Slide 24: Conclusions
WP5 deliverables staged between LS2 and LS3 Successful deployment in LS2, with key performance milestones achieved in Run 3
Feedback from the operational experience in Run 3 collected Performance excellent for ion and protons. Concerns for futures being addressed: hierarchy issues; halo populations; …
Future efforts focused on the production of LS3 collimators for IR1/5/7 Series production in industry of 36 new movable collimators has started. Additional contact for 15 fixed masks with the same contractor.
Status and feedback on ongoing production Production is on track: three pre-series collimators are in the final assembly phase. Series production for the remaining 33 collimators is pending the approval of the three pre-series, expected in March 2026. First deliveries of series units planned in November 2026. However, several sub-components series units are already available (Absorbing blocks, mechanical tables).
Thanks to all teams involved and ready to take on the LS3 challenges!

## Slide 25
Reserve slides

## Slide 26: Collimation impedance upgrade Phase 1
Successful deployment of first low-impedance phase.
More details on talks by C. Antuono, X. Buffat.

## Slide 27: Update on beam lifetime at the LHC
S. Morales
B. Salvachua
LHC beam lifetime in 2025 excellent! Typical around 10h while entering in collisions. Can we rely on that for the final HL-LHC beam parameters?

## Slide 28: Xray machine for crystal characterisation
Facility funded by WP5 & PNPI enables detailed measurements of mechanical properties of bent crystals:
Geometric properties and their stability vs thermal cycles; the crystal miscut.
Being finalised, will be used also for other crystal project at CERN.
All WP5 crystal tested as part of the acceptance.
Courtesy M. Di Castro, E. Matheson