## Slide 1: HL-LHC longitudinal beam stability for updated impedance model
Ivan Karpov, Theodoros Argyropoulos, Rama Calaga, Heiko Damerau, Frank Gerigk, Leandro Intelisano, Birk Karlsen-Baeck, Christophe Lannoy, Nicolas Mounet, Michela Neroni, Sigurd Nese, Elena Shaposhnikova, Helga Timko, Christine Vollinger, and Michail Zampetakis
Acknowledgements: Simon Albright, Ylenia Brischetto, Lorenzo Giacomel, Alexandre Lasheen, Benoit Salvant, and CPS/SPS/LHC OP teams
15th HL-LHC Collaboration Meeting, 02.10.2025

## Slide 2: Recap on single-bunch stability
LHC MD 2017
H. Timko et al., HB, 2018
Persistent oscillations after injection, resulting in particle losses
MV
Persistent oscillations after injection indicate that we are approaching the threshold of loss of Landau damping (LLD) for HL-LHC parameters
The LLD threshold is defined as (IK, T. Argyropoulos, E. Shaposhnikova, PRAB, 2021)
Complicated impedance model can be substituted by an effective broad-band (BB) impedance (IK, T. Argyropoulos, S. Nese, and E. Shaposhnikova, HB, 2021)
Effective impedance
Effective cut-off frequency

## Slide 3: Destabilizing effect of broad-band impedance
Coupled-bunch instabilities (CBI) driven by higher-order modes (HOM) were not observed in the LHC so far
HL-LHC will operate at higher intensity compared to LHC and crab cavities with strongly damped HOMs will be installed
In the presence of BB impedance, the CBI threshold is reduced below the LLD threshold
Instability thresholds at GeV for = 8 MV: HOM - , = 582 MHz
BB - , = 5 GHz
IK, WP2/WP4 Meeting, 30.11.2021
Semi-analytical result using MELODY*
*IK, Matrix Equations for LOngituDinal stabilitY code

## Slide 4: Destabilizing effect of broad-band impedance
Coupled-bunch instabilities (CBI) driven by higher-order modes (HOM) were not observed in the LHC so far
HL-LHC will operate at higher intensity compared to LHC and crab cavities with strongly damped HOMs will be installed
In the presence of BB impedance, the CBI threshold is reduced below the LLD threshold
No margin at HL-LHC parameters according to the present understanding of the (HL-) LHC impedance model
Mitigation measures need to be studied
Instability thresholds at GeV for = 8 MV: HOM - , = 582 MHz
BB - , = 5 GHz
IK, WP2/WP4 Meeting, 30.11.2021
Parameter spread
Semi-analytical result using MELODY*
*IK, Matrix Equations for LOngituDinal stabilitY code

## Slide 5: Generalized threshold
Typically, broadband (bb) and narrowband (nb) impedance sources are treated separately, except in a few examples of CBI growth rate calculations
Approximate threshold based on Lebedev equation (IK, E. Shaposhnikova, 2024)
Growth rates of most unstable modes for 9 bunches (MELODY - lines, BLonD - crosses)
Broadband impedance
Higher-order mode (HOM)

## Slide 6: Impact of BB impedance parameters
Parameters:
Growth rates of coupled-bunch instability strongly depend on the parameters of the BB impedance
Precise knowledge of the impedance model is crucial for evaluation of stability

## Slide 7: Latest measurements of BB impedance
Kick-response method
Longitudinal Schottky spectra
M. Zampetakis et. al, HL-LHC CM, 2024 and 2025 MD results
Measurements
Simulations for
C. Lannoy et. al, HL-LHC CM, 2024
Theory for
Simulations

## Slide 8: Latest measurements of BB impedance
Kick-response method
Longitudinal Schottky spectra
Measurements
Simulations for
C. Lannoy et. al, HL-LHC CM, 2024
Theory for
Simulations
M. Zampetakis et. al, HL-LHC CM, 2024 and 2025 MD results

## Slide 9: Possible cures: flattened particle distribution
Bunch flattening via RF phase modulation:
Developed in Tevatron to stop “dancing bunches”, as an alternative to the longitudinal damper (C. Y. Tan and A. Burov, PRAB, 2012)
Tested in 2012 in the LHC to demonstrate the reduction of beam-induced heating (E. Shaposhnikova et al, IPAC, 2014)
Routinely applied in physics since 2016
The LLD threshold does not depend on the cutoff frequency (IK, T. Argyropoulos, E. Shaposhnikova, PRAB, 2021)
Measurements in Tevatron
H. Timko et al, Evian, 2019
LHC

## Slide 10: Results for flattened distribution
Flatness parameter
Present model
Measurement-based model
Semi-analytical analysis confirms that a modified distribution can raise the instability threshold
Stability gain is sensitive to the “flatness” of the line density
Since the “measurement-based” model has a higher , improvement is more limited

## Slide 11: Implementation scenarios and potential challenges
RF phase modulation after injection in the LHC
Opening phase loop can seed instability
Instability can be potentially enhanced since
Modification of distribution in the SPS
Potentially different bunch-by-bunch shape due to strong transient beam loading
Preservation of “flatness” after filamentation in the LHC needs to be confirmed
Intra-beam scattering (IBS) might compromise flattening although leads to gradual bunch length increase
HOM + Broadband

## Slide 12: Possible cures: double-harmonic RF system
The LLD threshold with the second harmonic RF system in the bunch shortening mode scales as (L. Intelisano, PhD thesis, 2023
L. Intelisano, IK, H. Damerau, PRAB, 2025)
Scaling is confirmed in numerical analysis and measurements at the PS flattop
Measurements in PS at 26 GeV
Single RF (10 MHz)
Double RF (10 + 20 MHz)
The same scaling also applies to the coupled-bunch instability threshold (V. I. Balbekov and S. V. Ivanov, 1987), but the impact of BB impedance needs to be confirmed

## Slide 13: Results for double-harmonic RF system
Present model
Measurement-based model
The instability threshold can be significantly increased by operation in the bunch-shortening mode with a moderate RF voltage (one or two single-cell 800 MHz cavities per beam)
Slightly higher peak line density can impact blow-up due to IBS

## Slide 14: Possible future measurements
Preparation of flattened distribution in the SPS for single- and multi-bunch beams
LHC LLD measurements with flattened bunch distribution
-bunch instability driven by the main cavity impedance (requires disabling direct and one-turn delay feedback for at least one cavity)

## Slide 15: Summary
Loss of Landau damping and coupled-bunch instability are closely related in the longitudinal plane
The theoretical model was developed to describe semi-analytical results and confirmed by simulations
Knowledge of the (HL-)LHC impedance (especially the broadband part) was improved in the past years, while further refinements are ongoing
Instability driven by HOMs could be a serious performance limitation since LLD was already observed in LHC
Possible cures of multi-bunch instabilities (modified distribution function and second-harmonic RF system) are under investigation
Thank you for your attention!

## Slide 16: Backup slides

## Slide 17: Different instability mechanisms
HOM only
Broadband only
HOM + Broadband
BB impedance modifies the structure of the unstable mode

## Slide 18: Possible cures: flattened particle distribution
Bunch flattening via RF phase modulation :
Developed in Tevatron to stop “dancing bunches”, as an alternative to the longitudinal damper (C. Y. Tan and A. Burov, PRAB, 2012)
Tested in 2012 in the LHC to demonstrate the reduction of beam-induced heating (E. Shaposhnikova et al, IPAC, 2014)
Routinely applied in physics since 2016
Two scenarios:
RF phase modulation after injection in the LHC
Opening phase loop can seed instability
Instability can be potentially enhanced since
Modification of distribution in the SPS
Potentially different bunch-by-bunch shape due to strong transient beam loading
Preservation of “flatness” after filamentation in the LHC needs to be confirmed
Intra-beam scattering (IBS) might compromise flattening although leads to gradual bunch length increase
Measurements in Tevatron

## Slide 19: Measurements results
Courtesy of M. Zampetakis

## Slide 20: Possible cures: flattened particle distribution
Bunch flattening via RF phase modulation :
Developed in Tevatron to stop “dancing bunches”, as an alternative to the longitudinal damper (C. Y. Tan and A. Burov, PRAB, 2012)
Tested in 2012 in the LHC to demonstrate the reduction of beam-induced heating (E. Shaposhnikova et al, IPAC, 2014)
Routinely applied in physics since 2016
Two scenarios:
RF phase modulation after injection in the LHC
Opening phase loop can seed instability
Instability can be potentially enhanced since
Modification of distribution in the SPS
Potentially different bunch-by-bunch shape due to strong transient beam loading
Preservation of “flatness” after filamentation in the LHC needs to be confirmed
Intra-beam scattering (IBS) might compromise flattening although leads to gradual bunch length increase
Measurements in Tevatron
H. Timko et al, Evian, 2019
LHC

## Slide 21: LHC Longitudinal collective effects
E. Shaposhnikova et al, IPAC, 2011
First observation loss of Landau damping (LLD)

## Slide 22: Possible cures: modified particle distribution
Bunch flattening was developed in Tevatron (C. Y. Tan and A. Burov, 2012) and is routinely applied in the LHC from 2016
One can consider modifying the particle distribution in the SPS, which might be partially preserved in the LHC after filamentation
Gain in the LLD threshold depends on the cutoff frequency of the impedance model, but the CBI threshold is reduced at the same time
Potentially, an optimal distribution can be found
H. Timko et al, Evian, 2019

## Slide 23: Possible missing impedance
During preparation for the 2024 JAP workshop, the imaginary part of the MKI (and MKI-cool) and other kicker impedance was found to be missing in the LHC impedance model
Example of past CST simulations (H. Day, PhD thesis, 2013)
Similar impedance is observed in the latest CST simulations
Four MKI kickers add ~10% to the present impedance model
This subject will be discussed at the 104th IWG meeting

## Slide 24: Possible cures
We are close to the threshold without margin
Coupled-bunch feedback system?
2nd harmonic RF system increase LLD threshold and CBI threshold
Synchrotron frequency variation due to bunch-by-bunch parameter variation (bad for luminosity, but unavoidable) and transient beam loading can help to suppress LLD type instability
MELODY was extended to treat individual bunches using a single matrix (dimensions depend on number of bunches)
Some reduction of growth rates is observed for a toy model (9 bunches)
Example for short bunches of ~0.8 ns

## Slide 25: Possible cures
Example for short bunches of ~0.8 ns
We are close to the threshold without margin
Coupled-bunch feedback system?
2nd harmonic RF system increase LLD threshold and CBI threshold
Synchrotron frequency variation due to bunch-by-bunch parameter variation (bad for luminosity, but unavoidable) and transient beam loading can help to suppress LLD type instability
MELODY was extended to treat individual bunches using a single matrix (dimensions depend on number of bunches)
Some reduction of growth rates is observed for a toy model (9 bunches)

## Slide 26: Comparison with simulations
Overall good agreement with some discrepancies
Consistent with beam observations, as higher-harmonic RF system (800 MHz) is necessary to reach even LHC nominal intensity
More accurate measurements to be done
ns
LLD threshold
Example of simulations using BLonD
Coupled-bunch instability for bunch trains with 25 ns spacing, MV, GeV (MELODY)

## Slide 27: HL-LHC impedance model
BB contributions from different elements are added as a single BB resonator with = 5 GHz
It dominates the effective impedance of HL-LHC
Model refinement is necessary for precise predictions of instability threshold (new fellow is arriving)
Real part
Imaginary part
Input from N. Mounet

## Slide 28: Beam-based measurements of LLD threshold
This technique is already used in the SPS and PS (PhD project of L. Intelisano)
Precise knowledge of RF voltage is important (see details in talk by B. Karlsen-Baeck)
Injection with phase loop on
Phase loop off
Phase kick
Example of SPS MD on 29.04.2022
Different measurements were performed before LS2 (J. E. Muller, PhD thesis, 2016)

## Slide 29: Beam-based measurements of LLD threshold
This technique is already used in the SPS and PS (PhD project of L. Intelisano)
Precise knowledge of RF voltage is important (see details in talk by B. Karlsen-Baeck)
Residual oscillation amplitude contains information about impedance (IK, T. Argyropoulos, and E. Shaposhnikova, PRAB, 2021)
Injection with phase loop on
Phase loop off
Phase kick
Example of SPS MD on 29.04.2022
Different measurements were performed before LS2 (J. E. Muller, PhD thesis, 2016)

## Slide 30: Sensitivity to the cut-off frequency
Oscillation amplitude after the kick strongly depends on the effective cut-off frequency
Scanning parameter space allows to probe longitudinal impedance
= 4 GHz
= 8 GHz
MELODY results for single BB impedance at LHC flatbottom
LLD threshold
LLD threshold