## Slide 1: High-intensity MD results & impact on luminosity
15th HL-LHC Collaboration Meeting
02/10/2025
S. Kostoglou, C. Antuono, P. Arrutia, F. Asvesta, H. Bartosik, C. Bracco, R. Bruce, X. Buffat, D. Butti,
R. De Maria, Y. Dutheil, I. Efthymiopoulos, C. Hernalsteens, M. Hostettler, G. Iadarola, B. Karlsen-Baeck,
A. Kastrinellis, T. Levens, K. Li, C. Marelli, I. Mases, L. Mether, D. Mirarchi, S. Morales, N. Mounet,
Y. Papaphilippou, J. Pucek, A. Radoslavova, S. Redaelli, G. Rumolo, B. Salvachua, B. Salvant,
M. Solfaroli, F. Soubelet, G. Sterbini, H. Timko, R. Tomas, G. Trad, J. Uythoven, D. Valuch, F. Vellotti,
J. Wanczyk, J. Wenninger, C. Wiesner, D. Wollmann, M. Zampetakis, C. Zannini
Thanks to: MD coordinators, MP, LHC OP, Injectors OP, WP2..

## Slide 2: Towards HL-LHC operational scenario
Target: 3000 fb-1 (Run 1-6)
Beam & machine parameter evolution: models, DA, Run3 & HL MD experience.
Schedule: operational days + intensity ramp-up.
Alternative scenarios: flat optics, filling schemes, ultimate pileup, LHCb upgrade..
1. Luminosity
2. Dynamic Aperture
4. HL-LHC MDs
HL-LHC INDIVs  Collisions.
4x72b@2.3e11 ppb (1200b)  Injection.
2x56b@2.3e11 (600b)  Flat Top.
DA targets for acceptable beam lifetime.
Optics: Round vs Flat.
Critical phases: End of adjust, start/end of leveling.
Crossing angle leveling.
3. Experience from Run3
Negative octupole polarity.
Flat optics.
Losses in Adjust & tails.
Emittance growth in collisions
Crossing angle leveling.
BCMS vs standard beams.
* Covered yesterday (link)

## Slide 3: Overview
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6

## Slide 4: Overview
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6
Beam quality evolution with single HL bunches (emittance growth and tail studies along the cycle via WS). Importance of transverse tails for minimizing losses in Adjust & experimentally measured gain in integrated luminosity with “low-tails”.
Collisions in aggressive BB regime, reached 160 pileup!
MD Merit

## Slide 5: Overview
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6
Tried to collide for the 1st time with HL trains, dumped x3 due to corrector trip – unrelated to MD or beam type.
Reached for the 1st time flat top with HL trains!
Studied beam quality from Injection to Flat top.
HL alternative baseline (4x56) not available from injectors yet.
First step towards 2026 high intensity tests@6.8TeV!
MD Merit

## Slide 6: Overview
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6
Injection losses, RF aspects, debunching & intra-batch ADT cleaning, beam quality at Injection with long trains (emittance growth & tail increase).
MD ended after 6L2 pressure spike limits imposed for next 2025 MDs.
First step towards HL baseline!
MD Merit

## Slide 7: Critical phases for HL performance

## Slide 8: Critical phases for HL performance
Beam quality from injectors
Beam quality transfered in LHC
Injection losses
Start of ramp losses
Losses end of adjust & during collisions
Emittance growth of unknown source
PC ripple
Emittance growth of unknown source
Long-range BB regime
Emittance growth of unknown source
Tail evolution
Debunching
Head-on BB regime
Losses in Adjust: See X. Buffat this session
Start of ramp losses: See H. Timko this session
PC ripple: See G. Sterbini yesterday afternoon

## Slide 9: Critical phases for HL performance
Beam quality from injectors
Beam quality transfered in LHC
Injection losses
Start of ramp losses
Losses end of adjust & during collisions
Emittance growth of unknown source
PC ripple
Emittance growth of unknown source
Long-range BB regime
Emittance growth of unknown source
Tail evolution
Debunching
Head-on BB regime

## Slide 10: Injection: Injection losses with HL trains
2023: Losses during B1 injection, reaching BLM saturation in IR7 for RS01. High losses but also high variability across fills.
2024-25: Situation improved, but cause still unclear. Hypothesis was that it was due to shorter trains.
HL long trains: Currently being explored in MDs by ABT.
BLM limit
4x726.6e13p
B1
B2
Y. Dutheil, F. Velotti, C. Bracco,
B. Salvachua, S. Morales

## Slide 11: Injection: Injection losses with HL trains
2023: Losses during B1 injection, reaching BLM saturation in IR7 for RS01. High losses but also high variability across fills.
2024-25: Situation improved, but cause still unclear. Hypothesis was that it was due to shorter trains.
HL long trains: Currently being explored in MDs by ABT.
MD results (see backup slides):
  2x56: 5-10% of BLM thresholds. 4x56 to be tested in 2026.
  4x72: injected successfully, reaching 50-60% BLM thresholds (30% of electronic limit) with only 2-3% SPS scraping.
Conclusion:
  Feasible with tight margin, BE/SY to review BLM changes needed for LS3.
  Improvement w.r.t to 2023 pointing to injectors’ optimization of tails.

## Slide 12: Injection: Beam quality from SPS to LHC
 | SPS (after scraping) |  | LHC injection | LHC injection |  | 
 | Emittance | q-factor | Emittance | q-factor | Bunch intensity (ppb) | Bunch length (ns)
8b4e, 2x56 | εH=1.6 μm εV=1.5 μm LIU target=1.65 μm | qH=1.07 qV=1.06 | εH=1.7 μm εV=1.5 μm | qH=1.2 qV=1.1 | 2.31e11 | 1.2
Standard, 4x72 | εH=2.3 μm εV=2.1 μm LIU target=2.1 μm | qH=1.15 qV=1.16 | εH=2.4 μm εV=2.1 μm | qH=1.25 qV=1.1 | 2.25e11 | 1.25
BCMS, 5x48 | εH=1.6 μm εV=1.4 μm LIU target=1.65 μm | qH=1.22 qV=1.25 | - | - | - | -
From I. Mases LBOC
Conclusion: Reaching LHC injection with good brightness and controlled tails for both 8b4e and standard. Full scheme BCMS & 8b4e to be tested in next MD blocks 2025-26.

## Slide 13: Critical phases for HL performance
Beam quality from injectors
Beam quality transfered in LHC
Injection losses
Start of ramp losses
Losses end of adjust & during collisions
Emittance growth of unknown source
PC ripple
Emittance growth of unknown source
Long-range BB regime
Emittance growth of unknown source
Tail evolution
Debunching
Head-on BB regime

## Slide 14: Injection plateau: Emittance growth
Emittance growth during injection of unknown source, ~0.2 μm/h beyond IBS.
MD results:
  Although exact source not identified, brightness independent.
  Confirmed with both HL INDIVs and trains.
Max. brightness, model  HL INDIV
-20% brightness, model
-60% brightness, model
Measurements

## Slide 15: Injection plateau: Emittance growth
Emittance growth during injection of unknown source, ~0.2 μm/h beyond IBS.
MD results:
  Although exact source not identified, brightness independent.
  Confirmed with both HL INDIVs and trains.
IBS + 0.2 μm/h
Max. brightness, model  HL INDIV
-20% brightness, model
-60% brightness, model
Measurements

## Slide 16: Injection plateau: Emittance growth
Max. brightness, model  HL INDIV
-20% brightness, model
-60% brightness, model
Measurements
IBS growth rate
H
V
IBS + 0.2 μm/h
HL trains
Emittance growth during injection of unknown source, ~0.2 μm/h beyond IBS.
MD results:
  Although exact source not identified, brightness independent.
  Confirmed with both HL INDIVs and trains.
Conclusion: Not expected to degrade for HL beams.

## Slide 17: Injection plateau: Tail population
MD results:
  Tail increase of bunches at the end of the train (e-cloud related) during injection with long trains.
  Also observed during scrubbing with 2x72 and nominal bunch intensity.
  Based on correlation of transverse tails & losses at the end of Adjust (combined with tight DA at start of leveling for HL), can result in important intensity losses in Adjust  might be solved with e-cloud mitigation measures put in place for HL.
Conclusion: Tail development at injection due to e-cloud might be an issue for HL long trains.
q-factor
H
V
Blue: bunches at the start of the train
Red: bunches at the end of the train

## Slide 18: Ramp: Debunched beam & start of ramp losses
Debunched beam
B1
B2
Studies led by RF (see H. Timko, B. Karlsen-Baeck this session).
After TS1, 1h extended stay at injection in nominal operation & corresponding amount of debunched beam  ~55% BLM thresholds at start of ramp.
Nominal operation – extended stay at injection

## Slide 19: Ramp: Debunched beam & start of ramp losses
Debunched beam
B1
B2
Nominal operation – extended stay at injection
4x72 MD
Studies led by RF (see H. Timko, B. Karlsen-Baeck this session).
After TS1, 1h extended stay at injection in nominal operation & corresponding amount of debunched beam  ~55% BLM thresholds at start of ramp.
MD results:
  Similar levels of debunched beam at 4x72b, 1200b MD but cannot be directly confirmed (no ramp).
  8b4e, 600b: 5-8% BLM thresholds at start of ramp.
Applying FBCT/DCBCT calibration factor

## Slide 20: Ramp: Debunched beam & start of ramp losses
Statistics from 2025 operation after TS1 (see backup slides)

## Slide 21: Ramp: Debunched beam & start of ramp losses
4x72@2.3e11 ppb,
1200b projection
Statistics from 2025 operation after TS1 (see backup slides)
8b4e MD, measured

## Slide 22: Ramp: Debunched beam & start of ramp losses
Conclusions:
Clear need to ramp HL trains with large number of bunches for more accurate projections (RF MDs in 2025 & 2026).
Ramping a full HL machine will require mitigation measures:
  Clean debunched beam:
    ADT intra-batch cleaning (X. Buffat, D. Valuch et al.).
  Increase margin for losses at start of ramp:
    Raise BLM thresholds (D. Mirarchi, B. Salvachua et. al).
    PPLP (H. Timko, M. Solfaroli et. al).
  Prevent debunching:
    Increase RF voltage with high efficiency klystrons.
    Degrade emittances at injection to avoid debunching & preserve intensity.
4x72@2.3e11 ppb,
1200b projection
8b4e MD, measured
Statistics from 2025 operation after TS1 (see backup slides)

## Slide 23: Critical phases for HL performance
Beam quality from injectors
Beam quality transfered in LHC
Injection losses
Start of ramp losses
Losses end of adjust & during collisions
Emittance growth of unknown source
PC ripple
Emittance growth of unknown source
Long-range BB regime
Emittance growth of unknown source
Tail evolution
Debunching
Head-on BB regime

## Slide 24: Adjust: Minimizing losses at the end of adjust
Losses at the end of Adjust when entering head-on BB dominated regime. More critical for high brightness HL bunches.
MD results:
  Phase of cycle only tested with HL INDIVs at the moment.
  Injected two groups of bunches with different tail population (q=1 and q=1.5)
  Needs to be tested with trains.
Conclusion: Clear improvement of losses with Gaussian bunches. Measured 3% gain in integrated luminosity. Backed-up by simulations.
q=1 q=1.5
B1
B2
β*
xing
Burn-off limit

## Slide 25: Critical phases for HL performance
Beam quality from injectors
Beam quality transfered in LHC
Injection losses
Start of ramp losses
Losses end of adjust & during collisions
Emittance growth of unknown source
PC ripple
Emittance growth of unknown source
Long-range BB regime
Emittance growth of unknown source
Tail evolution
Debunching
Head-on BB regime

## Slide 26: Collisions: Emittance growth
Emittance growth during collisions of unknown source, especially in V.
MD results (see backup slides):
  Measured 0.05-0.09 μm/h, operational levels in 2025 ~0.07 μm/h.
  Non-colliding bunches blowing up less.
  Tails tend to gaussianize in time.
  Measured only with HL INDIVs and needs to be tested with trains.
Conclusion: HL INDIVs have similar emittance growth levels to current operation in physics. Pending validation with HL trains.

## Slide 27: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6

## Slide 28: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6
Collide HL trains, aiming for levelling at HL pileup for a few hours!
First step towards 2026 high intensity tests@3 TeV!
Start of ramp losses, beam quality comparison of all HL variants, limited in batches + number of bunches due to 6L2.
MD Merit

## Slide 29: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
Phase | Beam type | *Nb
Collisions | 8b4e 4x56 | 672
3 TeV | BCMS 5x48 | 1200
3 TeV | standard 4x72 | 1200
*To be reviewed based on operational levels
MD Merit
4x56b, blowup emittances at injection + other mitigations put in place, impact on start of ramp losses, impact on integrated luminosity.
Last opportunity for collisions with HL trains >1h.
Second step towards 2026 high intensity tests@6.8TeV!
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6

## Slide 30: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
MD Merit
All HL variants with proper filling scheme & large number of bunches for beam quality comparison + start of ramp losses.
Second step towards 2026 high intensity tests@3 TeV!
+ e-cloud studies.
Phase | Beam type | *Nb
Collisions | 8b4e 4x56 | 672
3 TeV | BCMS 5x48 | 1200
3 TeV | standard 4x72 | 1200
*To be reviewed based on operational levels
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6

## Slide 31: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
Phase | Beam type | Nb
Flat top | 8b4e 4x56 | 1972
3 TeV | BCMS 5x48 | 2748
3 TeV | standard 4x72 | ~2000
Phase | Beam type | *Nb
Collisions | 8b4e 4x56 | 672
3 TeV | BCMS 5x48 | 1200
3 TeV | standard 4x72 | 1200
*To be reviewed based on operational levels
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6

## Slide 32: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
Phase | Beam type | Nb
Flat top | 8b4e 4x56 | 1972
3 TeV | BCMS 5x48 | 2748
3 TeV | standard 4x72 | ~2000
In 2025-26 MDs we will progressively ramp intensity & refine injection/ramp/collisions strategies in view of 2026 high intensity tests & approach as much as possible HL baseline.
HL-LHC MDs are extremely important to obtain experience with HL aspects, identify limitations & prepare as best as possible to reach HL targets.
Phase | Beam type | *Nb
Collisions | 8b4e 4x56 | 672
3 TeV | BCMS 5x48 | 1200
3 TeV | standard 4x72 | 1200
*To be reviewed based on operational levels
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6

## Slide 33: Backup

## Slide 34: Injection: Injection losses with HL trains
MD results:
  2x56: 5-10% of BLM thresholds. 4x56 to be tested in 2026.
  4x72: injected successfully, reaching 50-60% BLM thresholds (30% of electronic limit) with only 2-3% SPS scraping.
Conclusion: Feasible with tight margin, BE/SY to review BLM changes needed for LS3. Improvement w.r.t to 2023 pointing to injectors’ optimization of tails.
8b4e MD, up to FT
4x72 MD, injection
Highest BLM ratios for all Running Sums
Vertical lines: injection B1/B2
RS1
20%
60%
Y. Dutheil, F. Velotti, C. Bracco,
B. Salvachua, S. Morales

## Slide 35: Ramp: Debunched beam & start of ramp losses
Before TS1: collimation hierarchy breakage issue, losing in IR7 TCLA, excluded from analysis.
B1
B2
TS1
Debunched beam B1/B2 vs start of ramp losses, 2025 statistics

## Slide 36: Collisions: Emittance growth
Emittance growth during collisions of unknown source, especially in V.
MD results:
  Measured 0.05-0.09 μm/h, operational levels in 2025 ~0.07 μm/h.
  Non-colliding bunches blowing up less.
  Tails tend to gaussianize in time.
  Measured only with HL INDIVs and needs to be tested with trains.
Conclusion: HL INDIVs have similar emittance growth levels to current operation in physics.
B1V
q-factor
  Emittance
Gaussian, colliding iP1/5
Gaussian, non-colliding
Non-gaussian, colliding IP1/5
Non-gaussian, non-colliding

## Slide 37: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6
Reached 160 pileup with HL INDIVs
Thanks to fast beta* levelling, crossing angle leveling, high brightness.
Ramped HL trains to top energy.
Thanks to 8b4e.
Injected 4x72 HL baseline beams in the LHC
Thanks to injector preparation, acceptable injection losses, RF capture & optimizations.
2025 MD1-2 awards

## Slide 38: Overview & Next steps
2026 high intensity tests
HL-LHC
2025 MDs
2026 MDs
 | Phase | Beam type | Nb
MD1 | Collisions | HL INDIVs | 6
MD2 | Flat top | 8b4e 2x56 | 560
 | Injection | standard 4x72 | 1152
Goals for MD3-4 | Collisions | 8b4e 2x56 | 560
 | Ramp 500 GeV | standard 1x72 | 300
 | Ramp 500 GeV | BCMS 2x36 | 300
 | 3 TeV | HL INDIVs | 6
Collisions with 8b4e HL trains.
All HL variants (8b4e, BCMS, standard) tested & ramped in the LHC.
Nominated 2025 MD3-4 awards

## Slide 39
2x48b@2.3e11pb, fill 10250, 348b